## Slide 1
IBIS Accuracy Study
March 31, 2000
IBIS Modeling Team - Egypt
Sherif Hammad
sherif_hammad@mentor.com

## Slide 2
Agenda
Criteria of comparison & abbreviations
Four waveforms effect
Two waveforms effect
No waveforms effect
Mid-point model accuracy
Model accuracy at different loading condition
Conclusion

## Slide 3
Comparison Criteria
Cross-Correlation Peak Value (CCPV)
Cross-Correlation Time Offset (CCTO)
Average Absolute Difference in V (AAD)
Average Absolute Difference in % (AAD) with respect to the DC span
Curve Overlay Metric (%) (COM)
Notes: First CCPV and CCTO are calculated. Then, the tested waveform is shifted by CCTO. Then, AAD and COM are calculated based on shifted waveform against the reference waveform.

## Slide 4
4 Waveforms Test Load: 50GND
[Rising Waveform [Rising Waveform] [Falling Waveform] [Falling Waveform] R_fixture = 50 R_fixture = 50 R_fixture = 50 R_fixture = 50 V_fixture = 0 V_fixture = 3.3 V_fixture = 3.3 V_fixture = 0
Notes: Simulation is done here based on 1ps step in both Spice and IS. Shift value, between the test and reference waveforms, will be affected by this simulation step.

## Slide 5
4 Waveforms Test Load: 503.3V
[Rising Waveform [Rising Waveform] [Falling Waveform] [Falling Waveform] R_fixture = 50 R_fixture = 50 R_fixture = 50 R_fixture = 50 V_fixture = 0 V_fixture = 3.3 V_fixture = 3.3 V_fixture = 0

## Slide 6: Effect of Four Waveforms
Four waveforms override ramp data.
Curve Overlay Metric is better than 99.8%.
Average Absolute Difference % (with respect to DC span) is maximum 0.2%.
Notes: 1- DC span is the voltage difference between 'high' and 'low' states (typically here 1.5V).
2- For LVDS buffers, all accuracy numbers must be re-evaluated again because of the smal swing nature (around 300mv) where AAD values are expected to be higher.
3- By 4WF, it's meant that a model covers its actual operating envorinment at certain load.

## Slide 7
2 Waveforms Test Load: 50GND
[Rising Waveform [Rising Waveform] [Falling Waveform] [Falling Waveform] R_fixture = 50 R_fixture = 50 R_fixture = 50 R_fixture = 50 V_fixture = 0 V_fixture = 3.3 V_fixture = 3.3 V_fixture = 0

## Slide 8: Effect of Two Waveforms
COM value is down to 96% from 99.8% where 4 waveforms are used.
AAD% expresses accuracy degradation from 0.16% (4WF case) to 4%.
Accuracy of rise part is much better since Rise to ground waveform is available.
Accuracy of fall part (to grounded load) is much worse since fall-to-vdd waveform is only given.

## Slide 9
2 Waveforms Test Load: 503.3V
[Rising Waveform [Rising Waveform] [Falling Waveform] [Falling Waveform] R_fixture = 50 R_fixture = 50 R_fixture = 50 R_fixture = 50 V_fixture = 0 V_fixture = 3.3 V_fixture = 3.3 V_fixture = 0

## Slide 10
Effect of Two Waveforms
COM value is down to 98.2% from 99.8% where 4 waveforms are used.
AAD% expresses accuracy degradation from 0.2% (4WF case) to 2%.
Accuracy of fall part is much better since Fall to VDD waveform is available.
Accuracy of rise part (load is to VDD) is much worse since rise-to-gnd waveform is only given.

## Slide 11
No Waveforms Test Load: 50GND
[Rising Waveform [Rising Waveform] [Falling Waveform] [Falling Waveform] R_fixture = 50 R_fixture = 50 R_fixture = 50 R_fixture = 50 V_fixture = 0 V_fixture = 3.3 V_fixture = 3.3 V_fixture = 0

## Slide 12
Effect of No Waveforms
Rise part is extracted based on dv/dt having the load connected to ground.
Fall part is extracted based on dv/dt having the load connected to VDD.
AAD and COM better expresse model bad accuracy.
Notes: DV/DT calclualtion base:
1: Rise: connect R-load to gnd and calculate 20%-80% slope
2:Fall: connect R-load to vdd and calculate 20%-80% slope
Based on this Ibis-standard (i think), it's expected and actually seen from previous curve that rise accuracy is better since the actual load is connected to ground. In other words, fall part was extracted based on ramp data away from actual loading condition.

## Slide 13
4 Waveforms Test Load: 501.65V
[Rising Waveform [Rising Waveform] [Falling Waveform] [Falling Waveform] R_fixture = 50 R_fixture = 50 R_fixture = 50 R_fixture = 50 V_fixture = 0 V_fixture = 3.3 V_fixture = 3.3 V_fixture = 0

## Slide 14
4 Waveforms Test Load: 30GND
[Rising Waveform [Rising Waveform] [Falling Waveform] [Falling Waveform] R_fixture = 50 R_fixture = 50 R_fixture = 50 R_fixture = 50 V_fixture = 0 V_fixture = 3.3 V_fixture = 3.3 V_fixture = 0
Notes: Here CCTO lost its meaning. Maximum corelation is obtained at zero shift.
CCPV can be compared (at third digit after decimal point) to that having 4WF at 50-to-gnd load.

## Slide 15
Mid-Point Accuracy & Testing Different Load
Model accuracy is not bad at 50Ohm to half VDD load when using 4 waveforms model.
AAD% (0.87%) and COM (99.1%) shows that 4 waveforms model cope well with different loading condition.

## Slide 16
Conclusion
Four waveforms are essential for best model accuracy at certain load.
Two waveforms model accuracy is limited.
Numerical relative merits (CCPV, CCTO, AAD, and COM) can be used to evaluate model accuracy.