## Slide 1: Tips and Tricks for Creating IBIS Models
Samples from a case study on the creation and QA of IBIS models from SPICE simulation models
Written by Jon Powell - Viewlogic Consulting Services
Presented by Cary Mandel - Technical Specialist

## Slide 2: OverView (sorry)
Some Important IBIS features
Setting up test circuits
Running QA
Some common problems
Some difficulties in IBIS
Example Model Simulation Comparisons

## Slide 3: Important IBIS features
VT Curves
Test Fixture Description
Properly chosen point distribution

## Slide 4: Setting up Test Circuits
Get rid of package parasitics. (Cdie required only)
Measure to a high accuracy
Set SPICE options to allow for exact voltage measurement
Be sure to measure long enough
Be sure input signal does not effect output.

## Slide 5: Running QA
QA against original SPICE VT data.
Use a well chosen mid-voltage point for time synchronization on rising and falling edges.
Add additional test cases
  Test Fixture (ie. 50pf)
  Transmission line.
  Full package test.

## Slide 6: Some Common Problems
Simulation Time Doesn’t allow waveform to reach full high or low.
SPICE model doesn’t behave well at Corners
SPICE model needs special control options to converge.
SPICE diode model creates unlikely amounts of current.
QA Simulation doesn’t reproduce some SPICE features.

## Slide 7: Some Difficulties in IBIS
100 point limit can create difficulties in fitting large MIN MAX TYP IV and VT curves. May require careful linearization.
MIN MAX and TYP may not describe full range of corners desired.
LC may not be enough information for package description (can use new 3.2 TLINE descriptions)
Transition Time not very useful for RTC or many highspeed advanced drivers.

## Slide 8: Example Model QA Simulations

## Slide 9: Without VT waveforms