## Slide 1
IBIS Summit
Munich 2001
Extraction of Key Ibis Parameters for Easier Model Selection
Category: Generating and Validating IBIS Models
John Berrie (Bristol) and Michael Schaeder (Paderborn)

## Slide 2: In this presentation
Picking IBIS models from the web
  Common problems
Can we make it easier with a basic utility (ibsinf)?
Summary

## Slide 3: Picking IBIS Models from the Web
Golden Parser checks syntax and basic semantics (driven by EDA software)
Specific EDA software does the rest
IBIS
EDA
Golden Parser API

## Slide 4: Common Problems
Wrong pin count
  Pins not modeled or wrongly modeled
  Pins wrongly defined
Buffer models
  Some EDA systems need unique names

## Slide 5: ibsinf Utility
ibis browsing assistant
  No need for licenses/EDA installations
Very basic information
Will consider donating as freeware
Still being improved

## Slide 6: General Information
Component: zk0815
Manufacturer: Newtech
#Pins: 48
#Modeled Pins: 44
#Supply Pins: 4
#Other Pins: -
#Models: 6
Model: BUF_01 (Input)
Model: BUF_07 (I/O)
Model: BUF_12 (I/O_open_source)
Model: DRV_03 (Output)
Model: DRV_06 (3-state)
Model: DRV_15 (Open_sink)
Package: pin/tssop48.pkg

## Slide 7: Input Model Information
Model: BUF_01
Type: Input
Polarity: Non-Inverting
Enable: Active-High
Vinl: 0.8V
Vinh: 2.0V
C_comp: 4.90pF; 2.70pF; 7.10pF
Voltage Range: 5.0V; 4.75V; 5.25V
Vmeas: -
Cref: -
Rref: -
Vref: -
Static Char.: GND_clamp; Power_clamp

## Slide 8: Output Model Information
Model: DRV_03
Type: Output
Polarity: Non-Inverting
C_comp: 3.40pF; 1.70pF; 5.10pF
Voltage Range: 5.0V; 4.75V; 5.25V
Static Char.: GND_clamp; Power_clamp; Pullup; Pulldown
Ramp dV/dt_r: 1.47/302p; 1.23/419p; 1.75/206p
Ramp dV/dt_f: 1.59/418p; 1.33/654p; 1.89/235p
Rise Wvf. 1: R_fixture = 50; V_fixture = 0.0
Fall Wvf. 1: R_fixture = 50; V_fixture = 0.0
Rise Wvf. 2: R_fixture = 50; V_fixture = 5.0; 4.5V; 5.5V
Fall Wvf. 2: R_fixture = 50; V_fixture = 5.0; 4.5V; 5.5V

## Slide 9: Summary
Helps when working off-line to the EDA system
  People with a PC but no simulator
    Easier delegation
  Less expertise needed
A very basic utility for the 80/20 rule