## Slide 1
DOGEN
A SIEMENS internal model Tool
Extensions 1999 - 2001
Hans Pichlmaier
ICN M TE1
Technology Applications
March, 16th 2001

## Slide 2: DOGEN - an internal model tool
Functionality overview
  Converting:
    QUAD -> IBIS model, topology
    IBIS -> QUAD model, .ebd, connector, package
    SPICE -> IBIS.ebd
  IBIS scaling: typ to min/max
  Check: QUAD models , IBIS models
  Works standalone or inside our BIOLIB structure
  Support of BIOLIB structure with many features
Notes: 3

## Slide 3
ELAN = DOGEN Functionality for Projects
ProjectBIOLIB
IBIS +
Project
Tool-Lib
QUAD /
QUIET Exp.
Project
Tool-Lib
ICX
Project
Tool-Lib
SPECCTRA
Quest
ELAN
BIOLIB
IBIS +
ELAN
IC
-- Index
-- Pinning
-- Package
-- Cells - Models
PASSIVE
-- Index
-- .dat Files
-- IBIS Templates
MODULE
-- Index
-- .ebd Files
-- Passive for .ebd
Layout-Data with
- used Part Numbers
- values of passive Components

## Slide 4: DOGEN - Extensions 1999 - 2001
Models for passive Components in BIOLIB
.ebd Modules inside BIOLIB
Evidence of model usage in projects
Complex Packages inside BIOLIB
Modelviewer for IV- and VT-curves
Conversion of Altera and Xilinx FPGA Files to IBIS Pinning
IBIS split and IBIS expand to make BIOLIB Elements from standard IBIS Models
Support of IBIS 3.2
Support of new QUAD Syntax: DIFFPIN, SERIESPIN

## Slide 5
Passive Components
[Model] FORMEL_SERNAME
Model_type Series
[R Series] IFNOT_DAT_LSER_PRINT_DAT_R FORMEL_RMIN FORMEL_RMAX
[Rl Series] IF_DAT_LSER_PRINT_DAT_R FORMEL_RMIN FORMEL_RMAX
[L Series] IF_DAT_LSER_PRINT_DAT_LSER NA NA
[C Series] IF_DAT_CPAR_PRINT_DAT_CPAR NA NA
[Model] v39243-z6080-j_ser
Model_type Series
[C Series] 50.000fF NA NA
[L Series] 2.000nH NA NA
[Rl Series] 8.200Ohm 8.118Ohm 8.282Ohm
model v39243-z6???-j
comp_type resistor
part_type Single
package 0805
template passiv/template/resistor/sgl.ibs
model_data
R VALUE
tol 1%
Lser 2.0nH
Cpar 0.05pF
end_model_data
1 DAT File for each
Component Line
e.g. 0805
1 Template for each type of passive Component
e.g. Resistor, Capacitor, Inductor, Connector, Fuse, Switch, Delayline, Diode
1 IBIS Model for each Part Number in the Layout

## Slide 6: Module in BIOLIB
WRITING ICX MODULE --
RESULT ibis board in file: result/ICX/A5E00031387_V2.ebd
RESULT ibis model in file: result/ICX/512MB-DIMM_PASSIV.mod
RESULT ibis model in file: result/ICX/v50004-f281-t210_K4S560432A-TC80_v2.ibs
WRITING QUAD MODULE --
RESULT quad topology in file: result/QUAD/A5E00031387_V2.top
RESULT quad location in file: result/QUAD/A5E00031387_V2.loc_TYP
RESULT quad location in file: result/QUAD/A5E00031387_V2.loc_DELMIN
RESULT quad location in file: result/QUAD/A5E00031387_V2.loc_DELMAX
RESULT quad location in file: result/QUAD/A5E00031387_V2.loc_XTALK
RESULT quad parameter in file: result/QUAD/A5E00031387_V2.xns
RESULT quad model in file: result/QUAD/A5E00031387_V2.mod
RESULT quad model in file: result/QUAD/512MB-DIMM_PASSIV.mod
RESULT quad model in file: result/QUAD/v50004-f281-t210_K4S560432A-TC80_v2.pin
--MODULE_SECTION
v50004-f153-t810 v1 A5E00021674
v50004-f396-t800 v1 A5E0003138
v50004-f396-t800 v2 A5E00031387_V2
v50004-f542-t800 v1 A5E00069622
v50004-f397-t800 v1 M374S0823CTS-G8
--END
dogen -f mb1 -o result -p v50004-f542-t800 -v v1
[Begin Board Description] A5E00069622
[Number Of Pins] 114
[Pin List] signal_name
10 /D(7)
...........
[Reference Designator Map]
C40 512MB-DIMM_PASSIV_C
D1 v50004-f563-t200 v1
D10 v50004-f563-t200 v1

## Slide 7
Evidence of Model usage in Projects
ProjectBIOLIB
IBIS +
Project
Tool-Lib
QUAD /
QUIET Exp.
Project
Tool-Lib
ICX
Project
Tool-Lib
SPECCTRA
Quest
ELAN
BIOLIB
IBIS +
ELAN
IC
-- Index
-- Pinning
-- Package
-- Cells - Models
PASSIVE
-- Index
-- .dat Files
-- IBIS Templates
MODULE
-- Index
-- .ebd Files
-- Passive for .ebd
Lists of used Components, Models, Packages by email to library group

## Slide 8: Future plans
Extension of Data for EMI Analysis and Powerbus Decoupling