## Slide 1
EMC model for prediction of parasitic emission
Etienne Sicard
etienne.sicard@insa-tlse.fr
http://intrage.insa-tlse.fr/~etienne
Etienne SICARD
AUTOMOTIVE SA
Christian MAROT
André PEYRE LAVIGNE
Claude HUET

## Slide 2
Contents
1. Context of the study
2. The IERSET project on EMC for ICs
3. System design methodology for EMC
4. Core emission model
5. Emission model with Ios
6. Emission model in TEM cell
7. Conclusion

## Slide 3
0.7µm, 2 metal layers
Up to 100,000 devices on a chip
CPU frequency 50MHz
0.12µm, 6 metal
Up to 200,000,000 devices
CPU frequency 1GHz
1991
2001
IC
1000 pins
40 pins
10 years of
evolution
1. Context of the study

## Slide 4
Stronger di/dt
Scaled current
Voltage supply decreases
Current amplitude keeps constant
Faster switching
Increased EMC problems
Time
di/dt
Voltage
Current
di/dt
Voltage & Current
1. Context of the study

## Slide 5
MHz
dBµV
0
20
40
60
80
100
10
100
1000
FM
GSM
RF
Ultimate target
Supplier A
Supplier B
10dB
40dB
Probably EMC compliant
Not EMC compliant
Low parasitic emission is a key argument
1. Context of the study

## Slide 6
Parasites on local links
433 MHz, 2.5GHz
Parasites on
your mobile phone
900, 1800,1900MHz
Parasites internal devices (ABS)
Example for automotive
1. Context of the study
Similar EMC problems in aerospace

## Slide 7
2. The IERSET project
European Research Centre on Electronics for Transportation identifies and co-ordinate co-operative research.
AIRBUS
TOULOUSE
AUTOMOTIVE SA
Objectives
Study and evaluation of emission /susceptibility measurement methods for integrated circuits
Definition and validation of a model to be used in PCB CAD tools to guarantee the EMC of electronic systems
Project EMC for ICs

## Slide 8
3. System Design Methodology for EMC
DESIGN
Architectural
Design
Design Entry
Design Architect
FABRICATION
Version n°
EMC Measurements
GO
NO GO
+ 6 months
+ $$$$$$$$
Compliance ?
Version n°
EMC compliant
Obsolete Design Methodology

## Slide 9
DESIGN
EMC Simulations
Compliance ?
IC Models
Architectural
Design
Design Entry
Design Architect
FABRICATION
EMC compliant
GO
Design Guidelines
Tools
Training
3. IC Design Methodology for EMC
Target Design Methodology

## Slide 10
Ib
Rvdd
Cd
Lvdd
Rvss
Lvss
Cb
External VDD
External VSS
IC model
4. Core Emission Model
Propose a simple model for the core, not handled by IBIS
Basic parameters
Cd, Ib
Advanced param.
R,L,Cb
-10
0
10
20
30
40
50
60
70
80
1
10
100
1000
f (MHz)
dBµV
Measurements
Simulation Cd, Ib
Peak harmonics
Primary resonance
Secondary
resonance
All parameters

## Slide 11
4. Core Emission Model
Current generator estimation
Physical Transistor level (Spice)
Gate level Activity
Interpolated Transistor level (Powermill)
Huge simulation
Limited to analog blocks
Difficult adaptation to usual tools
Limited to 1 M devices
Simple, not limited
Fast
Not very accurate
Equivalent
Current generator Ib

## Slide 12
5. Emission Model with IOs
Comparison between simulation and measurement on a 16 bit micro-controller
Validation for a 16 bit micro-controller
Within 10dB, but I/Os not handled
-10
0
10
20
30
40
50
60
70
80
1
10
100
1000
f (MHz)
dBµV in conducted mode
Simulation (PSPICE)
EMC model
Measurement (Conducted 1)

## Slide 13
5. Emission Model with IOs
Add IBIS I/O data
Zsub: basically a 1-10 serial resistance
Cio : decoupling capacitance for IO supply
IO block: reuse of IBIS
Ib
Rvdd
Core VDD
Core VSS
Cd
Lvdd
Rvss
Lvss
Cb
I/O
Zsub
I/O VSS
I/O VDD
Cio

## Slide 14
5. Emission Model with IOs
Validation
IO modify the spectrum at high frequencies (>300MHz)

## Slide 15
6. Emission in TEM cell
Cdie_gnd
Lpackage
Lseptum
50 
50 
Chip under test
Cdie_septum
KCoupling
To PCB
Receiver
Chip under test
PCB
Proposed model: capacitance & inductance coupling

## Slide 16
6. Emission in TEM cell
Model fits correctly up to 400MHz
At high frequencies, close from noise floor
Validation

## Slide 17
Conclusion
Technology scale down illustrated
More complex chips increase parasitic emission
An EMC model for Ics is mandatory
A simple model has been proposed
Satisfactory prediction of conducted emission
Prediction of the core emission in TEM investigated
Model proposal standardized by UTE (ICEM)
Future participation to ICEM cookbook