## Slide 1: Update on Zuken’s ibisinf Utility
Alexander Löhr Michael Schäder
Copyright © 2002 Zuken GmbH, EMC Technology Center, Vattmanstr. 3, D-33100 Paderborn, Germany Email: alexander.loehr@zuken.de michael.schaeder@zuken.de

## Slide 2: Short Outline of ibisinf History
ibisinf was born to simplify detection of common obvious errors and to get a fast overview on IBIS files.
First presented on the European IBIS Summit on 16th March 2001 in Munich, Germany.
Available on NT, Win2k, Solaris, HP-UX and Linux from http://www.zuken.com/ibis/
Over 400 downloads since March 2001.
Notes: - obvious errors in IBIS files are for instance are invalid pin count, not referenced but included buffers; an overview is given on component(s) as well as buffer models;
- the number of downloads shows the interest in and need of such an utility;

## Slide 3: Use ibisinf to Examine Models
  Checks syntax and semantics equal to ibischk3.
  Extracts component information like: Name, #pins, #models, assigned models, package data etc.
  Outputs buffer/model characteristics like: Name, type, polarity, voltage range, reference conditions, static characteristics, rising and falling waveforms.
  Now based on latest IBIS Golden Parser V3.2.8.
  Writes out model waveforms in spreadsheet format.
NEW
Notes: 1) because ibisinf is based on the IBIS Golden Parser, the tool does all the things (syntax, semantics checks) which ibischk3 does;
2) this gives rough but fast overview on component data in an IBIS file; -c option to extract this info;
3) this gives rough but fast overview on model data in an IBIS file; -m option get model data; New:
4) the latest Golden Parser is now integrated which has improved semantics check and some errors removed;
5) most important is now the ability to extract tables from ibis files in a sreadsheet compliant format; this has been realized on customer request to be able to process VT/VI curves further; the table values are delimited by tabs by default; -t option to do so (additional in this context, –d allows to specify the delimiter);

## Slide 4: How to Visualize or Correct Curves
Run ibisinf on IBIS model file to get overview on contents, and perhaps on problems.
Extract waveform from IBIS file by calling ibisinf example.ibs –m –t > ex_tbls.txt
Import table-file into spreadsheet application.
Modify the waveform with caution in a reasonable way.
Write modified table back into a file.
Replace given waveform in IBIS file with modified one in preferred ASCII editor.
Run ibisinf again to verify model changes.
Notes: --
-m –t extracts all tables of all available models from the IBIS file; to just extract tables of a particular models call ibisinf –m <buffername> -t;
within the spreadsheet tool it should be possible to select the table of interest, and to visualize its data graphically;
spreadsheet application should allow graphical data manipulation (just move points with mouse); the raw table values are changed accordingly;
just save the file in spreadsheet app.;
open IBIS model and tables file in ASCII editor; cut out corrected table section and replace faulty one in IBIS file;
run ibisinf again on the IBIS file to ensure model correctness