## Slide 1
Integrated Circuits Electromagnetic Model
IEC 62014 – 3 STATUS

## Slide 2
UTE EMC task force and program history
ICEM model technical basis, technical reminders
ICEM implementation in IBIS database
ICEM validation
ICEM cookbook
Conclusion
PLAN

## Slide 3
UTE EMC TASK FORCE
AND PROGRAM HISTORY

## Slide 4
Leader PERRIN Jean Claude TEXAS INSTRUMENTS
Members HUET Claude AIRBUS France
LEVANT Jean Luc ATMEL
MAROT Christian SIEMENS VEDEO Automotive
MAURICE Olivier VALEO
PERRAUD Richard EADS CRC
SAINTOT Pierre ST MICRO ELECTRONIQUE
SOUBEYRAN Amaury EADS CRC
University SICARD Etienne INSA
RAMDANI Mohamed ESEO
UTE TEAM

## Slide 5
History
1994 : WORKING GROUP UTE/CEF 93GT5 EMC
06 / 1997 : IEC 93 / 67 NP
1998 : DATE 98 / INTERNATIONAL TASK FORCE
2000 : DATE 2000 / IEC INTERNATIONAL EXPERTS MEETING
03 / 2001 : IEC 62014 - 3
  CDV proposal sent to IEC
  for standard approval
03 / 2001 : DATE 2001 MUNICH IBIS SUMMIT MEETING

## Slide 6
PROGRAM STATUS
IEC 62014-3 DOCUMENT COMPLETION AND IEC APPROVAL.
SANTA CLARA PRESENTATION (End of JANUARY 2002)
COOK BOOK UNDER CONSTRUCTION
DATE 2002 PARIS IBIS SUMMIT MEETING
ICEM and cookbook documents available on the UTE web:
www.ute-fr.com

## Slide 7
ICEM MODEL
Integrated Circuits Electromagnetic Model
TECHNICAL BASIS
TECHNICAL REMINDERS

## Slide 8
ELECTROMAGNETIC AND HF NOISE SOURCES
Power supply lines emission :
Switching activity in different modules (Internal/peripheral)
High frequency current through package connections
I/O connections noise emission :
Noise due to output fast signals and package characteristics
Noise coupling through package to the other I/O pins
Noise coupling through package to other powers supplies
IC Direct emission :
Package Bonding and metal die connections

## Slide 9
Mechanisms for parasitic emission
covered by ICEM model
Origin of parasitic emission in CMOS:
gate switching

## Slide 10
Power lines contribution
I/Os contribution

## Slide 11
ICEM IMPLEMENTATION
IN IBIS DATABASE

## Slide 12
CURRENT GENERATOR DESCRIPTION
[Ib generator]
[Cb capacitor]
| Variable Typ Min Max
C_pkg 2.045e-13 8.363e-14 3.75e-13
[Vdd Vss Pin]
[Ib current]
Variable
Ib (mA) 1 10 50 100 80 60 40 20
t (nS) .5 1 1.5 2 2.5 3 3.5 4
[Frequency]
| Variable Typ Min Max
F(MHz) 13 6 50

## Slide 13
ICEM in IBIS-ML
IBIS mark-up language (IBIS-X) makes ICEM implementation very easy
[define model] ICEM
| on chip capa
capacitor c_dec (vcc vss) C=5fF
| Serial supply resistor
resistor r_vdd (vcc vcc_int) R=10
resistor r_vss (vss vss_int) R=10
...
| current
Ib (vcc_int vss_int) I=It(TIME)
[It]
time I(typ)
0.0 0.3e-3
0.1e-9 0.3e-3
0.2e-9 0.5e-3
0.3e-9 0.8e-3
…
[end It]
[end define model] ICEM
Call of the user-defined model:
[begin header]
[ibis-ml version] 0.5
[filename] mpc755.ibs
[data] Nov 27,2001
[model] ICEM
[end]

## Slide 14
ICEM VALIDATION

## Slide 15: MODEL VERIFICATION
IERSET VALIDATION
TOULOUSE
VEDEO Automotive

## Slide 16: Emission Model with IOs

## Slide 17: Emission in TEM cell
Validation for the core & IOs
Model fits correctly up to 800MHz
At high frequencies, IO effects dominate

## Slide 18: DIRECT IC RADIATION CORRELATION BASED ON TEM CELL MEASUREMENT
TEM CELL
Simulation

## Slide 19
ICEM’S COOKBOOK

## Slide 20: COOK BOOK STATUS
UTE TEAM WORKING ON COOK BOOK
TO BE COMPLETED 1st JULY 2002.
“DIVA” PROJECT IN “MEDEA+” STRUCTURE
  CONTRIBUTORS : EADS CRC, INSA, AIRBUS
  APPLY ICEM MODEL TO SIMULATE COMPLEX PCB LAYOUT.
  VALIDATE THE COOK BOOK ( PARAMETERS
  EXTRACTION BASED ON COOK BOOK PROCESS)

## Slide 21: PARAMETERS EXTRACTION BASED ON MEASUREMENT
COOK BOOK STATUS

## Slide 22
CONCLUSION

## Slide 23
CONCLUSION
ICEM gives a capability to simulate EMC due to internal activity and of I/Os noise coupling
ICEM model is easy to add as a modification or add in the files of usual standards like IBIS
ICEM model parameters can be obtained by measurement (cook book) if data are not available from ICs manufacturers.
ICEM can be easily implemented in commercial simulation software