## Slide 1: IBIS Activity Report
Stephen Peters,
Intel Corp.

## Slide 2: Overview of Current Activities
IBIS version 4.0 is ready for review
  Draft copy is on IBIS website, http://www.eda.org/pub/ibis/ver4.0_wip/
IBIS Connector spec has expanded to include general purpose interconnect
  Expect revision 1.0 of the .icm specification to be available for review by June of this year.
New proposal from Mentor Graphics to extend IBIS modeling capabilities
  This proposal supercedes IBIS-X and the macro language work that was being done by the futures committee
Much work on extending IBIS into the EMC/EMI world
  Both Innoveda and INSA are pursuing proposals
Model Quality Group has formed
  Barry Katz of SiSoft is chair

## Slide 3: IBIS Version 4.0 – 10 more birds
BIRD62.6 - Receiver Threshold spec extensions
  [Receiver Thresholds] -Vinh/l_ac/dc and differential thresholds offsets from Vth, Tslew, sensitivities
  [External Reference] - External voltage reference
BIRD64.4 - [Alternate Package Models]
BIRD65.2 - C_comp split to any four voltage references
BIRD66, BIRD71 [Model Spec] additions
  11 Timing test load subparameter extensions, PCI, PCI-X support (separate rising, falling loads)
BIRD67 - 1000 V-T lines

## Slide 4: IBIS 4.0 Birds (cont.)
BIRD68.1 - Clarify V-T table rising and falling edges aligned
BIRD70.5 - Golden Waveforms
  [Test Data], [Test Load], and other keywords and subparameters to define golden waveforms (near, far, single-ended, differential, typ/min/max) and general test load circuit
BIRD72.3 - PMOS/NMOS series switch models
  Extends definition of series MOSFET to PMOS, NMOS and combinations - no syntax change
BIRD73.4 - Fall Back submodel
  Adds the Fall_back submodel for AVC technology
  Clarification and corrections to Bus_hold submodel

## Slide 5: IBIS 4.0 Ratification Plan
Review copy uploaded under “Ver 4.0 Work In Progress” link of IBIS home page
Committee review/vote on Version 4.0 to stabilize syntax and resolve any interaction issues
Start ibischk4 parser project - another review and possible clarification BIRDs
Committee review/vote Version 4.1
Package and submit for EIA letter ballot
  3 months review
  Respond formally to comments
If successful, ratify as ANSI/EIA-656-B

## Slide 6: IBIS Connector & Futures Groups
Connector spec has undergone extensive review
  Keywords simplified, syntax made to conform to IBIS “standards”
  .icm now supports frequency dependent matrixes, loss and S-parameter matrixes (Touchstone® format)
  Two keywords are being added to support general purpose interconnect (package models)
  Expect to see revision 1.0 in June of this year
Futures Committee has archived work on IBIS-X and IBIS-ML (macro language)
  Concentrating now on reviewing & vetting Mentor’s “multi-lingual modeling proposal”.

## Slide 7: Other Initiatives
EMI/EMC work continuing
  ICEM specification is now available, see today’s presentation.
  Guy Deburg (Innoveda) is working on a proposal for EMI parameters to be added to IBIS. See Jan. ’02 summit presentation for details.
Model Quality Group Formed
  Several presentations (SiQual and others) at the Jan. ’02 summit highlighted model quality issues.
  Official working group under Barry Katz formed to address issue
    Provide methods to generate accurate models
    Create metrics to quantify model quality
    One possible result is an agreed standard