## Slide 1: IBIS Basics Tutorial
Eckhard Lenski Siemens AG
European IBIS SUMMIT Meeting DATE 2003

## Slide 2: Overview
IBIS Basics tutorial
IBIS-Technologies
Parameters
Example
Conclusions
Literature
Overview
Vcc-References

## Slide 3: IBIS- Evolution

## Slide 4: Blocks of an basic IBIS-Model
Rising
R-fix Vcc
Falling
R-fix Gnd
Rising
R-fix Gnd
Falling
R-fix Vcc
Ramp
rise Gnd
Ramp
fall Vcc
Pullup
Pulldown
Power
clamp
Gnd
clamp
Threshold
Over-under
C_comp
pkg
pkg
pkg
I high
I low
Vcc
Gnd

## Slide 5: Basic V-I and V-t Curves
V
I
Gnd clamp
Power clamp
Vout
Iout
High/
pullup
Low/
pulldown
V1
GND
Vcc
V2
R-fix to VCC
Vcc
V2
R-fix to GND
V1
GND
V1
GND
Vcc
V2

## Slide 6: Example
IBIS Basics tutorial
IBIS-Technologies
Parameters
Example
Conclusions
Literature
Overview
Vcc-References

## Slide 7: Pinning and Package
[IBIS Ver] 3.2
[File Name] ALVCxxxx.ibs
[File Rev] 01.00
[Notes] HSPICE -> IBIS
[Source] DOGEN version V1.3-01
[Date] 31.01.2003
[Comment Char] |_char
[Component] ALVCxxxx
[Package]
| variable typ min max
R_pkg 0.100Ohm 0.050Ohm 0.500Ohm
L_pkg 3.380nH 2.050nH 6.010nH
C_pkg 0.309pF 0.140pF 0.610pF
[Manufacturer] vendor xyz
[Pin] signal_name model_name R_pin L_pin C_pin
1 PRE_L ALVC_REC-1_IN 0.443 6.43nH 1.56pF
2 SEL0 ALVC_REC-1_IN 0.411 6.11nH 1.43pF
3 1A1 ALVC_IO-1_BI 0.367 5.34nH 1.11pF
4 GND GND 0.111 2.45nH 2.33pF
.. .. ..
P3V3 POWER 0.145 3.49nH 1.67pF
NC NC 0.151 3.19nH 2.67pF
NC No-model 0.155 3.99nH 0.67pF

## Slide 8: Parameters
[Model] ALVC_3P3V_IO-XXX-1_BI
Model_type I/O
Vinh = 2.V
Vinl = 0.800V
Cref = 50.pF
Rref = 500.Ohm
Vref = 0.V
Vmeas = 1.500V
| variable typ min max
C_comp 5.pF 4.5pF 5.5pF
[Model Spec]
Vinh 1.9V 1.8V 2.0V
Vinl 0.9V 0.8V 1.5V
Vmeas 1.5V 1.4V 1.6V
S_overshoot_high 3.3V 3.1V 3.4V
S_overshoot_low -0.5V -0.5V -0.5V
D_overshoot_high 4.1V 3.9V 4.2V
D_overshoot_low -0.9V -0.9V -0.9V
D_overshoot_time 5.ns 5.ns 5.ns
[Voltage Range] 3.3V 3.1V 3.4V
[Pulldown Reference] 0.V 0.V 0.V
[Pullup Reference] 3.3V 3.1V 3.4V
[GND Clamp Reference] 0.V 0.V 0.V
[POWER Clamp Reference] 3.3V 3.1V 3.4V
[Temperature Range] 55. 0. 110.

## Slide 9: V-I Curves
[GND Clamp]
|Voltage I(typ) I(min) I(max)
-1.64V -2237.0mA -1789.6mA -2684.4mA
-1.22V -818.8mA -655.0mA -982.5mA
... ... ... ...
3.30V 0.0mA 0.0mA 0.0mA
3.46V 0.0mA 0.0mA 0.0mA
[POWER Clamp]
|Voltage I(typ) I(min) I(max) -1.64V 3925.0mA 3140.0mA 4710.0mA
-1.24V 1797.0mA 1437.6mA 2156.4mA
... ... ... ...
-0.40V 0.0mA 0.0mA 0.0mA 3.30V 0.0mA 0.0mA 0.0mA
3.46V 0.0mA 0.0mA 0.0mA
[Pullup]
|Voltage I(typ) I(min) I(max)
-0.30V 0.0mA 0.0mA 0.0mA
-0.20V 0.0mA 0.0mA 0.0mA
... ... ... ...
1.94V -115.3mA -92.2mA -138.3mA
3.46V -131.2mA -104.9mA -157.4mA
3.50V -131.2mA -104.9mA -157.4mA
[Pulldown]
|Voltage I(typ) I(min) I(max)
-0.400V -0.0mA -0.0mA -0.0mA
-0.300V -0.0mA -0.0mA -0.0mA
... ... ... ...
1.50V 82.6mA 66.0mA 99.1mA 3.46V 87.6mA 70.1mA 105.1mA
3.50V 87.6mA 70.1mA 105.1mA

## Slide 10: V-t Curves
[Rising Waveform]
R_fixture = 50.000Ohm
V_fixture = 3.300V
V_fixture_min = 3.135V
V_fixture_max = 3.465V
|Time V(typ) V(min) V(max)
0.00ns 0.65V 0.76V 0.57V
0.48ns 0.66V 0.77V 0.59V
... ... ... ...
2.40ns 3.30V 3.13V 3.46V
[Falling Waveform]
R_fixture = 50.000Ohm
V_fixture = 3.300V
V_fixture_min = 3.135V
V_fixture_max = 3.465V
|Time V(typ) V(min) V(max)
0.00ns 3.30V 3.13V 3.46V
0.21ns 3.28V 3.12V 3.43V
... ... ... ...
1.14ns 0.65V 0.76V 0.57V
[Ramp]
|variable typ min max
dV/dt_r 1.60V/0.15ns 1.45V/0.21ns 1.74V/0.11ns
dV/dt_f 1.50V/0.17ns 1.42V/0.24ns 1.73V/0.13ns
R_load = 50.000Ohm
[Rising Waveform]
R_fixture = 50.000Ohm
V_fixture = 0.000V
|Time V(typ) V(min) V(max)
0.00ns -0.000V 0.000V 0.000V
... ... ... ...
2.40ns 2.677V 2.420V 2.908V [Falling Waveform]
R_fixture = 50.000Ohm
V_fixture = 0.000V
|Time V(typ) V(min) V(max)
0.000ns 2.677V 2.420V 2.908V
... ... ... ...
1.148ns 0.000V 0.000V 0.000V

## Slide 11: Vcc-References
IBIS Basics tutorial
IBIS-Technologies
Vcc-References
Parameters
Example
Conclusions
Literature
Overview

## Slide 12: References for V-I Curves
V-I Curves
Technology Gnd Clamp Power Clamp Pulldown Pullup
Push-pull Gnd Ref Power Ref Pulldown Ref Pullup Ref
ECL Gnd Ref Power Ref Pulldown Ref Pullup Ref
Open sink Gnd Ref Power Ref Pulldown Ref (Pullup Ref)
Open source Gnd Ref Power Ref (Pulldown Ref) Pullup Ref

## Slide 13: Power Clamp
gnd-referenced
V
I
-3.3
0
2.5 3.3 5.8 6.6
Vcc-referenced
V
I
-3.3V 100mA
-1V 10mA
-0.5V 1mA
0.0V 0mA
3.3V 0mA
6.6V 0mA
Vtable
Iout
-3.3
0
3.3
Vtable
Vtable = Vcc - Vout
Vout = Vcc - Vtable
6.6
3.3
0
Vout
Vcc 3.3V
5.8
2.5
-0.8
Vout
Vcc 2.5V
Vout
6.6V 5.8V
4.3V 3.5V
3.8V 3.0V
3.3V 2.5V
0.0V -0.8V
-3.3V -4.1V

## Slide 14: Pullup Curve
Vout
Iout
High/
pullup
Low/
pulldown
Vout
Iout
High/
pullup
Low/
pulldown
Gnd Reference for
pullup & pulldown
Gnd Reference for pulldown
Vcc Reference for pullup
IBIS-Format

## Slide 15: ECL Curves
Vout
Iout
High/
pullup
Low/
pulldown
Vout
Iout
High/
pullup
Low/
pulldown
Vcc Reference for pulldown
Vcc Reference for pullup
Gnd Reference for
pullup & pulldown
IBIS-Format

## Slide 16: Parameters
IBIS Basics tutorial
IBIS-Technologies
Parameters
Example
Conclusions
Literature
Overview
Vcc-References

## Slide 17: Ramp Calculation
Rload
Vload rise
Vload fall
Push-pull ECL Open sink Open source hints
50 50 50 50
Gnd Vcc-2V Vcc/Vterm Gnd/Vterm
Vcc Vcc-2V Vcc/Vterm Gnd/Vterm
Default
Fixed
Fixed
Default: value can be changed ( e.g. 75Ohm, 100Ohm )
Fixed: value cannot be changed ( assumed by technology )

## Slide 18: Ramp Min Max Values
Rload
Vload
50 50 50
Vcc Vccmin Vccmax
Vcc-2V Vccmin-2V Vccmax –2V
typ min max
ECL
Rload
Vload rise
Vload fall
50 50 50
Vcc Vccmin Vccmax
Gnd Gnd Gnd
Vcc Vccmin Vccmax
typ min max
Push pull

## Slide 19: Rising / Falling Waveform
V-fixture
V-fixture-min
V-fixture-max
R-fixture
L-fixture
C-fixture
R-dut
L-dut
C-dut
required
optional
optional
required
optional
optional
optional
optional
optional
Default: 0
Default: 0
Default: 0
Default: 0
Default: 0
Default: 0
Default: 0
typical
min
max
Supply conditions
Subparameter note

## Slide 20: Example Rising Waveform
[Rising waveform]
R-fixture = 50
V-fixture = 3.3
|Time Typ Min Max
0ns 2.0 2.2 1.8
1ns 2.2 2.4 2.2
2ns 2.7 2.8 2.9
3ns 3.1 3.0 3.3
4ns 3.2 3.1 3.45
5ns 3.3 3.15 3.45
V-fixture-min = 0.0
V-fixture-max = 0.0
Zero-values by default
[Rising waveform]
R-fixture = 50
V-fixture = 3.3
V-fixture-min = 3.15
V-fixture-max = 3.45
|Time Typ Min Max
0ns 2.0 2.2 1.8
1ns 2.2 2.4 2.2
2ns 2.7 2.8 2.9
3ns 3.1 3.0 3.3
4ns 3.2 3.1 3.45
5ns 3.3 3.15 3.45
Correct subparameters

## Slide 21: Waveform Time Correlation
Use common reference point for stimulus waveform
Vcc
Gnd
t
stimulus waveform
t=0
t=0
output waveforms
t=0
Vcc
V2
Vcc
V2
t
V1
Gnd
t
V1
Gnd
t=0

## Slide 22: IBIS-Technologies
IBIS Basics tutorial
IBIS-Technologies
Parameters
Example
Conclusions
Literature
Overview
Vcc-References

## Slide 23: Push Pull (CMOS)
V
I
Gnd clamp
Power clamp
Vout
Iout
Pullup/
High
Pulldown/
Low
Rising
R-fix Vcc
Falling
R-fix Gnd
Rising
R-fix Gnd
Falling
R-fix Vcc
Ramp
rise Gnd
Ramp
fall Vcc
Pullup
Pulldown
Power
clamp
Gnd
clamp
Threshold
Over-under
C_comp
pkg
pkg
pkg
Vcc
V2
t
u
V1
GND
u
t
Vcc
V2
t
u
V1
GND
u
t
Vcc
V2
t
u
V1
GND
u
t
I high
I low
Vcc
Gnd

## Slide 24: ECL
Vh
Vl
t
u
Vh
Vl
t
u
Rising
R-fix Vtt
Falling
R-fix Vtt
Rising
R-fix Gnd
Falling
R-fix Vcc
Ramp
rise Vtt
Ramp
fall Vtt
Pullup
Pulldown
Power
clamp
Gnd
clamp
Threshold
Over-under
C_comp
pkg
pkg
pkg
Vh
Vl
t
u
Vh
Vl
t
u
Vcc
Vtt
Vout
Iout
High/
pullup
Low/
pulldown
Vcc
Vcc-2V

## Slide 25: Open Sink / Open Drain
Gnd
I high
I low
Vcc
V1
GND
u
t
V1
GND
u
t
Vout
Iout
High/
pullup
Low/
pulldown
Vcc
V2
t
u
Vcc
V2
t
u
Rising
R-fix Vcc
Falling
R-fix Gnd
Rising
R-fix Gnd
Falling
R-fix Vcc
Ramp
rise Vcc
Ramp
fall Vcc
Pullup
Pulldown
Power
clamp
Gnd
clamp
Threshold
Over-under
C_comp
pkg
pkg
pkg

## Slide 26: Open Source
Gnd
I high
I low
Vcc
V1
GND
u
t
V1
GND
u
t
Vout
Iout
High/
pullup
Low/
pulldown
Vcc
V2
t
u
Vcc
V2
t
u
Rising
R-fix Vcc
Falling
R-fix Gnd
Rising
R-fix Gnd
Falling
R-fix Vcc
Ramp
rise Gnd
Ramp
fall Gnd
Pullup
Pulldown
Power
clamp
Gnd
clamp
Threshold
Over-under
C_comp
pkg
pkg
pkg

## Slide 27: Technologies Overview
Model-Type Push Pull ECL Open Sink Open Source
Technologie
TTL X
CMOS X
PCI X
SSTL X
ECL X
PECL X
GTL X
GTLP X
CML X
LVDS X
CAN X X

## Slide 28: Literature
IBIS Basics tutorial
IBIS-Technologies
Vcc-References
Parameters
Example
Conclusions
Literature
Overview

## Slide 29: Literature
http://www.eigroup.org/ibis/ibis.htm
http://www.eigroup.org/ibis/articles.htm
( summits )
http://www.eigroup.org/ibis/tools.htm
( cookbook v2.1 )
http://www.eda.org/pub/ibis/training/
( IBIS_class_JEDEC.zip )
ftp://ftp.eda.org/pub/ibis
http://www.sisoft.com/ibis-quality/checklist

## Slide 30: Conclusions
IBIS Basics tutorial
IBIS-Technologies
Parameters
Example
Conclusions
Literature
Overview
Vcc-References

## Slide 31: Conclusions
- Take care of conditions for min max
- Include each used parameter if possible
- Use the correct modeltype with the
corresponding parameters
- Use the ibis quality checklist
(coming soon )

## Slide 32: Improvements
today
1885