## Slide 1: Can we stop the growing disparity between the potential of IBIS model parameters and the reality of delivered model parameters ?

## Slide 2: Agenda
Missing IO-Models with different PVT
Summary
IBIS QUALITY
Missing IBIS parameters
IBIS work in progress (WIP)

## Slide 3: PVT model classes
Model δVcc Tj Process
class
1 ± 5% 0 – 110 ± 2σ
2 ± 5% 0 – 110 ± 3σ
3 ± 5% m40 – 125 ± 2σ
4 ± 5% m40 – 125 ± 3σ
5 ± 10% 0 – 110 ± 2σ
6 ± 10% 0 – 110 ± 3σ
7 ± 10% m40 – 125 ± 2σ
8 ± 10% m40 – 125 ± 3σ
± 2σ means 95,5% of all shipped parts fulfill these limits
± 3σ means 99,7% of all shipped parts fulfill these limits
δVcc ± 5% means e.g. 3P3V -- 3P15V -- 3P45V
δVcc ± 10% means e.g. 3P3V -- 3P00V -- 3P60V
Vcc(V) Temp(°C) Process
3.6 -40 strong
3.45 0 strong
3.3 50 typ
3.15 110 weak
3.0 125 weak
Process Voltage Temoperature

## Slide 4: PVT for prop-delay
Vcc(V) Temp(°C) Process
3.6 -40 strong
3.45 0 strong
3.3 50 typ
3.15 110 weak
3.0 125 weak
Different Tpd :
VinL
VinH
Time / ns 
U / V

Process Voltage Temoperature

## Slide 5: PVT for overshoot
Vcc(V) Temp(°C) Process
3.6 -40 strong
3.45 0 strong
3.3 50 typ
3.15 110 weak
3.0 125 weak
D_over
_high
VinL
VinH
Time / ns 
U / V

The max-model class 8 is violating the
boundery for d-overshoot-high
Process Voltage Temoperature

## Slide 6: Pvt for first wave switching
Vcc(V) Temp(°C) Process
3.6 -40 strong
3.45 0 strong
3.3 50 typ
3.15 110 weak
3.0 125 weak
VinL
VinH
Time / ns 
U / V

The min-model class 8 does not pass
first-wave-switching
Process Voltage Temoperature

## Slide 7: PVT for HCMOS and SSTL
Example 2 SSTL2 / DDR:
DDR200-333 : Vcc : 2.3V - 2.7V
DDR400 : Vcc : 2.5V - 2.7V
HCMOS : Vcc : 2.0V - 6.0V
LVCMOS : Vcc : 1.0V - 5.5V
SSTL2 : Vcc: 2.3V - 2.7V
Example 1 LVCMOS
Vcctyp : 1.2V LVCMOS12
2.5V LVCMOS25
3.3V LVCMOS33
5.0V LVCMOS5
Some vendors supply these IO-models for logic devices
Process Voltage Temoperature

## Slide 8: History of ‚important‘ IBIS keywords/parameters
IBIS 1.0
June 1993
Ramp
V-I-curves
C-comp
IBIS 2.1
Dec 1995
Model-types
  Open- sink/source
  Ecl
Waveforms (rise/fall)
Package model
Pin mapping
IBIS 3.2
Aug 1999
Modelspec
  Overshoot
  Vinh / Vinl
Submodel
  Dyn. clamp
  bushold
Driver schedule
Package with Z0
Dimm-modules
IBIS 4.0
July 2002
Receiver thresholds
  Tslew,
  Vinh/l ac-dc
Submodel
  Fall back
IBIS 4.1
Jan 2003
External models
  Berkeley Spice
  VHDL- AMS
Model keywords and paramerters

## Slide 9: Support of ‚important‘ IBIS keywords/parameters
IBIS 1.0
June 1993
Ramp
V-I-curves
C-comp
IBIS 2.1
Dec 1995
Model-types
  Open- sink/source
  Ecl
Waveforms (rise/fall)
Package model
Pin mapping
IBIS 3.2
Aug 1999
Modelspec
  Overshoot
  Vinh / Vinl
Submodel
  Dyn. clamp
  bushold
Driver schedule
Package with Z0
Dimm-modules
IBIS 4.0
July 2002
Receiver thresholds
  Tslew,
  Vinh/l ac-dc
Submodel
  Fall back
IBIS 4.1
Jan 2003
External models
  Berkeley Spice
  VHDL- AMS
worst
bad
worse
good
Model keywords and paramerters

## Slide 10: SSTL / Receiver thresholds missing
T slew
VIL typ
VIH typ
Vth
Model keywords and paramerters
VinL ac
VinH ac
VinL dc
VinH dc

## Slide 11: Overshoot missing
Vss
D-over-low
D-over-time
S-over-low
U [V]
t [ns]
IBIS-spec
[S_overshoot_low] -0.52V -0.60V -0.65V
[S_overshoot_high] 4.05V 3.88V 4.33V
[D_overshoot_low] -1.20V -1.47V -1.11V
[D_overshoot_high] 4.44V 4.53V 4.77V
[ D_overshoot_time] 3ns 3ns 3ns
Philips supply these parameters for logic devices
Model keywords and paramerters

## Slide 12: Pin mapping missing
A1 GND3 VCC3
| 3P3V-Signalpin
A B C D E F G H I
1
2
3
4
5
6
7
8
9
Vcc3
Gnd3
IO-Bank 1
Vcc-lvds
Gnd-lvds
IO-Bank 3
Vcc1p8
Gnd1p8
IO-Bank 2
Vcc2p5
Vccclamp3
Gnd2p5
IO-Bank 4
B4 NC VCC3
| 3P3V supply
NC Vccclamp3
B1 GND2p5 VCC2p5
| 2P5V-Signalpin with diode
| to 3P3V
H6 NC VCC-lvds
H4 GND-lvds VCC-lvds
E1 NC VCCclamp3
| VCCclamp3P3V supply
B5 GND3 NC
| Gnd for 3P3V
I1 GND2p5 VCC2p5
Model keywords and paramerters

## Slide 13: IO-Model-type not correct
Z0
IBIS-IO-Model type
Input
Output
3-state
I/O
In
Out
Case I :
Tri
Bi
Case II :
Which will be the correct driver in case II ?
Model keywords and paramerters
Example : mismatch DB - IBIS

## Slide 14: IBIS Quality documents
IQ_checklist_kit.zip
  IQ-checklist.xls
  IQ-specification.txt
  USING-IQ-checklist.ppt
IBIS quality
IQ_example.ibs
  An example of an IBIS file that was run through the checklist

## Slide 15: Current status of IQ Committee Work
Checklist is complete
Checklist kit is complete
Example is available
Detailed instructions are available
Current task : list of additional checks that could be added to Golden Parser
Wanted: engineers / volunters who will use the checklist and provide feedback
IBIS quality

## Slide 16: Specifications for IBIS-IO-models
www.eigroup.org/ibis/ibis.html
IBIS spec
Cookbook ( new release will cover up to IBIS4.0 )
Accuraccy spec
Quality spec
Work in progress

## Slide 17: ICM Spec
Not yet supported by the tools, but:
It will/must be a standard
Can be changed into another format (for the tools)
Information about connector / package available in a specified format
Work in progress

## Slide 18: Missing descriptions for
driver schedule models
gtlp with open-sink/source (  new cookbook )
totem-pole-multistages
Fall back submodels
ODT-models (dynamic clamp ) (  new cookbook )
Bushold submodels
Keyword ReceiverThresholds (SSTL)
Work in progress

## Slide 19: ICEM and bird95
Integrated circuit electrical model for description of the power activities of the whole IC, especially for the core
For EMI- predictions
For ICEM there is a cookbook available
Work in progress
ICEM
Description of the current behavior of the outstage and their prestages with the use of I-T-tables
For SSO- analysis
Supply of a good cookbook required
Bird95.1
Notes: ICEM describes the power integrity of the whole IC with assumptions for the core switching behavior
( Integrated circuit electrical model )
Bird95.1 belongs more to the SSN for the outputstage, but includes also the behavoir of the prestages.
This means, that the current through the pre-stages as well as the crow-bar-current of the IO-stage itself will be taken into acount.
So power noise in simultaneous switching will be modeled more correctly
For a better description of the power supply behavior of the output stage the bird makes an suggestion, on how this can be modeled

## Slide 20: Summary ( work to do to decrease the disparity )
Models with different PVT must be delivered
( possible in IBIS ) for new models
IBIS supports different possibilities to help
the vendors to create IBIS-models with the
newest keywords/parameters
Quality Checklist is ready for use by vendors
( it‘s for free )
Important keywords/parameters for new models
must be supported by the vendors
For new keywords, the ibis-forum must provide
a clear description / cookbook