## Slide 1: Computer-Assisted Modeling of Digital I/O Buffers for IBIS
F.G.Canavero1, I.A.Maio1, I.S.Stievano1, M.Swaminathan2, P.Franzon3
1 Politecnico di Torino, ITALY (http://www.eln.polito.it/research/emc)
2 GaTech, Atlanta, USA
3 NC State University, USA

## Slide 2: Discussion within CPMT – TC12
Electrical Design, Modeling and Simulation (EDMS, TC-12) sub-commitee
EDMS sub-committee works on the standardization of design tools and design methodologies in packaging
http://www.ewh.ieee.org/soc/cpmt/tc12/
→ First meeting @ EPEP, Oct. 2004 in Portland, Oregon, USA.
http://www.ewh.ieee.org/soc/cpmt/tc12/standardization_files/IBIS_TC12a.ppt
Initiative for “Practical Macromodels for Digital I/O”
SPI (Signal Propagation on Interconnets) IEEE Workshop,
May. 10-13, 2005 in Garmisch-Partenkirchen, Germany
(c.f.p. at http://www.spi.uni-hannover.de/)

## Slide 3: I/O Buffers Macromodeling
  IP protection
  Vendor-independent format
  Have to capture TX, RX, and package parasitic essentials
  Sufficiently accurate to be useful
  Easy to automatically generate from Spice and Measurements
  Easy to verify
  Easy and fast to simulate
Required Goals:

## Slide 4: I/O Buffers Macromodeling Current status
Circuit-based modeling
Black-box modeling
- standard,
- large data/model libraries,
- EDA tools support...
…aimed at improving the modeling of latest technologies and high-order effects
- LVDS drivers with
pre-emphasis
- DDR memories,
- power supply ports…
v
i
e.g., parametric
modeling
i=F(v,d/dt)
specification and tools from http://www.eigroup.org/ibis/
(native IBIS)

## Slide 5: I/O Buffers Macromodeling The way forward
IBIS-based
models
Black-box
models
IBIS ver 4.1
“IBIS multilingual extension” (ver. 4.1) allows external SPICE, VHDL-AMS,…
user-defined models
TOOL for the “AUTOMATIC” generation of multi-platform (SPICE, VHDL-AMS,…) computational models

## Slide 6: Black-box modeling @ Politecnico di Torino
IC
i(t)
v(t)
i(t)
v(t)
F
i(k) = F(,[i(k-1)…, i(k-r),v(k),…, v(k-r)])
 nonlinear basis functions
Model parameters () via system identification methods
Mlog© (Macromodeling via parametric identification () of logic gates): Method & Tool

## Slide 7: Mlog features
Single-Ended
Differential
Drivers
Receivers
010…
010…
+
Power Supply ports
Temperature effects

## Slide 8: Mlog Tool
Tool available on request (igor.stievano@polito.it)

## Slide 9: Mlog Tool
0
0.5
1
1.5
x 10
-8
0
0.5
1
1.5
t, s
transient simulation time: 1.72e-008 s
v, V
0
0.5
1
1.5
x 10
-8
1.4
1.6
1.8
2
t, s
vdd, V
RUN YOUR PREFERRED CIRCUIT SOLVER (e.g. SPICE)

## Slide 10: Mlog Tool
AUTO LOADING

## Slide 11: Mlog Tool

## Slide 12: Conclusions (i)
  IP protection
  Vendor-independent format
  Have to capture TX, RX, and package parasitic essentials
  Sufficiently accurate to be useful
  Easy to automatically generate from Spice and Measurements
  Easy to verify
  Easy and fast to simulate
☺
☺
☺
☺
☺
☺
☺
☺
☺
☺
☺
☺
☺
☺
☺
☺

## Slide 13: Conclusions (ii)
Black-box models are expressed by equations that are used as they are, without any interpretation
no data to model conversion needed
flexible modeling methods
model enhancements do not affect IBIS and IBIS simulator structures
The distribution of black-box models would be a valuable complement to the distribution of behavioral data

## Slide 14: Acknowledgements
for providing the Analog/Mixed-Signal simulator environment (ADVance MSTM + EldoTM)
Thanks to
Sergio Perazza (Mentor, Italy) for the technical support on Mentors’ products
Arpad Muranyi (Intel) for VHDL templates and code posted on http://www.eda.org/pub/ibis/summits/jun03a/ and http://www.eda.org/pub/ibis/summits/feb04a/