## Slide 1: Modeling Formats and Procedures at Intel
Michael Mirmak
Intel Corp.
JEITA IBIS Conference
March 24, 2005
マイケル マ一マク
インテル コ一ポレ一ション
Notes: CG White Template

## Slide 2: Agenda
Introduction and Disclaimer
Modeling Flow
Formats Used for External Distribution
Future Direction and Investigations
Evaluating Model Formats
Key Questions for the Industry

## Slide 3: A Disclaimer
The following information is presented as the opinion of one person at Intel. This presentation does not necessarily represent Intel policy, commitments or preferences.
This is not presented on behalf of the IBIS Open Forum and does not represent the official IBIS Open Forum direction.

## Slide 4: General Modeling Flow
Conversion
to
Customer
Distribution
Format
Correlation
Between
Formats
or to Silicon
Internal
Buffer
Design
Format

## Slide 5: Modeling Flow
Buffer Design
  Internal SPICE-like format
  Internal tool also supports IBIS, AMS languages
Conversion to External Formats
  IBIS is majority model type supported
    Data generated directly from internal format
    Other proprietary behavioral formats on case-by-case basis
  Encrypted HSPICE used for one group of customers
    Process file conversion used for model generation
Correlation Over Process, Voltage, Temperature
  I-V curve-tracing performed to correlate IBIS
  Time- and frequency-domain analysis of systems
  “Silicon-to-Simulation” correlation of process files to factory production data

## Slide 6: Curve-Tracing Example
IBIS defines “envelope” for silicon data
  Weakest IBIS should be weaker than silicon, etc.
PULLUP CURVE – IBIS vs. SILICON
Min IBIS
Min Silicon

## Slide 7: External Formats
Different divisions use different formats
  Format choices based on customer demand and capabilities, internal technical analysis
Reasons for use of proprietary SPICE
  Control over buffer features (example: impedance)
  Latch-to-latch: more ps from timings at core!
TX
Buffer
RX
Buffer
CORE
CORE
PKG
PKG
PCB
IBIS MEASURES TIMING
HERE
LATCH-TO-LATCH
MEASURES TIMING HERE

## Slide 8: Transistor-Level SPICE Modeling
Why are transistor models popular?
  Familiar to users
  More detail seen as more accuracy (misconception)
  Behavioral models add some effort, burden
    Encrypted transistor very simple to distribute – just include everything and send files to customers
    Behavioral models require conversion, correlation
  Transistor simulation faster as computer speed increases
    PI, SSO still very difficult at transistor-level
  Behavioral methods sometimes difficult to use
    Example: impedance control in IBIS
  Latch-to-latch detail not seen in behavioral models
    AMS is promising here

## Slide 9: Studies of Behavioral Modeling Types
Intel team is studying formats
  Behavioral Modeling Workgroup meets weekly
  Mission: develop methods for IBIS, AMS modeling; analyze new proposals (ex. SPICE macromodeling)
Key goals
  Develop standardized methods, templates for AMS
  Add features: latch-to-latch, new controls (ex. impedance)
  Correlate AMS against internal format, proprietary SPICE
Ideal: a single format that can be used company-wide
  Short term: IBIS, encrypted HSPICE remain
  Longer term: IBIS divisions will move to AMS+IBIS
    Teams using encrypted HSPICE will evaluate AMS capabilities, consult with customers
  No compelling case for SPICE macromodeling yet

## Slide 10: How to Evaluate A Model Format
Seven basic desires for a modeling solution
  “I want it to be accurate”
  “I want it to be fast in my simulator”
  “I want it to protect my IP”
  “I want it to be standardized”
    Works for more than one tool
  “I want it available soon”
  “I want it easy to use/implement/automate”
  “I want maximum flexibility in describing my buffer design’s behavior”
A “perfect” solution can only meet six desires (so far)

## Slide 11: Customer Solutions and the 7 Rules

## Slide 12: Questions for Industry
Transistor encrypted SPICE is very popular
  Is either AMS or Macromodeling more compelling?
Will customers support behavioral modeling?
  Behavioral models are faster in simulation, but take more effort to generate
  Can customers be convinced they are accurate?
What is the best long-term industry solution?
  Macromodeling standardization will take time
  Should we develop macromodeling specification or educate industry about AMS usage?
How will IP be protected?
  Behavioral modeling uses algorithms, not process details or design netlists
  Some design algorithms may be sensitive
  Behavioral encryption may require standardization

## Slide 13: BACKUP

## Slide 14: What is the greatest use for IBIS?
IBIS originally consisted of two parts
  Device model behavioral data: V-t, I-V tables, etc.
    “Snapshot” at certain conditions (Temp, etc.)
  Interface specs, for user automation: Vinh, Vmeas, etc.
  Power supply information fits in both categories
With AMS or Macromodeling, some of IBIS redundant
  Behavioral modeling under IBIS very limited (no equations)
  Both alternatives are much more flexible than IBIS
IBIS interface specifications are still very useful
  AMS, Macromodeling describe device design behavior
  Still a need for a standardized SI “wrapper” around behavior
    Includes evaluation criteria
    Would help user judge device performance in system
    IBIS serves this need! Evaluation parameters for SI
    Need IBIS-based user-defined specs, measurements

## Slide 15: Solutions and the 7 Rules
IBIS 3.2/4.0
  Advantages
    Fast, IP protecting, standard, easy to use/implement
    Available immediately in tools
  Disadvantages
    Not accurate for certain functions (e.g., freq. dep. C)
    Not flexible (table-based, not equation-based)
AMS + IBIS
  Advantages
    Flexible, standardized, can be fast
    Can be accurate, depending on correlation effort
  Disadvantages
    Greater challenges to implementation
    Additional learning for users, model authors
      Templates would reduce this problem
    Not available in tools yet
    IP protection?

## Slide 16: Solutions and the 7 Rules
SPICE Macromodeling
  Advantages:
    EDA tools already support controlled sources
    Low barriers to use by behavioral experts
    Has flexibility beyond native IBIS
  Disadvantages:
    Obstacles to standards development
      Creating a standardized SPICE syntax
      Can this be done is less than two years?
    New features still require creation of new keywords
      Same development delay as in traditional IBIS
      Can controlled sources cover all equations?
    Still behavioral!
      More value than transistor-level models?
      Behavioral modeling expertise required!