## Slide 2: driver schedules: pre-/de-emphasis and frequency/data-rate issues
Eckhard Lenski
DATE , Munich , Germany
14th March 2008

## Slide 3
driver schedule: pre-/de-emphasis and frequency/data-rate issues
Pre-/De-emphasis basics
examples
Frequency /data rate
Driver schedule retrospection
summary

## Slide 4
driver schedule: pre-/de-emphasis and frequency/data-rate issues
Pre- /De-emphasis basics
Examples
Frequency /data rate
Driver schedule retrospections
summary
Notes: Sample animation slide
These are the only slides that have transitions.
These are to be spread sparingly through the presentation to help punctuate it.
Suggestion, these could be used at the start and/or end of section.

## Slide 5: pre-emphasis overview
CML- Preemphasis
Pre- or DE-emphasis is often realized with current-mode-drivers
and you can define 4 states:
( e.g. pre-emphasis )
Low
Low-Pre
High
High-Pre
time
Voltage
High
Low-Pre
High-Pre
Low
each bit after a change
of the logic state
is‚emphasized‘

## Slide 6: pre-emphasis switching modi
CML- Preemphasis
High
Low-Pre
High-Pre
Low
Low-Pre  High-Pre …101
1
1
There exist 4 possible switching modi
4
4
High  Low-Pre …110
3
3
High-Pre  Low-Pre …010
2
2
Low  High Pre …001

## Slide 7
driver schedule: püre-/de-emphasis and frequency/data-rate issues
Pre- / De-emphasis
Examples
Frequency /data rate
Driver schedule retrospections
summary
Notes: Sample animation slide
These are the only slides that have transitions.
These are to be spread sparingly through the presentation to help punctuate it.
Suggestion, these could be used at the start and/or end of section.

## Slide 8: driver schedule information
Driver schedule
IBIS summit presentations
    Arpad Muranyi
    Bob Ross
    Chris Reid
    Hazem Hegazy
    Lance Wang
    .......
IBIS cookbook 4.0
IBIS spec 4.2
????
time
v
Modeled with driver schedule

## Slide 9: driver schedule static curves
Driver schedule
[Model] 2-Driver-schedule
[Voltage Range] 3.30V 3.1350V 3.4650V
[GND Clamp]
[POWER Clamp]
[Pulldown]
[Pullup]
[Driver Schedule]
MODEL_1 0s NA 0ns NA
MODEL_2 0.5ns NA 0ns NA
[Model] Model_1
[GND Clamp]
[POWER Clamp]
[Pulldown]
[Pullup]
[Model] Model_2
[GND Clamp]
[POWER Clamp]
[Pulldown]
[Pullup]
Top level model tables
Scheduled model tables
Driver schedule timing

## Slide 10
driver schedule: pre-/de-emphasis and frequency/data-rate issues
Pre-/De-emphasis
Frequency / data rate
Examples
Driver schedule retrospections
summary
Notes: Sample animation slide
These are the only slides that have transitions.
These are to be spread sparingly through the presentation to help punctuate it.
Suggestion, these could be used at the start and/or end of section.

## Slide 11: Data signal & clock signal
Frequency / data rate
Data signal1 (NRZ)
Lo Hi Lo Hi Lo Hi Lo Hi
Data sampling window
Bit time or UI
clock signal
Lo Hi Lo Lo Lo Hi Lo Hi
Data signal2 (NRZ)
Clock period

## Slide 12: unit intervall and data rate (and frequency )
Frequency / data rate
Correlation
    Between Unit Intervall and Data rate
    Datarate = 1/ UI
      e.g.
    1.25Gbps = 1 / 800e-12s
    It takes one UI for one bit to be transmitted
Assuming a 1010.. Pattern
    For binary data signals :
Frequency = data rate /2
    This is not the clock frequency
    Eg. : Datarate  Frequency
5Gbps  2.5GHz
1.25Gbps  625MHz
Lo Hi Lo Lo Lo Hi Lo Hi
Data signal2
Duty cycle 25%
Duty cycle 50%
UI

## Slide 13: different patterns
pattern
1
0
1
1
0
0
1
0
time
V
data pattern 10101010
1
1
1
0
0
1
1
0
time
V
data pattern 11110100
1
1
0
0
1
0
1
0
time
V
data pattern 11001100

## Slide 14: classic IBIS model
Normaly the rising and falling times of the IBIS model
determines the max. frequency where the model can be used
Rule of thumb : Fmax IBIS model = 1/ ( trise + tfall )
Eg.: IBIS model with trise 2ns, tfall 2ns
Fmax = 1/ 4ns = 250Mhz
Trise Tfall
V
t
very simple IBIS model
Frequency / data rate
V
t
Trise Tfall
IBIS model

## Slide 15: driver schedule for Multi-Gigabit applications
Old rule of thumb : Fmax IBIS model = 1/ ( trise + tfall )
This rule is no longer valid
Frequency / data rate
The signal needs to be
long enough above high threshold
Or
Long enough below low threshold
And this for many times
V
t
Trise Tfall
V
t
very simple IBIS model
The signal needed to be
above high threshold
Or
below low threshold

## Slide 16
driver schedule: pre-/de-emphasis and frequency/data-rate issues
Pre-/De-emphasis
Frequency / data rate
Examples
Driver schedule retrospections
summary
Notes: Sample animation slide
These are the only slides that have transitions.
These are to be spread sparingly through the presentation to help punctuate it.
Suggestion, these could be used at the start and/or end of section.

## Slide 17: low frequencies pushpull-cmos model
Model has got risetime
and falltime of about 1ns
So it could be used
up to 500MHz !!??
Frequency / data rate
250MHz
0
0,2
0,4
0,6
0,8
1
1,2
0
1
2
3
4
5
V
t (ns)
t (ns)
100MHz
0
0,2
0,4
0,6
0,8
1
1,2
0
1
2
3
4
5
t
V
t (ns)

## Slide 18: high frequencies pushpull-cmos model
above 500MHz :
The behavior looks suspicious
Frequency / data rate
500MHz
0
0,2
0,4
0,6
0,8
1
1,2
0
1
2
3
4
5
t (ns)
V
750MHz
0
0,2
0,4
0,6
0,8
1
1,2
0
1
2
3
4
5
t (ns)
V

## Slide 19: Signal characteristics for pre-emphasis
time
each bit after a change
of the logic state
is‚emphasized‘
Frequency / data rate
1 1
High
High-Pre
rising egde contains information for datapattern 1 1
Low-Pre
Low
falling egde contains information for datapattern 0 0
0 0

## Slide 20: driver schedule @ 250MHz (tp=4ns)
Frequency / data rate
Rising part finished,
Model stays in this logic HIGH state,
until „tool“ switches to LOW
Rising egde part of driver schedule
0
0,5
1
1,5
2
2,5
3
3,5
4
t (ns)
V
0
0.6
0.8
1.0
1.2
1.4
1.6
1 0

## Slide 21: driver schedule @ 500MHz (tp=2ns)
Model shows the pre-emphasis behavior,
because the pattern 11 and 00 can be fulfilled
Rising part finished,
And the „tool“ switches to LOW
Frequency / data rate
0
0.6
0.8
1.0
1.2
1.4
1.6
0
0,5
1
1,5
2
2,5
3
3,5
4
t (ns)
V
1 0 1 0
Rising edge part of driver schedule

## Slide 22: driver schedule @ 750MHz (tp=1.333ns)
Model shows correct pre-emphasis behavior
for the first bit,
but for the second bit, it is switched off
Frequency / data rate
t (ns)
0
0.6
0.8
1.0
1.2
1.4
1.6
0
0,5
1
1,5
2
2,5
3
3,5
4
V
1 1 0 0 1 1 0 0
Rising edge part of driver schedule
Rising part not yet finished,
But the „tool“ switches to LOW

## Slide 23: driver schedule @ 1000MHz (tp=1ns)
Model shows a switching from High to Low,
but between High-Pre and Low-Pre,
So only the pattern 101010
will be shown correctly
Frequency / data rate
0
0,5
1
1,5
2
2,5
3
3,5
4
0
0.6
0.8
1.0
1.2
1.4
1.6
t (ns)
V
1 0 1 0 1 0
Rising edge part of driver schedule
Rising part only first bit finished,
But the „tool“ switches to LOW

## Slide 24: driver schedule @ 1250MHz (tp=0.8ns)
There is not enough time for the first bit
Because the tool starts switching off
Frequency / data rate
0
0,5
1
1,5
2
2,5
3
3,5
4
t (ns)
V
0
0.6
0.8
1.0
1.2
1.4
1.6
1 0 1 0 1 0 1 0
Rising edge part of driver schedule
Rising part not yet finished,
But the „tool“ switches to LOW

## Slide 25: eye diagrams preliminary
Frequency / data rate
!! Under construction !!

## Slide 26: driver schedule @ (250MHz) UI = 2000ps
Frequency / data rate

## Slide 27: driver schedule @ (500MHz) UI = 1000ps
Frequency / data rate

## Slide 28: driver schedule @ (750MHz) UI = 666.66ps
Frequency / data rate

## Slide 29: driver schedule @ (1000MHz) UI = 500ps
Frequency / data rate

## Slide 30
driver schedule: pre-/de-emphasis and frequency/data-rate issues
Pre-/De-emphasis
Examples
Frequency /data rate
Driver schedule retrospections
summary
Notes: Sample animation slide
These are the only slides that have transitions.
These are to be spread sparingly through the presentation to help punctuate it.
Suggestion, these could be used at the start and/or end of section.

## Slide 31: scope of application
summary
For normal pushpull-cmos
frequency
0
Fmax
data rate
0
G1
G2
G3
1.25Gbps
2.5Gbps
3.125Gbps
For Driver schedule modeling pre-emphasis

## Slide 32: encoded pattern
summary
For normal cmos
    10 pattern is encoded in the model
For Driver schedule modeling pre-emphasis
    1100 pattern is encoded in the model

## Slide 33: Summary
Ibis models (exception of driver schedule ) are ‚valid‘ for a frequency range which is set by the risefalltime of the model
Driver schedule modeling pre-emphasis are valid only for one datarate/frequency, corresponding to the UI they are made for
Tool don‘t cares about encoded bitpattern in model or the included bit-time / UI
User has to take care that the „frequency“ corresponds to UI
summary

## Slide 34: Thank You
Questions ?