## Slide 1
IBIS Version 3.2 - Update
Presentation for the 1999 IBIS Open Forum Summit
Stephen Peters - Vice Chair, EIA/IBIS Open Forum

## Slide 2
Current IBIS status
3.2 spec ratified at Jan. 1999 phone conference
Golden Parser complete and available
  IBIS website: http://www.eia.org/EIG/IBIS/ibis.htm
Version 3.2 going for ANSI-EIA ratification
  will be known at ANSI-EIA 656A

## Slide 3
Background - IBIS 2.1
I/O described with I/V curves and V/T curves
Initial support for GTL+ technology
However, there were limitations...
  Passive elements could not be described in IBIS
  Not adequate for multi-stage I/O and cartridge packaging technology
  Package limited to lumped L/R/C description

## Slide 4
IBIS 3.2 Enhancements Overview
Four basic areas were addressed
  I- Support for additional device types
    passive (2 pin) devices, terminators, bus switches
  II - Extended model specs and simulation hooks
    ringback and hysteresis specs, model selectors
  III - Support for advanced driver/receiver technology
    multi-staged outputs, bus hold, dynamic clamps
  IV - Enhanced package descriptions
    transmission line package stubs, .ebd files

## Slide 5
I - Additional Device Types
Support for passive (2 pin) devices
  [Series Pin Mapping] keyword allows pin to pin mapping
  ‘Series’ model type is added to [Model] Keyword
    can now describe series R/L/C, Lc, Rc components
    [Series Current] keyword describes diode I/V tables
Support for termination components
  added ‘Terminator’ model type to [Model] Keyword
  designed to model terminator packs (including RC)

## Slide 6
I - Additional Device Types (cont.)
Support for FET bus switches (Quickswitch)
  ‘series_switch’ model type added
    [On], [Off] keyword added to describe states
    on state uses [Series MOSFET] keyword to describe I/V
    off state model falls back to series R (very high value)
  [Series Switch Groups] allows user to describe functionality of a crossbar switch

## Slide 7
II - Extended Model Specification
Ringback/Hysteresis/Immunity limits added
  user specifies both static and dynamic overshoot/undershoot with [Model Spec] keyword
  supports Pentium® Pro processor specing methodology
[Model Selector] keyword for swapping in and out models
  more than one model can be mapped to a pin
  user (thru simulator I/F) selects which model to use

## Slide 8
III - Advanced Driver Technology
IBIS 3.2 can directly model multi-stage outputs
  [Driver Schedule] allows user to switch in/out curves
  supports GTL+ PMOS kicker
Added support for diode transient time effects
  user supplies a ‘transit time’ parameter
  add to [GND clamp] or [Power Clamp] curves on IC input to model diode kickback effect

## Slide 9
III - Advanced Driver Tech (cont.)
IBIS 3.2 introduces [Add Submodel] concept
  allows top level [Model] to call out additional functionality
  currently defined submodels include:
    Dynamic_clamp - switch on and off extra clamp tables
    Bus_Hold - switch on or off extra output tables
  Driver Schedule will most likely move here

## Slide 10
IV- Enhanced Package Descriptions
Transmission line description added to .pkg files
  each trace divided into sections
  each section described as a lumped or distributed element (i.e. transmission line)
  Branches (fork, endfork) allowed
  coupling only supported for pin field
Used for describing PGA and BGA pad to pin connections

## Slide 11
IV- Enhanced Package Description (cont.)
Electrical Board Description (.ebd) file
  .ebd file describes path between IC(s) mounted on a circuit board and external connector
  Traces described as lumped elements or uncoupled transmission lines
  If coupling is desired use a physical data base
.ebd files directly supports Pentium® II Processor cartridge descriptions

## Slide 12
What’s Ahead For IBIS
Connector models (coupled and uncoupled) are in the works
[Add Submodel] can be a path for general purpose expansion
  submodel can be anything
Possible merge or incorporation with IMIC standard??