## Slide 1
Detecting Typical Bugs
in IBIS Models

## Slide 2: Overview
IBIS Models are widely available for buffer
modelling to support signal integrity analysis
 Simple checks are recommended to guarantee
accurate simulation results
The models are easy to generate, to understand and to apply for simulation
Sometimes models contain bugs, which prevent users from successful simulation

## Slide 3: Overview
How to detect typical bugs?
 Users should briefly examine IBIS models
before application
Syntax bugs and other minor problems are detected by the parser
Other problems like inconsistencies in the specification of the electrical behavior are easily detected by ‘human’ plausibility checks

## Slide 4: Simple Problems
Simple problems are usually detected by the parser:
 Easy to find and to correct!
The file name specified inside the file does not correspond with the actual file name
The manufactures name is too long
...

## Slide 5: Supply Voltages
Different supply voltages are used for the
component buffers. Example:
 This results in incorrect pullup and Vcc clamping
characteristics
The external supply voltage of a component is Vdd = 3.3V
But for output buffers of HSTL normally Vddq = 1,5V is used
Often Vddq is set to Vdd in IBIS models

## Slide 6: Pullup Currents
Specification of pullup currents
Ipup(Vtable) = Ipup(Vcc - V out)
Vcc relative definition
Vtable
Vout
Ipup
GND
Vcc

## Slide 7: Pullup Currents
Specification of pullup currents
inverted current direction
Vcc relative specification not considered
Typical mistakes

## Slide 8: Pullup Currents
Another experience
Often, the V/I curves do not pass the origin ( I(0V)  0 )
 In conjunction with Vcc,this results into a
static high level which does not match with the specified value

## Slide 9: Clamping Characteristics
included in the pullup / pulldown currents
and specified separately
 Same effect considered twice
Clamping effect

## Slide 10: Invalid Ramp Data
Rising edge (dV/dt) is specified such that dV=3V
From static V/I curves with specified load Vlow and Vhigh are calculated such that Vhigh-Vlow = 2.8V
Example:
 Conflicting specifications

## Slide 11: Differential Buffers
static behavior (e.g. V / I curves)
dynamic behavior (dv/dt, rising/falling waveforms)
Often, dynamic behavior is measured using differential terminations
IBIS only supports independent buffer description for positive and negative output by
This load cannot be considered in IBIS models!
R
C1
C2
(+)
(-)

## Slide 12: Conclusion
IBIS models are well suited for SI analysis, but
Manufactures should spend more effort to make sure that the models are correct
Users should not trust in models blindly, as simple plausibility checks can avoid incorrect simulation results