## Slide 1
Future Requirements on
Frequency Dependent
Package and MCM Modeling

## Slide 2: Overview
Recent results of research projects have shown
that it will be necessary to consider frequency
dependent behaviour of MCM and package
interconnect structures in future.
Requirements:
PARASITICS, http://parasitics.ims.uni-hannover.de,
funded by BMBF under grant 01 M 3034 G
Limited complexity to be applied in time domain simulation
Reasonable accuracy
1
1

## Slide 3: Example
Typical MCM structure
Objects to be modelled:
redistribution network
x/y wiring
vias

## Slide 4: Example
Basic lumped elements for
signal path description
Equivalent circuit for Skin Effect
modelling (R  f)
T element
 element
Frequency independent structures

## Slide 5: Example
Simulation model for
a selected MCM signal
path using basic lumped
elements
 Complex network of
passive components

## Slide 6: Example
Comparison of
simulation and
measurement
Scattering
parameter S11

## Slide 7: Example
Comparison of
simulation and
measurement
Scattering
parameter S21

## Slide 8: Coupling
Consideration of parallel interconnect structures
has to be limited to allow efficient parameter
extraction and simulation
 4 x 4 system of frequency dependent transmission
line parameters to consider coupling effects

## Slide 9: Conclusion
Lumped element descriptions are sufficient for frequency dependent modelling of single signal paths on MCM and packages
Currently IBIS is supporting only limited structures to support this kind of modeling
IBIS format has to become more flexible to support various types of lumped element models efficiently
Frequency dependent transmission line parameters will become important for modelling of signal paths including coupling in future