## Slide 1: IBIS model verification
www.sintecs.eu
  European IBIS summit 2010
  Hildesheim, Germany
  May, 12th 2010
  Presenter: Hans Klos
  hans.klos@sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>

## Slide 2: Background
  Sintecs is a European electronics design engineering & services company
  Sintecs
    Offices: Hengelo, The Netherlands, and Minsk, Belarus
    High speed board design and analysis
  IBIS modeling experiences
    Creation and verification of ibis models
    Free IBIS model viewing and editing utility, "IBIS Development Studio“
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>

## Slide 3: IBIS model verification
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>
  Step 1. IBIS golden parser
  Step 2. Graphical inspection
  Step 3. IBIS quality checks
  Step 4. Simulation with standard test load
  Step 5. Compare with measurement result

## Slide 4: IBIS Quality levels
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>
  IQ0 - No check performed
  IQ1 - Passes IBISCHK without Errors or unexplained Warnings
  IQ2 - IQ1 + data for basic simulation checked
  IQ3 - IQ2 + data for timing analysis checked
  IQ4 - IQ3 + data for power analysis checked
  Special designators
  IQ3M - IQ3 + correlated against hardware measurements
  IQ3MS - IQ3 + correlated against measurements and simulation
  IQ3GS - IQ3 + golden waveforms + correlated against simulation
  IQ4X - IQ4, but exception(s) to check(s) commented in file

## Slide 5: Golden Parser and graphical inspection
www.sintecs.eu
IBIS Golden parser check
Graphical Inspection with an IBIS model viewer
© Sintecs BV 2010 <number>
IBIS model verification

## Slide 6: Non-monotonic waveform
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>
Pull-down data is non-monotonic, do I need to fix this and how???

## Slide 7: Combine waveforms
When the pull-down and ground clamp IV curves are combined, the non-monotonic behavior is not present. Still fix pull-down ???
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>

## Slide 8: ESD clamping diodes
Example:
Standard CMOS device without signal clamping diodes.
The ground clamp of this CMOS buffer, clamps multiple Amps (ESD diode present).
Can you use this diode for signal clamping?
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>

## Slide 9: Effect of ESD clamping diodes in IBIS
Blue waveform is with the ground-clamp and the red waveform, when the ground clamp is disabled.
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>

## Slide 10: C_comp example
  C_comp value is 10x larger than in datasheet
    IBIS golden parser doesn’t complain.
C_comp = 10 pF
C_comp = 1 pF
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>

## Slide 11: IBIS Quality check
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>
  Different level and type of checks
    Components checks
    Model checks

## Slide 12: Model verification time
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>
  Time spend for full verification (Level3) depends on the number of models available in the ibis model.
  Example Altera Stratix IV has more than 300 different buffer models. Verifying this ibis model with the IBIS Quality template will cost several weeks/months.
    What will happen when you get a new version of the Stratix IV model ??

## Slide 13: Other model types
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>
  IBIS AMI
  Touchstone model
  IBIS ICM
  Package model
  EBD model

## Slide 14: IBIS-AMI
  What is IBIS-AMI
  The IBIS Algorithmic Modeling Interface (IBIS-AMI) is a modeling standard for SerDes transceivers that enables fast, accurate, statistically significant simulation of multi-gigabit serial links. IBIS-AMI was developed by a consortium of EDA, Semiconductor and Systems companies and was approved as part of the IBIS 5.0 specification in August 2008.
  IBIS-AMI models have two parts
    Analog model
    Algorithmic model
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>

## Slide 15: IBIS-AMI model verification
  Algorithmic model
  Supplied as binary code (.DLL) that gets linked into the Channel Simulator at runtime
  No verification can be done, comparison with measurement is needed.
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>

## Slide 16: Touchstone model
  A Touchstone file (also known as an SnP file) is an ASCII text file used for documenting the n-port network parameter data of an active device or passive interconnect network.
  Touchstone® File Format Specification Version 2.0 (April 2009)
  A Touchstone parser, tschk2, is available
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>

## Slide 17: IBIS ICM
  The IBIS Interconnect Modeling Specification (ICM) is a behavioral, ASCII-based file format for distributing passive interconnect modeling information.
  An ICM parser, icmchk1vailable.
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>

## Slide 18: Package model
  Available in ibis model or in separate *.pkg file.
  More detailed package model than standard lumped R_pin, L_pin, C_pin or generic [Package] statement.
  .pkg models are transmission line models
    RLC matrixes for coupling
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>

## Slide 19: EBD model
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>
  EBD – Electrical Board Description
  A pure transmission line description without coupling
  All inductance and capacitance parameters listed in the file are derived with respect to well-defined reference plane (s) within the board
  Via in EBD is described as zero length with lumped RLC value
  EBD is good for transmission line effect investigation and timing analysis for first order consideration.

## Slide 20: Conclusion
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>
  Verification of IBIS models is needed for accurate SI analyses
  Different types of models are available
  Detailed verification of IBIS models costs a lot of time
  Automation needed for accurate and fast model verification

## Slide 21
Questions ?
www.sintecs.eu
IBIS model verification
© Sintecs BV 2010 <number>
Notes: <number>