## Slide 1: IBIS Activities
Bob Ross
European IBIS Summit
Hildesheim, Germany
May 12, 2010
bob@teraspeed.com

## Slide 2: IBIS Organization
Officers
  Chair: Bob Ross, Teraspeed Consulting Group
  Vice-Chair: Lance Wang, IO Methodology
  Secretary: Randy Wolff, Micron Technology
  Webmaster: Syed Huq, Cisco Systems
  Postmaster: Mike LaBonte, Cisco Systems
  Librarian: Anders Ekholm, Ericsson
Active task groups
  IBIS Model Review – Free review service
  Quality - IBIS Quality Specification, correlation
  Interconnect - Touchstone Spec., ICM, MCP
  Advanced Technology Modeling - AMI work

## Slide 3: “ibischk5” Parser (2009)
Ibischk5, Version 5.0.3
  Free executables: http://www.eda.org/pub/ibis/ibischk5/
  Supports IBIS Version 5.0 (ratified 2008)
    Algorithmic model interface for Serdes analysis
    Power delivery system SSO and gate modulation
    EMI parameters
    Other – (area based thresholds)
Checks all [IBIS Ver]s of IBIS files
Over $100,000 of contracted work since 1993
Supports .ibs, .pkg, .ebd, and .ami formats directly or through linkages

## Slide 4: New Flags in ibischk5
–ami for <file_name>.ami (algorithmic model interface control file)
–numbered for numbered Error, Warning, Notes and Caution messages
Usage: ibischk5 <IBS filename>
: ibischk5 -ebd <EBD filename>
: ibischk5 -pkg <PKG filename>
: ibischk5 -ami <AMI filename>
Usage: ibischk5 -caution -numbered <IBS filename>
: ibischk5 -caution -numbered -ebd <EBD filename>
: ibischk5 -caution -numbered -pkg <PKG filename>
: ibischk5 -caution -numbered -ami <AMI filename>
The flags prior to the file name can be in any order, and the -caution and/or -numbered flags are optional.

## Slide 5: ibischk5 {–numbered} –ami file4.ami
Checking file4.ami for IBIS 5.0 Compatibility...
ERROR - Illegal Usage value A specified for Param1
ERROR - Illegal Type value B specified for Param1
ERROR - Illegal Format value C specified for Param1
ERROR - No Reserved_Parameters found
Errors : 4
File Failed
Checking file4.ami for IBIS 5.0 Compatibility...
E4627 - Illegal Usage value A specified for Param1
E4627 - Illegal Type value B specified for Param1
E4627 - Illegal Format value C specified for Param1
E4622 - No Reserved_Parameters found
Errors : 4
File Failed

## Slide 6: “tschk2” Parser (2009)
Checks Touchstone Version 1.0 (TS1) and Version 2.0 (TS2)
  Error and Warning numbers
  Free executables: http://www.eda.org/pub/ibis/tschk2/
Converts TS1 to TS2, TS2 to TS1 where practical with -canonical* flags
Provides comment headers and real, imaginary format (RI) with -describe flag
Source code package includes 440+ test cases
C++, well documented
Thanks to contractor Agilent Technologies

## Slide 7: tschk2 {-canonical*} FILE
{-canonical | -canonical-v2}
  TS1, TS2  TS2
  Provides number of ports, frequencies and other information
  Un-normalizes TS1 Y-, Z-, G- and H-parameters and effective noise resistance
{-canonical-v1}
  TS1, TS2  TS1 where practical
  Applies column formatting rules and 2-port 21_12 ordering
  Normalizes TS2 Y-, Z-, G- and H-parameters and effective noise resistance
  No mixed mode or selectable reference resistance processing

## Slide 8: Projects, Activities
IBIS Version 5.1 – improved AMI
  ibischk5, Version 5.0.X – bug fixes, Version 5.1.0 with improvements
Touchstone 2.1 – adds sparse matrix mapping and binary format
  tschk2, Version 2.1.0
IBIS Interconnect Subcircuit Spice (IBIS-ISS)
Model Connection Protocol (MCP)
Correlation specification in Quality task group
IBIS summits, thanks Ralf Bruening and Eckhard Lenski for arranging the European IBIS Summits