## Slide 1: BIRD95 and BIRD98 Simulations
May 11, 2011
Randy Wolff – Micron Technology
Lance Wang – IO Methodology
European IBIS Summit
Naples, Italy
May 11, 2011

## Slide 2: Introduction
[Composite Current] table data – added to IBIS 5.0 through BIRD95.
[ISSO PD] and [ISSO PU] table data – added to IBIS 5.0 through BIRD98.
Simulation done with two tools (available to authors) that include full/partial support for BIRD95 and BIRD98 in current releases.
IBIS 5.0 DDR3 model developed and used to compare simulation tools to golden SPICE model results.
May 11, 2011

## Slide 3: [Composite Current]
Describes the shape of the rising and falling edge current waveforms from the power reference terminal of the buffer*.
Adds pre-driver current I-t data.
May 11, 2011
* Text and image from IBIS 5.0 Specification

## Slide 4: [Composite Current] Data
Load = 50 ohms to [Pullup Reference]
May 11, 2011

## Slide 5: [Composite Current] Data
Load = 50 ohms to [Pulldown Reference]
May 11, 2011

## Slide 6: [Composite Current] Data
Load = 1E9 ohms to [Pulldown Reference] (No load)
May 11, 2011

## Slide 7: [Composite Current] Observations
Significant ‘dead time’ must be added to beginning of V-t curves to correlate with time of pre-driver current.
  This limits model switching rate – encourages overclocking.
  Example model originally DDR3-1066, now DDR3-800.
[Composite Current] only includes [Pullup Reference] supply current.
  Algorithms can only assume that [Pulldown Reference] current is equal to [Pullup Reference] current.
  Is this valid?
May 11, 2011

## Slide 8: [ISSO PU] & [ISSO PD]
Data tables define the effective current of the pullup/pulldown structures of a buffer as a function of the voltage on the pullup/pulldown reference nodes*.
Adds modeling of the gate modulation effect on driver current (IDS vs. VGS).
May 11, 2011
* Text and image from IBIS 5.0 Specification

## Slide 9: [ISSO PD] Data
May 11, 2011
Pulldown
ISSO PD

## Slide 10: [ISSO PU] Data
May 11, 2011
Pullup
ISSO PU

## Slide 11: [ISSO PU] & [ISSO PD] data in IBISCHK5
IBISCHK5 checks that Isso_pd(0)=Ipd(Vcc) and Isso_pu(0)=Ipu(Vcc).
  Pulldown is 0.42% different, Pullup is 0.12% different (typ).
  IBISCHK5 issues a WARNING. Is it too sensitive?
    WARNING - Model DQ_34_1066: Minimum ISSO_PD current ( 0.031A) at 0V does not match Pulldown current ( 0.031A) at reference ( 1.425V)
IBISCHK5 checks that Isso_pd(Vcc)=0 and Isso_pu(Vcc)=0.
  Should a value of X nA cause a WARNING?
    WARNING - Model DQ_34_1066: Minimum ISSO_PD current (-0.000A) at Pullup reference ( 1.425V) - table value ( 1.425V) is non-zero
  Note that the number of significant digits reported in the WARNING messages are not enough to indicate a problem.
May 11, 2011

## Slide 12: Using [ISSO PU] & [ISSO PD] data
Modulation coefficients can be calculated from the data (Ksso_pu & Ksso_pd).
  What is the Ksso_pu value for a 50mV drop in Vcc?
    Ksso_pu(Vtable_pu) = Isso_pu(Vtable_pu)/Isso_pu(0)
    Ksso_pu(50mV) = Isso_pu(50mV)/Isso_pu(0)
    Ksso_pu = -28.1067mA/-30.16485mA = 0.9318
  What is the Ksso_pd value for a 50mV rise in Vss?
    Ksso_pd(Vtable_pd) = Isso_pd(Vtable_pd)/Isso_pd(0)
    Ksso_pd(50mV) = Isso_pd(50mV)/Isso_pd(0)
    Ksso_pd = 34.83905mA/37.13536mA = 0.9382
  For this example, a 50mV drop in supply voltage translates to a ~7% reduction in the K scale factor.
May 11, 2011

## Slide 13: Simulation Results
Comparing Tools A & B
May 11, 2011

## Slide 14: Simulation Setups
PRBS pattern, minimum bit width of 1.25ns.
Typical corner only.
On-die decoupling capacitance included.
  No method to properly include through IBIS syntax (Series models attach to Pins, not die).
Sim 1: DQ1 only, no package model
  Compares BIRD95 directly to SPICE.
Sim 2: DQ1 only, Rpkg = 5 Ω
  Tests BIRD98 current scaling.
Sim 3: DQ1 + DQ2 (in tri-state) with 8-port SPICE coupled package model
  What happens with real package RLCs?
Sim 4: DQ1 + DQ2 (with different PRBS) with SPICE package model
  What happens with more than one buffer (real SSO conditions)?
May 11, 2011
VTT
50 Ω
Zo=50 Ω
3pF
PKG
VSSQ
PKG
VTT
50 Ω
Zo=50 Ω
3pF
PKG
VCCQ
PKG
DQ1
DQ2
VSSQ_DIE
VCCQ_DIE
I(VCCQ)
I(VSSQ)
DECAP

## Slide 15: Sim 1, Tool A
May 11, 2011
VSSQ current improved over baseline.
VCCQ current matches well.

## Slide 16: Sim 1, Tool B
May 11, 2011
VSSQ current improved over tool A.
VCCQ current matches well.

## Slide 17: Sim 1, Tool A, 1.25ns Bit Width
May 11, 2011
[Composite Current] is truncated
[Composite Current] is truncated

## Slide 18: Sim 1, Tool B, 1.25ns Bit Width
May 11, 2011
[Composite Current] is NOT truncated
[Composite Current] is NOT truncated

## Slide 19: Sim 2, Tool A
May 11, 2011
BIRD98 alone is a poor match.
BIRD98 improves BIRD95 results.
Matching to SPICE results ok.

## Slide 20: Sim 2, Tool B
May 11, 2011
BIRD98 alone is a poor match.
BIRD98 improves BIRD95 results.
Matching to SPICE results ok.

## Slide 21: Sim 3, Tool A
May 11, 2011
BIRD95 and BIRD95 + 98 results are a better match to SPICE.
SPICE shows delay not seen with IBIS.

## Slide 22: Sim 3, Tool B
May 11, 2011
BIRD95 and BIRD95 + 98 results are a better match to SPICE.
SPICE shows some delay not seen with IBIS.

## Slide 23: Sim 4, Tool A
May 11, 2011
BIRD95 and BIRD95 + 98 results are a better match to SPICE.
Results not improving with com-plexity of sim.

## Slide 24: Sim 4, Tool B
May 11, 2011
BIRD95 and BIRD95 + 98 results are a better match to SPICE.
Results not improving with com-plexity of sim.

## Slide 25: Conclusions
Implementations of BIRD95 significantly improve power supply current simulation accuracy.
Implementations of BIRD98 improve upon accuracy of BIRD95 alone.
BIRD98 without BIRD95 does not improve results for these test cases.
Algorithms could use further improvement to better match SPICE simulations that include package parasitics.
IBISCHK5 may be too ‘sensitive’ for BIRD98 checks.
May 11, 2011

## Slide 26
Jul 29, 2026