## Slide 1: DDR4 IBIS Power Integrity Simulation
Randy Wolff – Micron Technology
Lance Wang – IO Methodology
European IBIS Summit
Sorrento, Italy
May 16, 2012

## Slide 2: Outline
DDR4 introduction
Motivation for presentation
DDR4 IBIS 5.0 model creation
Power Integrity simulation results
Conclusions

## Slide 3: DDR4 Introduction
Latest generation of SDRAM memory
  SDR  DDR1  DDR2  DDR3  DDR4
1.2V VDD/VDDQ
1600Mbps – 3200Mbps data rates
Output Drive Impedance – 34, 40, 48 ohms
DQ bus termination to VDDQ – significant change to signaling versus DDR3
On-Die Termination is pullup-only to VDDQ
  RTT_nom has all selections available, 240/(n) where n is 1 to 7 and off. [240, 120, 80, 60, 48, 40, 34]

## Slide 4: Motivation
PI capabilities of DDR3-800 models investigated last year
DDR4-1600+ versus DDR3
  Higher data rates – overclocking issues?
  VDDQ terminated bus – do imbalanced VDDQ/VSSQ currents cause any inaccuracies?
  Different pre-driver characteristics
  Similar VDDQ/VSSQ decoupling characteristics
Updated software – how does it handle the new models?

## Slide 5: DDR4 IBIS 5.0 Model Creation
Automated buffer extraction tool used for quick data extraction
Extracted I-V, 4 V-t + [Composite Current]s, [ISSO PU] and [ISSO PD]
  Best-points-fit algorithm applied to all data sets
    Not critical with 1000 possible data points on V-t and I-t, but what if you need to later downgrade a model to 100 points for IBIS 3.2 compatibility?
    Critical for data sets with 100 points (I-V)

## Slide 6: [Composite Current] Data
Note min corner is ~850ps long, bit time is 625ps

## Slide 7: V-t Data
V-t/I-t start/end times match, time points non-correlated

## Slide 8: I-V Data – Pullup, Pulldown, ISSO
ISSO data is very linear in range of Voltage supply swing

## Slide 9: Power Integrity Simulation Results

## Slide 10: Simulation Setups
PRBS pattern, minimum bit width of 625ps.
Typical corner only.
On-die decoupling capacitance included as SPICE subckt model
Sim 1: DQ2 only, no package model
  Compares IBIS 5.0 directly to SPICE.
Sim 2: DQ2 only, Lpkg(VSSQ/VSS)=0.15nH, Lpkg(VCCQ)=0.30nH, K=0.2
Sim 3: DQ[0-7] + DQS_t/DQS_c (DQ2 with different PRBS) with fully coupled SPICE package model
  Testing real SSO conditions
VTT = VCCQ
50 Ω
Zo=50 Ω
2pF
PKG
VSSQ
PKG
50 Ω
Zo=50 Ω
2pF
PKG
VCCQ
PKG
DQ2
DQ[0,1,3–7] +
DQS_t/DQS_c
VSSQ_DIE
VCCQ_DIE
I(VCCQ)
I(VSSQ)
DECAP
load
VTT = VCCQ

## Slide 11: Sim 1, DDR4-1600
VCCQ current matches well.
Significant improvement over IBIS 3.2.

## Slide 12: Sim 1, DDR4-1600
VSS/VSSQ shorted on die introduce pre-pre-driver currents that IBIS can’t model.
Appears to be a slight overclocking issue in the VCCQ currents. Dead time at end of typical corner V-t curves already chopped.

## Slide 13: Sim 1, DDR4-1866 (overclocked)
At DDR4-1866, bit time of 536ps causes severe overclocking issues.
V-t waveform is ~750ps long with tail removed. Can still remove ~100ps from start delay. Will this help?

## Slide 14: Sim 1, DDR4-1866 (overclocked)
Current wave-form shows overclocking artifacts and is shifted 100ps. Looks like a Bug!
Removing 100ps from initial delay time fixes Voltage waveform at the load.

## Slide 15: Sim 2, Includes L_pkg
Reasonable correlation between SPICE and IBIS 5.0 models.
More detailed power supply decoupling model might improve results.

## Slide 16: Sim 3, Full SSO Simulation
Good VCCQ current correla-tion between SPICE and IBIS 5.0 models.
VCCQ voltage noise over-estimated.
Slight time delay in SPICE results not modeled in IBIS.

## Slide 17: Conclusions
Overclocking issues with IBIS 5.0 models are a serious concern at 1600Mbps+ data rates.
DDR4 Power Integrity can be modeled reasonably well with IBIS 5.0.
Automated IBIS extraction tools for IBIS 5.0 PI data tables will help speed up adoption and prevalence of these models.