## Slide 1: Ibischk5 Specification and Parser
European IBIS Summit
Paris, France, May 15, 2013
Bob Ross Mike LaBonte
Teraspeed Consulting Group Signal Integrity Software
(SiSoft)
bob@teraspeed.com mikelabonte@eda.org
Presented by Anders Ekholm, Ericsson

## Slide 2: Outline
Ibischk5 specification
  Document update
  Work in progress
Ibischk5 Version 5.1.3 release
  BUG140 discussion

## Slide 3: Outline of ibischk5 Parser Spec
…
…

## Slide 4: Command Line for ibischk5
–ami for <file_name>.ami (algorithmic model interface control file)
–numbered for numbered Error, Warning, Notes, Caution, and Bug messages
Usage: ibischk5 <IBS filename>
: ibischk5 -ebd <EBD filename>
: ibischk5 -pkg <PKG filename>
: ibischk5 -ami <AMI filename>
Usage: ibischk5 -caution -numbered <IBS filename>
: ibischk5 -caution -numbered -ebd <EBD filename>
: ibischk5 -caution -numbered -pkg <PKG filename>
: ibischk5 -caution -numbered -ami <AMI filename>
The flags prior to the file name can be in any order, and the -caution and/or -numbered flags are optional.

## Slide 5: ibischk5 {–numbered} –ami file4.ami
Checking file4.ami for IBIS 5.0 Compatibility...
ERROR - Illegal Usage value A specified for Param1
ERROR - Illegal Type value B specified for Param1
ERROR - Illegal Format value C specified for Param1
ERROR - No Reserved_Parameters found
Errors : 4
File Failed
Checking file4.ami for IBIS 5.0 Compatibility...
E4627 - Illegal Usage value A specified for Param1
E4627 - Illegal Type value B specified for Param1
E4627 - Illegal Format value C specified for Param1
E4622 - No Reserved_Parameters found
Errors : 4
File Failed

## Slide 6: Parser Classifications –numbered to get message no.
E – Error (violation of a specification rule or serious modeling convention violation)
W – Warning (out of range data or other unexpected model data)
C – Caution (requires caution flag, legal but probably wrong entry)
N – Note (so far, used for non-monotonic tables)
B – Program Bug (an Internal Error that may be related to operating system, memory allocation or ambiguous code branches
U – Unused (message that is no longer available)

## Slide 7: 1200+ Unique Message Strings http://www.eda.org/ibis/ibischk5/ibischk5_messages_draft2.xlsx

## Slide 8: Revised Spread Sheet (based on script conversion from source spread sheet)

## Slide 9: Semi-automated Documentation Steps
Initial spread sheet from parser developer
Modify spread sheet by script
Sort by Symbol (source code modules)
and move entries into sections
Final editing of comments and indexing of message numbers to sections

## Slide 10: Example – Error 102
IBISCHK5 V5.1.3
Checking error_number_example.ibs for IBIS 3.2 Compatibility...
E0102 (line 133) - Orphan Model keyword.
Errors : 1
File Failed
MDL Section Message (see spread sheet)
…
0102 E Orphan Model keyword %filename% %linenum% Model keyword found but not within
a Model declaration
…

## Slide 11: Ongoing Project by Iteration
Process used to correct source spread sheet
Comments expanded (for example, the percent thresholds for Errors and Warnings for V-T matching)
Some related messages will be described (such as different non-monotonic messages)
Some messages will remain incomplete or TBD
Indexing of message numbers to message section and pages planned

## Slide 12: Ibischk5 V5.1.3 release (6 Bugs)
Released March, 2013 (source code and several executables)
Mostly trivial Bugs based on feedback from developers using parser source code
BUG140 dealt with changing non-monotonic Warning to Note shown later
BUG144 dealt with an Internal Error (B) message moved to an Error (E) message (B0122 moved to E0174)

## Slide 13: Real Data from BUG140 and Cadence Presentation
“Golden Parser Non-monotonic Warning’s Investigation” by Yingxin Sun and Joy Li, Cadence Design Systems, November 9, 2012: http://tinyurl.com/byqu7yn
Presented at IBIS Quality Committee November 27, 2012
BUG140: http://www.eda.org/ibis/bugs/ibischk/bug140.txt
(In all test cases, the [Gnd Clamp] data is 0.0 in the region of interest)
Material taken from “Combined I-V Table Checks (BUG140)”, January 31, 2013 IBIS Summit Bob Ross, Yingxin Sun and Joy Li

## Slide 14: BUG140 Issue
Unexpected Non-Monotonic Warnings for Combined I-V Tables (derived from monotonic data)
Combined I-V table checks:
  [Pulldown] + [Gnd Clamp] + [Power Clamp]
  [Pullup] + [Gnd Clamp] + [Power Clamp]
Ibischk5 parser is de facto standard for IBIS model correctness (and ibischk5 is embedded in tools)
Some companies require 0 Errors, 0 Warnings
IBIS Quality Spec, recommends 0 Errors and 0 Warnings
Warning messages create support issue for model authors or automatic modeling utility

## Slide 15: Facts
No specification REQUIREMENT that individual or combined I-V tables be monotonic
No stated method to sum mismatched voltage points (piecewise linear interpolation is allowed and used)
Specification recommends individual I-V table parser checking
Combined checks added with BUG94 (BUG92 dealt with submodels): http://www.eda.org/ibis/bugs/ibischk/
Non-monotonicity often occurs outside of normal simulation region – in clamping region and not a problem
Ibischk5 parser is operating correctly

## Slide 16: Observations
Non-monotonic behavior can occur
  Combined I-V table slope is small
  I-V table points are misaligned due to
    Offset V intervals due to Gnd, Vdd and delta V
    Different reference voltages (min/max)
    Extraction with piecewise linear interpolation calculations (if not done right)
    I-V tables have different V resolution
  Combination of above cases

## Slide 17: Example: x Step 2, Offset by 1 (Red: Interpolated Value)
x y1 y2 y1-y2 = 0?
= x^2 = x^2
0 0
1 2 1 1
2 4 5 -1
3 10 9 1
4 16 17 -1
5 26 25 1
6 36
Non-monotonic due to piecewise linear interpolation on both columns

## Slide 18: x Step 0.02, Offset by 0.01 (Red: Interpolated Value)
x y1 y2 y1-y2
= x^2 = x^2
0.00 0.0000
0.01 0.0002 0.0001 0.0001
0.02 0.0004 0.0005 -0.0001
0.03 0.0010 0.0009 0.0001
0.04 0.0016 0.0017 -0.0001
0.05 0.0026 0.0025 0.0001
0.06 0.0036
Still non-monotonic with higher resolution data

## Slide 19: x Steps 0.02 and 0.01, 0.00 Offset (Red: Interpolated Value)
x y1 y2 y1-y2
= x^2 = x^2
0.00 0.0000 0.0000 0.0000
0.01 0.0002 0.0001 0.0001
0.02 0.0004 0.0004 0.0000
0.03 0.0010 0.0009 0.0001
0.04 0.0016 0.0016 0.0000
0.05 0.0026 0.0025 0.0001
0.06 0.0036 0.0036 0.0000
Different resolution data causes non-monotonic combination

## Slide 20: bug140a.ibs Maximum Data (Vdd = 1.3 V)
1.8 V
1.8 V
Power Clamp
Pulldown

## Slide 23: BUG140 Resolution
Change WARNING to NOTE
  Valid solution for user
  Avoids tool and model developer support issues
Add “based on piecewise linear interpolation” to message
No practical fix
  Still issues with higher resolution or choosing percentage threshold for non-monotonic warning
  Piecewise linear interpolation is legal, and spline fitting would just hide information

## Slide 24: Checking bug140a.ibs
IBISCHK5 V5.1.2
Checking bug140a.ibs for IBIS 3.2 Compatibility...
NOTE (line 39) - Pulldown Typical data is non-monotonic
NOTE (line 42) - Pulldown Minimum data is non-monotonic
NOTE (line 42) - Pulldown Maximum data is non-monotonic
NOTE (line 135) - Pullup Typical data is non-monotonic
NOTE (line 137) - Pullup Maximum data is non-monotonic
NOTE (line 138) - Pullup Minimum data is non-monotonic
WARNING - Combined Pulldown for Model: iobuf Maximum data is non-monotonic
Errors : 0
Warnings: 1
File Passed

## Slide 25: Fixed bug140a.ibs in Version 5.1.3
IBISCHK5 V5.1.3
Checking bug140a.ibs for IBIS 3.2 Compatibility...
NOTE (line 39) - Pulldown Typical data is non-monotonic
NOTE (line 42) - Pulldown Minimum data is non-monotonic
NOTE (line 42) - Pulldown Maximum data is non-monotonic
NOTE (line 135) - Pullup Typical data is non-monotonic
NOTE (line 137) - Pullup Maximum data is non-monotonic
NOTE (line 138) - Pullup Minimum data is non-monotonic
NOTE - Combined Pulldown for Model: iobuf Maximum data is non-monotonic based on piece-wise linear interpolation
Errors : 0
File Passed

## Slide 26: Closure
Parser specification for ibischk5 being produced
For best checking results, use the latest version of ibischk5
Parser being updated as new BUG reports are submitted and processed.