## Slide 1: Ibischk5/6 Specification Document Update
European IBIS Summit
Ghent, Belgium, May 14, 2014
Bob Ross Mike LaBonte
Teraspeed Consulting Group Signal Integrity Software
(SiSoft)
bob@teraspeed.com mikelabonte@eda.org
Presented by Anders Ekholm, Ericsson

## Slide 2: Outline
Ibischk5 specification
  Document update
  Work in progress
Example of Specification page
Current ibischk Release Activity
Conclusions

## Slide 3: Outline of ibischk5 Parser Spec
…
…

## Slide 4: Command Line for ibischk5
–ami for <file_name>.ami (algorithmic model interface control file)
–numbered for numbered Error, Warning, Notes, Caution, and Bug messages
Usage: ibischk5 <IBS filename>
: ibischk5 -ebd <EBD filename>
: ibischk5 -pkg <PKG filename>
: ibischk5 -ami <AMI filename>
Usage: ibischk5 -caution -numbered <IBS filename>
: ibischk5 -caution -numbered -ebd <EBD filename>
: ibischk5 -caution -numbered -pkg <PKG filename>
: ibischk5 -caution -numbered -ami <AMI filename>
The flags prior to the file name can be in any order, and the -caution and/or -numbered flags are optional.

## Slide 5: ibischk5 {–numbered} –ami file4.ami
Checking file4.ami for IBIS 5.0 Compatibility...
ERROR - Illegal Usage value A specified for Param1
ERROR - Illegal Type value B specified for Param1
ERROR - Illegal Format value C specified for Param1
ERROR - No Reserved_Parameters found
Errors : 4
File Failed
Checking file4.ami for IBIS 5.0 Compatibility...
E4627 - Illegal Usage value A specified for Param1
E4627 - Illegal Type value B specified for Param1
E4627 - Illegal Format value C specified for Param1
E4622 - No Reserved_Parameters found
Errors : 4
File Failed

## Slide 6: Parser Classifications –numbered for message numbers
E – Error (violation of a specification rule or serious modeling convention violation)
W – Warning (out of range data or other unexpected model data)
C – Caution (requires caution flag, legal but probably wrong entry)
N – Note (so far, used for non-monotonic tables)
B – Program Bug (an Internal Error that may be related to operating system, memory allocation or ambiguous code branches
U – Unused (message that is no longer available)

## Slide 7: 1200+ Unique Message Strings http://www.eda.org/ibis/ibischk5/ibischk5_messages_draft2.xlsx

## Slide 8: Example – Error 102
IBISCHK5 V5.1.4
Checking error_number_example.ibs for IBIS 3.2 Compatibility...
E0102 (line 133) - Orphan Model keyword.
Errors : 1
File Failed
MDL Section Message (from a converted spread sheet)

## Slide 9: Semi-automated Documentation Steps
Initial spread sheet from parser developer
Modify spread sheet by script
Sort by Symbol (source code modules)
and move entries into sections
Final editing of comments and indexing of message numbers to sections

## Slide 10: Sample Section Page (Based on Converted Spreadsheet)

## Slide 11: Ongoing Project by Iteration
Process used to correct source spread sheet
Comments expanded (for example, the percent thresholds for Errors and Warnings for V-T matching)
Some related messages will be described (such as different non-monotonic messages)
Some comments will remain incomplete or TBD
Indexing of message numbers to sections and planned

## Slide 12: Current ibischk Release Activity
Ibischk5 V5.1.4 released September, 2013 (tables based on this release)
New ibischk6 V6.0.0 expected May, 2014
  New features per IBIS Version 6.0 plus BUG fixes
  A few more messages expected in the parser document specification
  Semi-automated process expected to speed up production of new document

## Slide 13: Closure
Parser specification for ibischk5 being produced
For best checking results, use the latest version of ibischk5 or ibischk6 when available
Parser being updated as new BUG reports are submitted and processed
Work for ibischk6 due soon