## Slide 1
Study of Solving IBIS Single VT
Xuefeng Chen
(xfchen@synopsys.com)
SYNOPSYS
Asian IBIS Summit Meeting
Shanghai, China
November 11, 2008

## Slide 2: Outline
Introduce of VT Solving
Try Two Methods to Solve Single VT
- Method 1: Experiential Way
- Method 2: Impose Constraint
- Comparison of Two Methods
Conclusions

## Slide 3: Outline
Introduce of VT Solving
Try Two Methods to Solve Single VT
- Method 1: Experiential Way
- Method 2: Impose Constraint
- Comparison of Two Methods
Conclusions

## Slide 4: Introduce VT Solving
VT waveforms occur firstly in IBIS2.0
VT waveforms describe transient characteristic of buffer, and be used to solving PU,PD scaling coefficients in pre-simulation computing.
The well known 2EQ/2UK algorithm is for two VT waveforms – one waveform for one linear equation.
Arpad Muranyi: http://www.vhdl.org/pub/ibis/summits/mar06/muranyi1.pdf
Bob Ross: http://www.vhdl.org/pub/ibis/summits/jun03a/ross.pdf
Theoretically, there is no solution for single VT – one linear equation, but two unknowns.

## Slide 5
Introduce of VT Solving
- Recall 2EQ/2UK algorithm
0 = Ku(t) * Iu(Vwfm1(t)) + Ipc(Vwfm1(t)) - Kd(t) * Id(Vwfm1(t)) - Igc(Vwfm1(t)) - Idie(Vwfm1(t))
0 = Ku(t) * Iu(Vwfm2(t)) + Ipc(Vwfm2(t)) - Kd(t) * Id(Vwfm2(t)) - Igc(Vwfm2(t)) - Idie(Vwfm2(t))
Solution of two unknowns : Ku(t) , Kd(t) i.e. scaling coefficients of PU, PD
Where Idie(t) can be obtained by VT waveform and *_fixtures.
(Refer http://www.vhdl.org/pub/ibis/summits/sep07a/chen.pdf )

## Slide 6
Description of Test Example
- For 2EQ/2UK algorithm, VT waveforms with V_fixture = 0v and 1.8v are used
- For Single VT waveform try, the VT waveform with V_fixture=0.9v is used
- In later slides, the same model is used
Model_type I/O
|
Vinl = 0.650V
Vinh = 1.150V
Vmeas = 0.900V
Vref = 0.900V
Cref = 0.000pF
Rref = 25.000Ohm
| typ min max
C_comp 2.911pF 2.841pF 2.984pF
[Voltage Range] 1.800V 1.700V 1.900V
[Temperature Range] 25.0 85.0 0.0
|******************************************************************************
[Pulldown]
…
[Pullup]
…
[GND Clamp]
…
[POWER Clamp]
…
[Ramp]
R_load = 25.000Ohm
| typ min max
dV/dt_r 0.532V/152.000ps 0.441V/172.000ps 0.600V/138.000ps
dV/dt_f 0.532V/328.000ps 0.441V/372.000ps 0.600V/296.000ps
[Rising Waveform]
V_fixture = 0.000V
V_fixture_min = 0.000V
V_fixture_max = 0.000V
R_fixture = 25.000Ohm
L_fixture = 0.000nH
C_fixture = 0.000pF
|
[Rising Waveform]
V_fixture = 0.900V
V_fixture_min = 0.850V
V_fixture_max = 0.950V
R_fixture = 25.000Ohm
L_fixture = 0.000nH
C_fixture = 0.000pF
|
[Rising Waveform]
V_fixture = 1.800V
V_fixture_min = 1.700V
V_fixture_max = 1.900V
R_fixture = 25.000Ohm
L_fixture = 0.000nH
C_fixture = 0.000pF
[Falling Waveform]
V_fixture = 0.000V
V_fixture_min = 0.000V
V_fixture_max = 0.000V
R_fixture = 25.000Ohm
L_fixture = 0.000nH
C_fixture = 0.000pF
|
[Falling Waveform]
V_fixture = 0.900V
V_fixture_min = 0.850V
V_fixture_max = 0.950V
R_fixture = 25.000Ohm
L_fixture = 0.000nH
C_fixture = 0.000pF
|
[Falling Waveform]
V_fixture = 1.800V
V_fixture_min = 1.700V
V_fixture_max = 1.900V
R_fixture = 25.000Ohm
L_fixture = 0.000nH
C_fixture = 0.000pF

## Slide 7: 2EQ/2UK solutions
Basically Ku, Kd swing between 0 and 1
For rising, Kd decreases to 0 earlier than Ku increases to 1;
For falling, Ku decreases to 0 earlier than Kd increases to 1
The time cost of Kd transition for rising(or Ku transition for falling) is about 15% of total time cost
The delay before Kd transition for rising(or Ku transition for falling) ) is about 15% of total time cost
total time cost of rising(low to high)
total time cost of falling(high to low)
time cost of Kd transition
time cost of Ku transition
delay of Kd
delay of Ku
Kd
Ku
Output

## Slide 8: Outline
Introduce of VT Solving
Try Two Methods to Solve Single VT
- Method 1: Experiential Way
- Method 2: Impose Constraint
- Comparison of Two Methods
Conclusions

## Slide 9
For rising:
- construct solution of Kd as simple PWL
- computing Ku by the single VT waveform and Kd
For falling:
- construct solution of Ku as simple PWL
- computing Kd by the single VT waveform and Ku
Note of two key values in PWL - delay and ramp:
- They can be tuned well to get proper percent value of total transition time.
E.g. Both are15% in the test case.
- But It’s hard to apply this fixed value to all IBIS models
delay
ramp
Solution of Kd for rising or Ku for falling
Two Methods to Solve Single VT
- Method 1: Experiential Way

## Slide 10: Solution by Method 1
Kd is constructed for rising
Ku is constructed for falling
Kd
Ku

## Slide 11
Buffer Output by Method 1
- Loaded In Series with R and V (1)
Rload = 25ohm
Vload = 0.9v
Vload = 1.35v
Vload = 0v
Vload = 0.45v
Vload = 1.8v
V(out_2vt) : output by solving two VT waveforms
V(out_1v): output by solving single VT waveform

## Slide 12
Buffer Output by Method 1
- Loaded In Series with R and V (2)
Rload = 5ohm
Vload = 0.9v
Vload = 1.35v
Vload = 0v
Vload = 0.45v
Vload = 1.8v
V(out_2vt) : output by solving two VT waveforms
V(out_1v): output by solving single VT waveform

## Slide 13
Buffer Output by Method 1
- Loaded In Series with R and V (3)
Rload = 45ohm
Vload = 0.9v
Vload = 1.35v
Vload = 0v
Vload = 0.45v
Vload = 1.8v
V(out_2vt) : output by solving two VT waveforms
V(out_1v): output by solving single VT waveform

## Slide 14
A simple constraint is imposed, with formula:
Ku + Kd = 1
Two Methods to Solve Single VT
- Method 2: Impose Constraint

## Slide 15: Solution by Method 2
Ku
Kd

## Slide 16
Buffer Output by Method 2
- Loaded In Series with R and V (1)
Rload = 25ohm
Vload = 0.9v
Vload = 1.35v
Vload = 0v
Vload = 0.45v
Vload = 1.8v
V(out_2vt) : output by solving two VT waveforms
V(out_1v): output by solving single VT waveform

## Slide 17
Buffer Output by Method 2
- Loaded In Series with R and V (2)
Rload = 5ohm
Vload = 0.9v
Vload = 1.35v
Vload = 0v
Vload = 0.45v
Vload = 1.8v
V(out_2vt) : output by solving two VT waveforms
V(out_1v): output by solving single VT waveform

## Slide 18
Buffer Output by Method 2
- Loaded In Series with R and V (3)
Rload = 45ohm
Vload = 0.9v
Vload = 1.35v
Vload = 0v
Vload = 0.45v
Vload = 1.8v
V(out_2vt) : output by solving two VT waveforms
V(out_1v): output by solving single VT waveform

## Slide 19: Comparison of Two Methods
Experiential Way
Impose Constraint
Better accuracy if constructed PWL is tuned well
Hard to find a general well-tuned PWL for all IBIS models
Worse Accuracy especially when loading is far way from R_fixture/V_fixture of VT waveform in model.
It’s a general method and easy to implement
Note:
From testing, more cases show better accuracy with method 1, even with fixed percent values of delay and ramp w.r.t total transition time

## Slide 20: Outline
Introduce of VT Solving
Try Two Methods to Solve Single VT
- Method 1: Experiential Way
- Method 2: Impose Constraint
- Comparison of Two Methods
Conclusions

## Slide 21: Conclusions
It’s not easy to find a general method to get accurate enough solution for all IBIS model with single VT waveform.
For more cases, Method 1(experiential way) with fixed percent of delay and ramp time can get better solution than Method 2(impose constraint)
Maybe we can offer two tuning parameters for model extractor in IBIS model file in order to improve accuracy of Method 1.

## Slide 22
Predictable Success