## Slide 1
AMI Model
in SI Simulation
November 11,2008
Asian IBIS Summit, Shanghai China
Guan Tao
guantao@huawei.com

## Slide 2: Outline
AMI Model in Serial Link Simulation
  Background
  Serial Link Introduction
  Experiencing AMI Simulation
  Highlights and Questions
PLL Model and AMI
  Background
  JTF and PNS

## Slide 3: Background
Generally, the development of serial link SI simulation is left behind the Serdes development.
It is difficult to acquire the chip model for SI simulation. For data rate of 6Gbps＋，Serdes encrypted Hspice Model is not available;
Even with some private simulation tools and models from chip vendors, a high confident result is difficult to get through simulation;
Now, evaluating the serial link system through measurement is normally used;
However only measurement is not enough, and simulation is still an important way;
IBIS 5.0 was ratified at 29th August, 2008, which provides users a good solution for serial link simulation.
IBIS committee makes a great progress on Serdes model and serial link simulation.

## Slide 4: Background
IBIS-AMI Modeling:
Constructing sub-components in transmitter with AMI model;
The channel is characterized with impulse response;
Constructing sub-components in the receivers with AMI model, including CDR;
Providing a process on how to use AMI models.
Transmit Equalizer
Package Interconnect
System Interconnect
Clock
Recovery
Data
Recovery
Serializer
Package Interconnect
Receive Equalizer
TX
RX
Picture reference from “SerDes Modeling and IBIS” at DAC_2007_IBIS_Summit

## Slide 5: Experiencing AMI Simulation
Simulation setup:
IBM AMI model includes 3-tap Tx FFE, 5-tap Rx DFE;
CDR behavior model embedded in RX model;
11.0Gbps data rate and one million bits simulated;
Tx and Rx package models included;
Three different backplane channels used;
Three data patterns: CJPAT, PRBS 7, PRBS 31.

## Slide 6: Experiencing AMI Simulation
Channel descriptions:
Channel 1 : 10.72inch FR4 + 25inch Rogers Backplane + 2 connectors
Channel 2 : 23inch N4000+20inch FR4 + 2 connectors
Channel 3 : 30inch FR4 + 2 connectors
Channel 1
Channel 2
Channel 3

## Slide 7: Experiencing AMI Simulation
AMI Model Introduction:
("hss11_cu08.dml"
(IbisIOCell
(ideal_50term_pulldown
(MacroModel
(MacroType TDiffIO )
(NumberOfTerminals 8 )
(SubCircuits “)
……
(hss11_cu08_rx_dfe
(ami
(ibmhssrx_103_win "E:\IBMSerdes\dll_lib"
(ibis 1 )
(ndfe 5 )
(dfelimit
(0.5 0.25 0.125 0.125 0.125 ) )
(dfe
(0 0 0 0 0 ) )
(rotlin "E:\IBMSerdes\include_files\pr_fast.dat" ) ) )
(hss11_cu08_tx_ffe
(ami
(ibmhsstx_104_win "E:\IBMSerdes\dll_lib"
(ibis 1 )
(nffe 3 )
(rffe 1 )
(cffe 1 )
(qffe 6 )
(lffe
(0.25 1.0 0.5 ) ) ) )
AMI Rx model
AMI Tx model
This is the IBM Serdes AMI model supporting 11Gbps.

## Slide 8: Experiencing AMI Simulation
****Channel Analysis Report******
Tue Sep 02 09:45:44 2008
Channel Inputs:
Bit period = 9.09090909091e-011
No of drivers = 1
No of taps = 1
Tap optimization = No
Stimulus configuration = poly31
Channel coding = No
Char Directory =
E:IBMSerdes/result_channel/char/
Simulation Controls:
No of bits simulated = 1000000
Measurement Delay = 4.4e-005
Eye Measurements:
Eye height = 91 mV
UI at max height = 0.48 UI
Eye jitter = 0.36 UI
BER Report:
logBER UI
-9 0.57
-10 0.56
-11 0.55
-12 0.54
-13 0.53
-14 0.52
-15 0.51
Simulation Input Parameters:
Simulation Type = Time Domain Channel Simulation
Random Jitter = 0.44 %
Periodic Jitter:
Magnitude = 0.05 UI
Freq (cycles per ui) = 0.01
Frequency Offset = 0 ppm
Duty Cycle Distortion = 0 %
Report Sample:
Eye width
under different
bit error ratios
Eye Height

## Slide 9: Experiencing AMI Simulation
Eye Diagram
Bathtub
CJPAT-- blue
PRBS 7-- cyan
PRBS 31– red
Cases of channel 2 and channel 3 are listed in the following page>>>
Channel 1
Channel 1

## Slide 10: Experiencing AMI Simulation
Channel 2
Channel 2
Channel 3
Channel 3

## Slide 11: Experiencing AMI Simulation
Data pattern Channel 2 | Eye Height (mV) | Eye Width (UI)
CJPAT(8B/10B) | 21 | 0.33
PRBS 7 | 45 | 0.58
PRBS 31 | 15 | 0
Data pattern Channel 1 | Eye Height (mV) | Eye Width (UI)
CJPAT(8B/10B) | 100 | 0.59
PRBS 7 | 104 | 0.64
PRBS 31 | 91 | 0.54
Data pattern Channel 3 | Eye Height (mV) | Eye Width (UI)
CJPAT(8B/10B) | 3 | 0.11
PRBS 7 | 41 | 0.71
PRBS 31 | 16 | 0

## Slide 12: Highlights
AMI model includes FFE, DFE and CDR. The model integrity is better. The encrypted Hspice Model always excludes the DFE and CDR.
It is feasible for users to do a large amount of bits simulation, and ISI effect is fully taken into consideration.
Users could set jitter parameters of Tx and Rx, so the jitter of Serdes could be considered..
AMI model support calculating the coefficients of DFE and FFE automatically, and it could shorten the simulation cycle.

## Slide 13: Drawbacks
Modeling method is complicated and no auxiliary tools helping generate the AMI model. Most IC vendors do not supply AMI models.
Users cannot evaluate the simulation results, owing to lack of the mask specification. So it is difficult for users to judge whether the serial link meets the requirement.
It is impossible for users to judge the accuracy of AMI models and to improve it.
Some IC vendors suggest that the simulation is a reference for design and cannot be used for a final decision.
The AMI model, used in the previous example, is a vendor-specific format model, not based on IBIS. The interoperability is not good.
With current AMI model, users couldn’t analyze the contribution of clock jitter and power noise, owing to lack of JTF (jitter transfer function) and PNS (power noise sensitivity).

## Slide 14: Outline
AMI Model in Serial Link Simulation
  Background
  Serial Link Introduction
  Experiencing AMI Simulation
  Highlights and Questions
PLL Model and AMI
  Background
  JTF and PNS

## Slide 15: Background
In the current product, clock jitter and power noise are important contributions of BER;
According to our survey, it is feasible to construct PLL model through measurement;
It is a good solution to add the JTF and PNS into the AMI model, This could improve the integrity of Serdes model.
Users could use the solution to estimate the link jitter contributed by the jitter of reference clock and power noise of the PLL.
Chun xing Huang gives an initial idea on analyzing PLL model in the Serial Link Analysis and PLL Model at Asian IBIS Summit 2007, Beijing. The engineers of Huawei continue a research on constructing the PLL model.

## Slide 16: JTF and PNS
Jitter Transfer Function (JTF) is defined as the ratio of output data jitter and reference clock jitter;
Power Noise Sensitivity (PNS) is defined as the ratio of output data jitter and power noise.
Ref clock
PLL
Tx
Data
Trigger clock
Power Noise
PLL
Tx
Data
Trigger clock
JTF
PNS

## Slide 17: JTF and PNS
Jitter Transfer Function
Power Noise Sensitivity
PLL characteristics are derived by measurement
The measurement environment is the IBM Serdes, supporting 2.0Gbps~3.2Gbps.

## Slide 18: JTF and PNS Application
When jitter transfer function is known, jitter introduced from input clock could be calculated;
Jitter_out(f) = transfunction(f)*jitter_clock_in(f)
When power noise sensitivity is known, jitter introduced from power noise could be calculated:
Jitter_out(f) = powersensitivity(f)*power_noise(f)
According to the description above, users could analyze the output jitter introduced by reference clock jitter and power noise, and optimize the power of PLL.
It is time for us to consider the PLL model in the SI analysis.

## Slide 19: Suggestions
Users will feel more convenient, if AMI model could provide the following features:
Some keywords of eye mask specification, such as eye height and width, which is used to estimate simulation results, should be provided in the AMI model;
Checklist for AMI model is necessary to guarantee AMI model quality.
Adding the jitter transfer function and power noise sensitivity in AMI model