## Slide 1: Optimum Frequency Sampling in S-Parameter Extraction and Simulation
Jinghua Huang
(jhhuang@synopsys.com)
SYNOPSYS
Asian IBIS Submit
Shanghai, China
Nov. 11, 2008

## Slide 2: Agenda
Issues in S-parameter creation (model generation strategies)
Handling bad S-parameters (simulation strategies)
Tools to check S-parameter quality

## Slide 3: Agenda
Issues in S-parameter creation (model generation strategies)
Handling bad S-parameters (simulation strategies)
Tools to check S-parameter quality

## Slide 4: S-parameter creation
Suppliers often ship S-parameter representations of their product (package, connector, amplifier, etc.)
S-parameter models are extracted by test and measurement equipment or by numerical methods (i.e., simulation)
Notes: <number>
Suppliers: either external or internal to the customer site.

## Slide 5: Issues in S-parameter creation
S-parameter “table” model typically shows its weakness when…
  Limited frequency range coverage
  DC point absent
  Coarse sampling
  Unintentional non-passivity
    Especially with bad terminations
  Measurement noise
  etc…
Notes: <number>
Suppliers: either external or internal to the customer site.

## Slide 6: Influence on simulation results
Frequency domain accuracy verification (AC analysis)
  Key point: get required frequency point from provided S-parameter table model using inter-/extrapolation method.
Time domain accuracy verification (Transient analysis)
  Key point: Get time domain impulse response h(t) and do convolution

## Slide 7: Key points in obtaining h(t)
IFFT
  Equally spaced 2^N points needed
  Need to cover wide enough frequency range, from DC to several harmonics of input signal
Rational Function Approximation
  Delay extraction
  Sampling and start pole determination
  Avoid measurement noise
  Accurately obtaining not-given S-parameters from the table model is extremely important to simulation results!

## Slide 8: AC analysis example (sparse vs. dense)
Sparse: narrow range, few samples
  .ac lin 101 1e6 10e9
Dense: wide range, lots of samples
  .ac dec 301 1 30e9
Notes: <number>
.ac lin 101 1e6 10e9: 101 points spread linearly from 1 MHz to 10 GHz.
.ac dec 301 1 30e9: 301 points per decade from 1 Hz to 30 GHz.

## Slide 9: AC verification results: 1 MHz - 60 GHz
.ac lin 101 1e6 10e9
Magnitude vs Frequency (1 MHz - 60 GHz)
.ac dec 301 1 30e9
Max diff = 539 uV
RMS diff = 63 uV
Max diff = 139 uV
RMS diff = 27 uV
Sparse S Model
Dense S Model
Absolute Diff (1 MHz - 10 GHz)
Notes: <number>
AC verification test bench run with default S element settings. OP output nodes for source and s element overlaid as
shown.

## Slide 10: Sparse S Model issues in AC Sparse S Model: 1 MHz - 10 GHz
# Hz S MA R 50.0000
0.100000E+07 0.925839E-02 6.32755 . . .
. . .
0.368301E-03 16.4700 . . .
0.100990E+09 0.354922E-01 60.3283 . . .
0.205661E-02 47.4395 . . .
. . .
0.200980E+09 0.608898E-01 66.5493 . . .
0.314144E-02 46.8725 . . .
1 MHz
101 MHz
Interpolation error
Extrapolation error
The ".ac lin 101 1e6 10e9" generated S model data up to 10 GHz
AC verification test bench specified fstop of 60 GHz
Notes: <number>
CosmosScope calculator and measures shown above.

## Slide 11: Transient response - 3 GHz Pulse
Max diff = 11 mV
RMS diff = 3.4 mV
Max diff = 25.3 mV
RMS diff = 11.5 mV
Sparse S Model
Dense S Model
Transient waveform
Absolute Diff
Notes: <number>

## Slide 12: What does “good” S-parameter look like?
Provide DC point
Covers wide enough frequency range
  From DC to several harmonics of input signal
Necessary dense data point (but not too dense to avoid big data files)
Passive, within the unit circle in Smith Chart
Smooth, without measurement noise
etc…

## Slide 13: Agenda
Issues in S-parameter creation (model generation strategies)
Handling bad S-parameters (simulation strategies)
Tools to check S-parameter quality

## Slide 14: Using bad S-parameters?
S-parameter “table” model typically shows its weakness when…
  Limited frequency range coverage
  DC point absent
  Coarse sampling
  Unintentional non-passivity
    Especially with bad terminations
  Measurement noise
  etc…
Can we use this kind of S-parameters if they are provided?
  Yes, if…
Notes: <number>

## Slide 15: Guessing not-given values
Interpolation & extrapolation
  Piecewise constant
  Piecewise linear
  Spline
  Partially apply rational function approximation
  Hybrid method
  etc…
Base data format
  Real/Imaginary(RI)
  Magnitude/Angle(MA)
  etc…
  Physical modeling (guess) based on provided table model!!

## Slide 16: Interpolation method comparison
Inter-/extrapolation method | Numerical polynomial approximation (Piecewise constant, linear, spline, etc.) | Partially apply rational function approximation | Hybrid method
Advantages | . Quick . Bounded error | . Consider causality . Accurate phase estimation | . Combing advantages of several methods
Disadvantages | . Causality & passivity issue . Phase estimation difficulties | . Time consuming . Passivity violation . Noise sensitive | . False switch between each method . Noise sensitive
Suggestions | Efficient for most common cases | Usually used in hybrid method | Use for cases with local resonances

## Slide 17: Interpolation method comparison
Base data format | Real/Imaginary(RI) | Magnitude/Angle(MA)
Advantages | . No phase over-estimation issue in local resonance region | . Smooth curves connecting given sample points (more physical)
Disadvantages | . May under-estimate phase information . Straight line between given sample points (unphysical) | . May over-estimate phase change in local resonance region
Suggestions | use with very dense table model | Efficient for most cases

## Slide 18: RI v.s. MA (linear) interpolation
Real/Imaginary
  Straight line
Magnitude/Angle
  Circled
  Suitable for linear systems
  Requires unwrapped phase guess
    Clockwise assumption
RI interpolation
MA interpolation

## Slide 19: Local resonances
Turning clockwise locally, looks counter-clockwise globally

## Slide 20: Hybrid interpolation
Combine possible best ways
  Advantage of MA based interpolation
  Capture local resonances
    Finding local centers
    Use rational functions
Conventional MA
Hybrid

## Slide 21: Noise reduction
Data smoothing functions

## Slide 22: Passivity check/enforcement
Passivity violation makes unintentional oscillator
  Voltage blows up
Passivity checker
  Check eigenvalues of I-SS’ (S’: conjugate transpose)
Passivity enforcement
  “modify” original parameters
  Add minimum amount of constant loss
Under construction

## Slide 23: Agenda
Issues in S-parameter creation (model generation strategies)
Handling bad S-parameters (simulation strategies)
Tools to check S-parameter quality

## Slide 24: How to select proper inter-/extrapolation method?
Check your given S-parameter table model on Smith Chart
Determine which method and what data format should to be used for inter-/extrapolation
Check what you get from the selected inter-/extrapolation S-parameter data on Smith Chart

## Slide 25: What does good S-parameter look like?
Good quality S-parameters always show beautiful curves on Smith Chart!
Notes: <number>

## Slide 26
Predictable Success