## Slide 1: Eye Masks in IBIS
Meng, Yubao (yubao@cadence.com)
Cadence Shanghai SPB R&D Center
Asian IBIS Summit,
Shanghai China,
November 11, 2008

## Slide 2: Agenda
Problem – Eye Masks are independent of IBIS models
Proposal – Include Eye Mask data in IBIS models
Examples
Conclusion

## Slide 3: Problem
Eye diagrams can be used to validate clock and data meets:
  Interface standards
  Device specific requirements
Eye masks are not tied to IBIS models today
  They must be manually added to simulation results
  This may delay eye mask checking until late in design flow
IBIS does support voltage threshold, but there is no support of a time domain ‘threshold’

## Slide 4: Proposal
Eye mask data should be included in IBIS files
  Design flows will be improved
Eye mask data can represent either standard requirements (i.e. PCI Express) or device specific eye limits
  IC companies can offer more value and differentiation in their IBIS models

## Slide 5: Eye Masks in IBIS Models Allows integration of device specific time and voltage limits
SerDes Channel Analysis
  Interface standard eye masks can be included in IBIS models for easy checking of interface compliance
  SerDes vendors may want to “advertise” less stringent eye mask requirements in their IBIS models
Common / Source Sync
  The time ‘threshold’ limit can be sum of setup and hold time and other relevant elements
  A device specific eye mask can be located at a time axis that equates to the clock / strobe edge
Notes: ? Time vs. UI proposal

## Slide 6: Example: HDMI SerDes Eye Mask
HDMI eye mask
HDMI TP2 eye mask
Notes: Example of two HDMI (interface standard) masks

## Slide 7: Example: Source Synchronous Signal Eye Mask
Source synchronous signal eye mask are aligned with their strobe signal sampling time
The basic eye mask elements can be setup time, hold time and strobe jitter
Notes: example

## Slide 8: Example: Common Clock Signal Eye Mask
Common clock signal eye mask should be located at time axis according the driver’s clock edge
Notes: example

## Slide 9: Conclusion
Eye masks are commonly used to validate that signals are compliant with standard interface requirements
Including eye mask data in IBIS models will
  Promote earlier use of eye masks in the design process allowing problems to be discovered earlier
  Allow IC vendors to advertise their device-specific less-stringent eye mask requirements
We would like to share our experience and promote this to the IBIS standard

## Slide 10: Thanks