## Slide 1: New Table-based Keywords in IBIS 5.0 A Cookbook-style Guide
Michael Mirmak
Intel Corporation
Chair, IBIS Open Forum
michael.mirmak@intel.com
IBIS Summit
Shanghai, China
November 11, 2008
马梦宽
英特尔公司
IBIS 委员会主席
亚洲 IBIS 技术研讨会
中国上海
2008 年 11 月 11 日

## Slide 2: Legal Disclaimers
THIS DOCUMENT AND RELATED MATERIALS AND INFORMATION ARE PROVIDED "AS IS" WITH NO WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY IMPLIED WARRANTY OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, NON-INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS, OR ANY WARRANTY OTHERWISE ARISING OUT OF ANY PROPOSAL, SPECIFICATION, OR SAMPLE. INTEL ASSUMES NO RESPONSIBILITY FOR ANY ERRORS CONTAINED IN THIS DOCUMENT AND HAS NO LIABILITIES OR OBLIGATIONS FOR ANY DAMAGES ARISING FROM OR IN CONNECTION WITH THE USE OF THIS DOCUMENT.
Performance tests and ratings are measured using specific computer systems and/or components and reflect the approximate performance as measured by those tests. Any difference in system hardware or software design or configuration may affect actual performance.
Intel may make changes to specifications, product descriptions, dates and plans at any time, without notice.
Copyright © 2008, Intel Corporation. All rights reserved.

## Slide 3: IBIS Development
IBIS 3.2#
IBIS 4.0
IBIS 4.1
IBIS 4.2#
IBIS 5.0
# ANSI standard
Links to Verilog-AMS, VHDL-AMS
and Berkeley SPICE files
Differential thresholds, loads
New meas. & delay loads
Golden Waveforms and loads
All IBIS 2.1 features plus
Package modeling
Series devices
Scheduled drivers
Added analog-only support (Verilog-A)
Fixes for standardization
Advanced Modeling Interface (AMI)
Gate modulation support
Current distribution support
2004
1999
2006
2008
2002
Multi-Lingual
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Two New IBIS 5.0 Table-Based Keywords
[ISSO_PD], [ISSO_PU]
  Originally called BIRD97/98
  Characterizes buffer current modulation due to supply variation
    For example, SSO, “droop” or “bounce” events
    Tools today scale the [Pulldown]… I-V tables, which is inappropriate
  Each one a table of current vs. voltage (I-V) data, per corner
[Composite Current]
  Originally called BIRD95
  Characterizes currents from the supply rail through the buffer, as the buffer switches into a known load
  A table of current vs. time (I-t) data, per corner
  Resolves ambiguous rail current distribution from known pad current
    For example, can capture crowbar and/or pre-driver currents
    Tools today “guess” at buffer current distributions
Notes: Both actually help with SSO, in different ways. Together, better than apart

## Slide 5: ISSO_PD
Similar to but different than [Pulldown], which characterizes
output strength with fixed reference
How is it extracted?
PD
PU
Vcc
Short-circuit
effectively
removes
the pullup section
Vtable
Pulldown
section is “on”
(buffer at logical 0)
+
-
Measure the current
as voltage is swept
from –Vcc to Vcc
Results
An I-V table that
characterizes
pulldown strength
as its reference
voltage varies…
I
Notes: Supply rails here could be power reference, ground reference, etc. Note that the specification provides excellent guidance on extraction. Clamp currents must be *excluded.*

## Slide 6: ISSO_PU
Vcc
Similar to but different than [Pullup], which characterizes
output strength with fixed reference
How is it extracted?
PD
PU
Short-circuit
effectively
removes
the pulldown section
Vtable
I
Pullup
section is “on”
(buffer at logical 1)
+
-
Measure the current
as voltage is swept
from –Vcc to Vcc
(relative to Vcc!)
Results
An I-V table that
characterizes
pullup strength
as its reference
voltage varies…
Notes: Supply rails here could be power reference, ground reference, etc. Note that the specification provides excellent guidance on extraction. Clamp currents must be *excluded.*

## Slide 7: ISSO_PD
What does the resulting waveforms look like?
Diode effects should be removed from the
raw data
Simple example: no
pre-driver,
single-stage CMOS
Notes: Note that the current should actually resemble the I-V table for the output, to some degree, for an example this simple.

## Slide 8: ISSO_PD, ISSO_PU - Recommendations
Very similar to traditional I-V tables
Ensure that extraction polarities are correct
  Similar to sweep sources for [Pullup], [Pulldown]
Watch out for clamp currents
  Clamp currents should be excluded from ISSO tables
  This includes on-die termination effects!
Watch out for reference voltages
  [Pullup Reference], [Pulldown Reference], etc. still apply
Beware of what isn’t included
  ISSO keywords describe the final driver stage, not the pre-driver
  The keywords describe static, not dynamic, current modulation

## Slide 9: Composite Current
How is it extracted?
PD
PU
Vcc
I
Predriver
Vfixture
+
-
Rfixture
On-die
decoupling
Classical
IBIS Buffer
Rail
Parasitics

## Slide 10: Composite Current
What does the resulting waveform look like?
Wave shapes will be
similar to [Rising …] and [Falling Waveform] V-t tables
Watch for noise…

## Slide 11: Composite Current - Recommendations
Very similar to traditional V-t tables
but using currents
Supply sufficient data, ideally including…
  Tables using the same load as [Rising…] and [Falling Waveform]
  Tables for no-load conditions (extremely high resistances)
Ensure the data is time-correlated to existing V-t tables
  Must start and end in states and with delays matching associated [Rising Waveform] and [Falling Waveform] tables
Make the power delivery structure is complete and includes…
  Buffer rail inductances and resistances
  Pre-driver structures (if/when connected to the driver rails)
  On-die decoupling structures, at buffer-level scale
Follow the same rules as for V-t tables
  Provide sufficient time-points for smooth transitions
  Use resistive-only loads
Notes: And, as noted earlier, watch for noise and ensure its cause is understood. Be careful with inductive paths! AMS or more generic modeling approaches may cover more.

## Slide 12: Additional Notes
Support
  IBISCHK5 parser should be available in the first half of 2009
  No tools today support these keywords, or automatically extracting data for them
Today’s Options
  SPICE templates can be created to extract the data manually
  Composite Current data can be used with existing models in a SPICE implementation (see References)
  The IBIS 5.0 specification contains guidance on [ISSO_PD], [ISSO_PU] adjustments to how I-V and V-t data interact
Notes: Specification advice on ISSO_PD, ISSO_PU adjustments useful for those creating their own tools.

## Slide 13: Summary
Start collecting data now, and encourage
your model and EDA tool providers
to support these keywords!
[ISSO_PD], [ISSO_PU]
  Characterize buffer supply voltage modulation
  Resembles traditional I-V tables like [Pulldown]
  Can capture gate variation, bounce and droop effects
[Composite Current]
  Characterizes buffer current distribution
  Resembles traditional V-t tables like [Rising Waveform]
  Can reveal and include crowbar current effects
Notes: Comments from tool vendors are invited.

## Slide 14: References
  Official IBIS Website, including tools, articles, specifications
    http://www.eigroup.org/ibis/
  IBIS Specification 5.0
    http://www.eda.org/ibis/ver5.0/
  IBIS Summit presentations
    http://www.eda-stds.org/ibis/summits/index-bydate.htm
    Excellent presentations in 2005 and 2006 cover BIRD 95 and 97/98
  Test Code and Development Documents
    http://www.vhdl.org/pub/ibis/futures/
    http://www.eda.org/ibis/docs/
  The IBIS 4.0 Cookbook – recommended for model creation!
    http://www.eda-stds.org/ibis/cookbook/
  Join the IBIS and IBIS-Users e-mail reflectors!