## Slide 1: Touchstone Version 2.0 Mixed-Mode Syntax
Bob Ross
bob@teraspeed.com
Asian IBIS Summit (China)
Shanghai, China
November 11, 2008

## Slide 2: Outline
Background and Overview
Generalized mixed-mode syntax
(Abbreviations)
  SE: single-ended
  MM: mixed-mode for differential and common modes such as “Sdd11” or “Sdc12”
  GMM: generalized mixed-mode for combination of SE and MM data

## Slide 3: Background
Touchstone issued in 1984 by EEsof (now part of Agilent Technologies)
Touchstone is an OPEN, de-facto format supported by nearly all companies supplying or handling S-parameter data
Older Touchstone “Version 1.0” uploaded as public reference for ICM reference
  http://www.eda.org/ibis/connector/
Touchstone Version 2.0 extended to remove some format limitations and to add some resistance per port flexibility for PDS applications
  http://www.eda.org/pub/ibis/adhoc/interconnect/

## Slide 4: Touchstone Version 2.0 Eight IBIS-like Keywords (so far)
Required keywords
  [Version] 2.0
  [Number of Ports] <n>
  [Two-Port Data Order] {21_12 | 12_21} (for n=2 only)
  [Number of Frequencies] <nf>
Optional keywords
  [Reference] <list of n reference resistances in port order>
  [Matrix Format] {Full | Lower | Upper}
  [Mixed-Mode Order] {Di,j, Ci,j, Si,j entries}
  [Number of Noise Frequencies] <nnf>
Details (except [Mixed-Mode Order]) reported February, 2008
  http://www.eda.org/ibis/summits/feb08/ross1.pdf

## Slide 5: “Version 1.0” Fixed Format Examples (f = frequency, s = data-pair)
S1P f s f s f s f …
S2P f s s s s f s s s s f s s s s f …
S3P f s s s s s s s s s f s s s s s s s s s f …
S4P f s s s s s s s s s s s s s s s s f s s s s s s s s s s s s s s s s f …
S5P f s s s s s s s s s s s s s s s s s s s s s s s s s f …
S6P f s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s f …
Formatting, frequency ordering, and end of file implies number of ports and frequencies values.
Etc …

## Slide 6: Version 1.0 Block Arrangement
Option Line For example, # GHZ S MA R 50
N-port Data Block (rigid format rules)
SE Data
Optional Noise Data Block (n=2 only)

## Slide 7: Version 2.0 Block Arrangement
Option Line and All Keywords (first entry is [Version] 2.0)
N-port Data Block (flexible format, new line only for each frequency)
SE, MM or GMM data
Optional Noise Data Block (n=2 only)

## Slide 8: [Mixed-Mode Order] Keyword
Applies for S, Y, Z n-port matrices
Allows general re-ordering of ports (SE, MM, GMM)
Main document (3 pages) and Appendix A (6+ pages) gives mathematical details
Argument port indices are for new SE ports
  S<k> C<i,j> D<i,j> for single-ended, common mode, and differential mode port numbers (1, …, n)
Argument positions apply to data block

## Slide 9: [Mixed-Mode Order] D1,2 C1,2 S3 (balun, splitter, op. amp. example)
1
2
3
“2”
“1d”
“1c”
SE
GMM
pos entry GMM
D1,2 1,2
C1,2 1,2
S3 3
Sdd1,2 Sdc1,2 Sd1,2;3
Scd1,2 Scc1,2 Sc1,2;3
S3d1,2 S3c1,2 S33
S11 S12 S13
S21 S22 S23
S31 S32 S33
SE port notation in both blocks, position gives mapping
“S” above means n-port entry (S, Y, or Z)
“S” argument means Single-ended
Data Block

## Slide 10: [Mixed-Mode Order] D1,2 C1,2 S3 (with GMM port notation)
1
2
3
“2”
“1d”
“1c”
SE
GMM
pos entry GMM
D1,2 “1”
C1,2 “1”
S3 “2”
Sdd11 Sdc11 Sd12
Scd11 Scc11 Sc12
S2d1 S2c1 “S22”
S11 S12 S13
S21 S22 S23
S31 S32 S33
Typical GMM port notation (“1”,”2”) NOT used
“1”

## Slide 11: [Mixed-Mode Order] D1,2 S3 C1,2 (GMM data with new S3 C1,2 positions)
1
2
3
“2”
“1d”
“1c”
SE
GMM
pos entry GMM
D1,2 “1”
S3 “2”
C1,2 “1”
Sdd11 Sd12 Sdc11
S2d1 “S22” S2c1
Scd11 Sc12 Scc11
S11 S12 S13
S21 S22 S23
S31 S32 S33
GMM data block with different positions “S22” and “Scc11”
Interchange 2 and 3

## Slide 12: [Mixed-Mode Order] D1,3 S2 C1,3 (SE defined with new order)
1
3
2
“2”
“1d”
“1c”
SE
GMM
pos entry GMM
D1,3 “1”
S2 “2”
C1,3 “1”
Sdd11 Sd12 Sdc11
S2d1 “S22” S2c1
Scd11 Sc12 Scc11
S11 S12 S13
S21 S22 S23
S31 S32 S33
Mapping data block to new SE port order

## Slide 13: [Mixed-Mode Order] D1,2 D3,4 C1,2 C3,4 (1,2 and 3,4 port-pairs)
1
2
3
“2d”
“1d”
“1c”
SE
MM
pos entry MM
D1,2 “1”
D3,4 “2”
C1,2 “1”
4 C3,4 “2”
Sdd11 Sdd12 Sdc11 Sdc12
Sdd21 Sdd22 Sdc21 Sdc22
Scd11 Scd12 Scc11 Scc12
Scd21 Scd22 Scc21 Scc22
S11 S12 S13 S14
S21 S22 S23 S24
S31 S32 S33 S34
S41 S42 S43 S44
Diff Port notation by position, numbers for SE ports
“1”
4
“2c”
“2”

## Slide 14: [Mixed-Mode Order] D1,3 D2,4 C1,3 C2,4 (1,3 and 2,4 port-pairs)
1
3
2
“2d”
“1d”
“1c”
SE
MM
pos entry MM
D1,3 “1”
D2,4 “2”
C1,3 “1”
4 C2,4 “2”
Sdd11 Sdd12 Sdc11 Sdc12
Sdd21 Sdd22 Sdc21 Sdc22
Scd11 Scd12 Scc11 Scc12
Scd21 Scd22 Scc21 Scc22
S11 S12 S13 S14
S21 S22 S23 S24
S31 S32 S33 S34
S41 S42 S43 S44
Diff Ports reference same SE positions
“1”
4
“2c”
“2”

## Slide 15: [Mixed-Mode Order] S1 S3 S4 S2 (SE-1 data re-ordered to SE-2)
1
2
3
2
1
4
SE-2
SE-1
pos entry SE-1
1 S1 1
2 S3 3
3 S4 4
4 S2 2
S11 S13 S14 S12
S31 S33 S34 S32
S41 S43 S44 S42
S22 S23 S24 S22
S11 S12 S13 S14
S21 S22 S23 S24
S31 S32 S33 S34
S41 S42 S43 S44
SE-1 uses SE-2 data notation in matrix
4
3

## Slide 16: Closure
Several EDA tools already implementing portions of the mixed-mode syntax
  S, Y, Z parameters for n-ports
  SE, MM, GMM capability
Touchstone 2.0 provides standard, interchangable GMM format when adopted by industry
Minimal changes from Touchstone “1.0” and Touchstone 2.0 for easy bi-directional migration of tools over several years
Some minor changes still being considered