## Slide 1: De-emphasis Buffer Modeling Issues with IBIS
Nanditha Rao
Intel Corporation
nanditha.p.rao@intel.com
Asian IBIS Summit
Tokyo, Japan
November 14, 2008

## Slide 2: Legal Disclaimer
INFORMATION IN THIS DOCUMENT IS PROVIDED IN CONNECTION WITH INTEL® PRODUCTS. NO LICENSE, EXPRESS OR IMPLIED, BY ESTOPPEL OR OTHERWISE, TO ANY INTELLECTUAL PROPERTY RIGHTS IS GRANTED BY THIS DOCUMENT. EXCEPT AS PROVIDED IN INTEL'S TERMS AND CONDITIONS OF SALE FOR SUCH PRODUCTS, INTEL ASSUMES NO LIABILITY WHATSOEVER, AND INTEL DISCLAIMS ANY EXPRESS OR IMPLIED WARRANTY, RELATING TO SALE AND/OR USE OF INTEL PRODUCTS INCLUDING LIABILITY OR WARRANTIES RELATING TO FITNESS FOR A PARTICULAR PURPOSE, MERCHANTABILITY, OR INFRINGEMENT OF ANY PATENT, COPYRIGHT OR OTHER INTELLECTUAL PROPERTY RIGHT.
UNLESS OTHERWISE AGREED IN WRITING BY INTEL, THE INTEL PRODUCTS ARE NOT DESIGNED NOR INTENDED FOR ANY APPLICATION IN WHICH THE FAILURE OF THE INTEL PRODUCT COULD CREATE A SITUATION WHERE PERSONAL INJURY OR DEATH MAY OCCUR.
Intel may make changes to specifications and product descriptions at any time, without notice. Designers must not rely on the absence or characteristics of any features or instructions marked "reserved" or "undefined." Intel reserves these for future definition and shall have no responsibility whatsoever for conflicts or incompatibilities arising from future changes to them. The information here is subject to change without notice. Do not finalize a design with this information.
The products described in this document may contain design defects or errors known as errata which may cause the product to deviate from published specifications. Current characterized errata are available on request.
Intel, and the Intel logo are trademarks of Intel Corporation in the U.S. and other countries.
*Other names and brands may be claimed as the property of others.
Copyright © 2008, Intel Corporation. All rights reserved.

## Slide 3: Agenda
Brief background
  Differential buffer with de-emphasis
  De-emphasis implementation in IBIS
Different de-emphasis implementation
  A different de-emphasis approach
  Boost stimulus derivation
  Example boost stimulus in SPICE
Modeling the “new” boost
  Issues with defining the boost
  Single-ended or differential?
  Verilog* AMS approach
Comments and future work

## Slide 4: Differential Buffer
Single-ended
Differential
PCI Express* differential buffer example
100Ω off die
ON
OFF
DP
DN
PBIAS
NBIAS
PDPM
PDNM
NDPM
NDNM
VCC
OFF
ON
In_p
In_n
VCC/2
55Ω
55Ω
Note: NBIAS and PBIAS are set to get 10mA from the driver

## Slide 5: Differential Buffer with De-emphasis
In_p and In_n are main stimulus patterns Boost_p = In_p Boost_n = In_n
(Main+boost)
Adding a second buffer (de-emphasis/boost)- WIRED-OR
Boost adds to the main during full-swing (101010) operation
Recall M. Mirmak’s
“Issues with C_comp and Differential Multi-stage IBIS Models”
Apr 2004
Main buffer
De-emphasis/ boost buffer
ON
OFF
ON
DP
DN
PBIAS
NBIAS
PDPM
PDNM
NDPM
NDNM
VCC
PBIAS
NBIAS
PDP
PDN
NDN
NDP
DN
DP
ON
ON
In_p
In_n
Boost_p
Boost_n
100Ω off die
OFF
OFF
OFF
VCC/2
55Ω
55Ω

## Slide 6: Differential Buffer with De-emphasis
(Main-boost)
During de-emphasized operation (continuous ones/zeroes), opposite legs of the buffer are switched on (one of the methodologies)
Main buffer
De-emphasis/ boost buffer
ON
OFF
ON
DP
DN
PBIAS
NBIAS
PDPM
PDNM
NDPM
NDNM
VCC
PBIAS
NBIAS
PDP
PDN
NDN
NDP
DN
DP
ON
ON
In_p
In_n
Boost_p
Boost_n
100Ω off die
OFF
OFF
OFF
VCC/2
55Ω
55Ω
Boost_p = In_p
Boost_n = In_n

## Slide 7: De-emphasis Implementation in IBIS
Two differential buffers– main and boost are WIRED-OR
Terminations and parasitics shouldn’t be duplicated
Boost is driven by a stimulus derived from the main pattern depending on the de-emphasis logic
C_comp is split between main and boost in the ratio of number of driver slices (one of the ways)
Boost (t) = Inp (t-1)
Ndp On, pdp Off
BOOST INPUTS
COMBINED OUTPUT
Ndn Off, pdn On
Ndp,pdp
Ndn, pdn
Ndn On, pdn Off
Ndp Off, pdp On
De-emphasis sets in
MAIN INPUTS
1 0 1 1 1 0 1
1 0 1 0 0 0 1
Ndp,pdp
Ndn, pdn

## Slide 8: De-emphasis - Different Approach
During de-emphasized operation, the boost buffer is completely shut off. Load sees only main
You can no-longer tie these inputs together
(Main)
100Ω off die
Main buffer
De-emphasis/ boost buffer
ON
OFF
DP
DN
PBIAS
NBIAS
PDPM
PDNM
NDPM
NDNM
VCC
PBIAS
NBIAS
PDP
PDN
NDN
NDP
DN
DP
ON
In_p
In_n
Boost_p
Boost_n
OFF
OFF
OFF
VCC/2
55Ω
55Ω
OFF
OFF

## Slide 9: Boost Stimulus… Some Derivations
Boost input stimulus will need to be different
Inp 1 0 1 0 1 1 1 1 0 0
Boost_NDP 1 0 1 0 1 0 0 0 0 0
Boost_PDP 1 0 1 0 1 1 1 1 0 1
OFF
OFF
OFF
OFF
OFF
OFF
OFF
OFF
Inp(t-1) | Inp(t) | Boost_NDP | Boost_PDP
0 | 0 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 1 | 0 | 1
Boost_NDP= Inp(t-1) . Inp(t)
Boost_PDP= Inp(t-1) . Inp(t)
Boost_PDP= Boost_PDP
Boost_NDN= Inn(t-1) . Inn(t)
Boost_PDN= Inn(t-1) . Inn(t)
Boost_PDN= Boost_PDN
Similar logic applies for ndn and pdn, except that they will follow Inn

## Slide 10: Example Boost Stimulus in SPICE
*********************** Logic for Boost_NDP*************************
E_inx inpdelay 0 DELAY inp 0 TD='period/2' ****Delay
E_intn in2 0 vol='inV-V(inpdelay)' **Inversion of the delay
**AND inp and in2
Gswitch Boost_NDP inp VCR PWL(1) inp 0 0v,1e-6 vcc,10m
Gswitch1 Boost_NDP in2 VCR PWL(1) in2 0 0v,1e-6 vcc,10m
Rxxx Boost_NDP 0 1E6 *** OUTPUT LOAD
*************************Logic for Boost_PDP*********************
E_inx1 inpdelay1 0 DELAY inp 0 TD='period/2‘ **Delay
E_inn1 inpbar 0 vol='inV-V(inp)‘ **Inversion
Gswitch2 bpbar inpbar VCR PWL(1) inpbar 0 0v,1e-6 vcc,10m
Gswitch3 bpbar inpdelay1 VCR PWL(1) inpdelay1 0 0v,1e-6 vcc,10m
E_boostp Boost_PDP 0 vol='inV-V(bpbar)‘ **Inversion
Rxxx1 Boost_PDP 0 1E6 *** OUTPUT LOAD
Similarly for NDN and PDN

## Slide 11: The ‘Working’ Stimulus
NDP=0 (OFF) during de-emphasis
N follows i/p during normal mode
PDP=1 (OFF) during de-emphasis
P follows i/p during normal mode
In_p
boost_ndp
In_p
boost_pdp
In_n
boost_ndn
In_n
boost_pdn
NDN=0 (OFF) during de-emphasis
N follows i/p during normal mode
PDN=1 (OFF) during de-emphasis
P follows i/p during normal mode

## Slide 12: Modeling the ‘New’ Boost
Approach 1: Define 2 B-elements for main and 1 B-element for each of pdn, pdp,ndp and ndn (modeled as differential buffer)
Transistor
IBIS
Doesn’t work as
Boost == 2 differential buffers
TX+ Pad
TX- Pad
Wired OR
Input
stimulus
pattern
Boost
stimulus
pattern
Inp
pdp
pdn
ndp
ndn
Differential Main buffer
Differential Boost buffer
Inverting
Non- inverting
Inverting
Non- inverting
P
P
N
N
Inverting
Non- inverting
P
N
De-emp logic
Inp

## Slide 13: Modeling the ‘New’ Boost
Approach 2: Define either pdp and pdn or ndp and ndn (modeled as differential buffer)
Transistor
IBIS
TX+ Pad
TX- Pad
Wired OR
Input
stimulus
pattern
Boost
stimulus
pattern
pdp
pdn
De-emp logic
Differential Main buffer
Differential Boost buffer
Inverting
Non- inverting
Inverting
Non- inverting
P
P
N
N
Inp
Inp
  Differential swing correlates well
  Mismatch on de-emphasis transition
  C_comp distribution gets tricky
Recall A.Muranyi’s
“Data Dependent Buffer Characteristics”
Jan 2003

## Slide 14: A Further Issue
Transistor
IBIS
However, single ended signals are incorrect as we ignored ndn and ndp
6-dB De-emphasis
Half the driver is switched off during switch from transition to non-transition ==>Odd behavior in transistor
Table-based IBIS cannot mimic this behavior

## Slide 15: Earlier De-emp Approach
Miscorrelation was not observed with the previous de-emp methodology
Fairly good C_comp distribution
Transistor
IBIS
Current reverses through boost buffer during de-emphasis

## Slide 16: Modeling the ‘New’ Boost
Approach 3:
  Model boost as single-ended buffer instead of differential
  Define 4 B-elements- with pdp, pdn, ndp and ndn stimulus
Transistor
IBIS
Issue with weird single ended signals resolved
But miscorrelation in differential swing!
TX+ Pad
TX- Pad
Wired OR
Input
stimulus
pattern
Boost
stimulus
pattern
pdp
pdn
De-emp logic
ndp
ndn
Differential Main buffer
Boost buffer
Inverting
Non- inverting
Single-ended buffer
P
N
Single-ended buffer
Single-ended buffer
Single-ended buffer
Inp
Inp

## Slide 17: Verilog* AMS Model
Approach 4:
  Create equation based Verilog*-AMS model for the differential buffer
  Shows good correlation
Transistor
Verilog* A

## Slide 18: Comments and Future Work
Different de-emphasis implementations will need different boost stimulus logic
Correlation issues observed while modeling the new de-emphasis buffer using table-based ibis
  Manual fine tuning could fix this, but tedious and not the best approach
Verilog* AMS approach provides good correlation
Alternatives for investigation:
  Driver schedule
  AMS approach