## Slide 1: Using S-Parameters for Accurate Simulation
ANSYS China
Baolong Li
Baolong.li@ansoft.com.cn
Greg Pitner
gpitner@ansoft.com
Asian IBIS Summit Shanghai China Nov4, 2009
Notes: <number>

## Slide 2: Background
S-parameter is becoming more and more popular in high speed simulation
In Howard Johnson’s book, we believe the Fknee is the upper limit of T-Line model
But is it accurate enough for transient analysis in GHz analysis?
Notes: <number>

## Slide 3: Fourier transform
Fourier transform provide mathematical mechanism for transforming frequency data to timing domain
There are two approximations in real application
  Finite band width
  Discrete data point
Notes: <number>

## Slide 4: Finite bandwidth
Finite bandwidth S parameter like a “window” function
Notes: <number>

## Slide 5: Finite bandwidth Problems
“Window” function will cause Oscillation
Notes: <number>

## Slide 6: Finite bandwidth Problems
Increase bandwidth cause sharper oscillation, but never disappear
If expand bandwidth to infinite
Notes: <number>

## Slide 7: Using other “windows”
Hamming
Hanning
Blackman
Welch
Bartlett
Notes: <number>

## Slide 8: Results of other “windows”
Attenuate the spectrum near upper limit
Trade-off between edge and oscillation
Notes: <number>

## Slide 9: Idea step response of different “windows”
Notes: <number>

## Slide 10: Finite edge response of Rectangular “window”
Finite edge response of Rectangular “window”
Rectangular “window” is Non-Causal system
Notes: <number>

## Slide 11: Finite edge response of Rectangular “window”
If increase , will closer to 0
Notes: <number>

## Slide 12: Discrete data point
Simulation is discrete point data both in Timing domain and Frequency domain:
Relationships of step
Minimum timing step is decided by the bandwidth which has been discussed
Notes: <number>

## Slide 13: Timing step influence
1 inch and 3 inch matched T_line’s step response using different timing step:
Only different delay are expected, but different oscillation when bigger timing step
Reduce timing step get correct results
Notes: <number>

## Slide 14: Frequency step influence
Discrete frequency point data convert to timing domain look like repeating series of long pulse.(Discrete Fourier transform)
If frequency step is bigger, the repeating series pulse will interrupt each other
  Same T_line S21 using different frequency step and corresponding transient results
Notes: <number>

## Slide 15: Different requirements of parallel and Serial signal simulation
Parallel signal is repeating of one bit.
  One rising and falling edge
  Frequency step should be denser than 1/T
Serial signal is series of bit.
  Random bits for testing ISI
  Frequency step should be denser than 1/n*UI
Notes: <number>

## Slide 16: conclusion
Mathematical based simulation or testing have native limitation
Serdes GHz simulation need broadband channel characteristic
  Fknee is limited, 5/Tr or 10/Tr
Discrete frequency point data is also critical for analysis
Notes: <number>

## Slide 17
Thank you
谢谢
Notes: <number>