## Slide 1: Huawei's IBIS model quality specification and technology Asian IBIS Summit, Shanghai China November 4, 2009 Lijun Huawei Technologies Co., LTD june_lee@huawei.com

## Slide 2: Overview
Huawei’s model quality process
Golden model specification
Model quality report
IBIS model Correction
Correction methodology
Correction case

## Slide 3: Golden Model Specification
Huawei’s specification:
Huawei follows the IQ Spec, but more detailed;
Actual PCB measurement based correlation;
Model level: Copper model
Silver model
Golden1 model (for signal reflection)
Golden2 model (for timing)
Golden3 model (for SI+PI co-design)
Background:
IBIS model provided by many different chip vendors;
System vendor’s requirement should be considered in IQ spec

## Slide 4: Huawei IBIS Quality report
Part1: Huawei’s model quality checklist
Part2: Waveform comparison
Part3: Electrical Specifications: simulation VS measurement
If passed , Huawei model level will be set as followed:
Copper model
Silver model
Golden1 model (for signal reflect)
Golden2 model (for timing)
Golden3 model (for SI+PI co-design)

## Slide 5: Golden Model Specification
Part1: Huawei’s model quality checklist

## Slide 6: Golden Model Specification
Part2: Waveform comparison: FTS (Fast/typical/slow) simulation VS measurment
Channel S-parameter test
actual PCB measurement VS simulation

## Slide 7: Model Quality report
Part3: Electrical Specifications: simulation VS measurement
FOM:

## Slide 8: Overview
Huawei’s model quality process
Golden model specification
Model validation/quality report
IBIS model Correction
Correction methodology
Correction case

## Slide 9: Background
Once there are some data issues in IBIS model：
Non-monotonic VI table Non-monotonic Vt table
What can we do ?

## Slide 10
Correction Methodology
Topology.：
Driver → Interconnect → Receiver
It’s important to keep consistent with the channel1 and channel2

## Slide 11
（1） PKG correction
PKG and C_comp parameters should match the datasheet
PKG and C_comp model should match the TDR curves
其主导因素：
1) 保持C-comp不变，改变边沿速率（Ramp data）；
2) 保持边沿速率不变，改变C-comp；
Correction Methodology

## Slide 12
（2）VI/VT data table correction
Correction Methodology
VI/VT data is not really accuracy, should be adjusted sometimes;
Rubbish VI/VT data in, rubbish waveform out.

## Slide 13
（3） Macro model Correction
More faster rising edge, more SSN，
Traditional IBIS could not support SSN modeling
Correction Methodology
We add a behavioral current source in IBIS, modeling the SSN.
Would Improve the simulation accuracy

## Slide 14
吻合度参数： 35%  15%  10%  5%
Correction case：
Correction case
The correction technology improved the model quality significantly

## Slide 15
Conclusion
Huawei follows the IQ Spec, but more detailed;
Actual PCB measurement based correlation is significance;
Model correction technology is a good way to improve model quality;
Expect to release IBIS correction technology specification

## Slide 16
References
Official IBIS Website, including tools, articles, specifications
– http://www.eigroup.org/ibis/
iq_ver_2_0.pdf
– http://www.eda.org/pub/ibis/quality_wip/iq_ver_2_0.pdf
IBIS Summit presentations 2007~2008
– http://www.eda-stds.org/ibis/summits/index-bydate.htm
Micron model quality report
– http://www.micron.com/products/partdetail?part=MT18JSF25672AY-1G1
Altera model quality
– http://www.altera.com/literature/wp/signal-integrity_s2-v4.pdf
Mark Alexander Xilinx Corp. 《ssn master circuit》
– http://www.xilinx.com/products/virtex4/pdfs/virtex-4_power_system_performance.pdf