## Slide 1: IBIS Quality Review
Asian IBIS Summit, Tokyo, Japan
November 6, 2009
(Previously presented in China, November 4, 2009)
Anders Ekholm, Ericsson & Mike LaBonte, Cisco Systems
A status review of the IBIS Quality specification

## Slide 2
IBIS Quality Task Group
Web:
  http://www.vhdl.org/pub/ibis/quality_wip
Email list:
  http://www.freelists.org/list/ibis-quality
  Or send email
  To: ibis-quality-request@freelists.org
  Subject: subscribe
Meetings:
  Tuesdays from 11:00am to 12:00pm Eastern Time
Questions? Mike LaBonte milabont@cisco.com

## Slide 3
Brief History
2002 March - Barry Katz started IBIS-Quality
2004 November - IQ 1.0 specification completed
2005 August - Parser bug 90 submitted and approved
2006 March - Parser bug 94 submitted and approved
2006 April - Book “Semiconductor Modeling” discusses IQ
(Roy Leventhal, Lynne Green)
2006 August - IQ 1.1 specification initiated
2009 August - IQ 1.1 renamed IQ 2.0
2009 October - IQ 2.0 approval expected

## Slide 4
Specification Version 1.0
IBIS Quality Levels
  0 Can be checked by IBISCHK, plus a few others
  1 Correctness, completeness, and simulation checks
  2a Simulation correlated
  2b Bench measurement correlated
  3 Simulation and measurement correlated

## Slide 5
Issues with IQ Version 1.0
Passing IQ Level 0 does not sound like much of an accomplishment
  Is a non-compliant file level -1?
There should be a strict level for “Passes IBISCHK”
No other IQ check should duplicate IBISCHK
Can’t have a correlated model without full IQ check
Some checks are weak (“should” vs. “must”)
Feedback from JEITA

## Slide 6
Specification Version 2.0
IBIS Quality Levels
  IQ0 Not Checked
  IQ1 Passes IBISCHK
  IQ2 Suitable for Waveform Simulation
  IQ3 Suitable for Timing Analysis
  IQ4 Suitable for Power Analysis * (defined, but no checks)
Special Designators
  S Simulation correlated
  M Measurement correlated
  X Exceptions
  G Has Golden Waveforms
IQ0
IQ3
IQ2
IQ1
IQ4
M
S
X

## Slide 7
The Only LEVEL 1 Check (IBISCHK)
2.1 {LEVEL 1} IBIS file passes IBISCHK
Checking a123_test.ibs for IBIS 4.1 Compatibility...
ERROR (line 446) - [Receiver Thresholds] should be specified immediately after all the subparameters of a model and before the other keywords of a model except [Model Spec]
ERROR - Model DQ_FULL Receiver Thresholds: Tslew_ac must be specified for single ended receivers
WARNING - Model DQ_HALF Pullup Typical data is non-monotonic
WARNING - Model DQ_HALF Pulldown Minimum data is non-monotonic
WARNING - Model DQ_HALF Pullup Minimum data is non-monotonic
WARNING - Model DQ_HALF Pullup Maximum data is non-monotonic
WARNING - Model DQ_FULL Pullup Typical data is non-monotonic
Errors : 2
Warnings: 5
File Failed

## Slide 8
Example LEVEL 2 Checks (Waveforms)
5.3.7. {LEVEL 2} Combined I-V tables are monotonic
5.3.8. {LEVEL 2} [Pulldown] I-V tables pass through zero/zero
5.3.9. {LEVEL 2} [Pullup] I-V tables pass through zero/zeroI-V
5.3.10. {LEVEL 2} No leakage current in clamp tables
5.3.11. {LEVEL 2} I-V behavior not double-counted

## Slide 9
Example LEVEL 3 Checks (Timing)
3.2.2. {LEVEL 3} [Pin] RLC parasitics are present and reasonable
3.3.1. {LEVEL 3} [Diff Pin] Vdiff and Tdelay_* complete and reasonable
5.2.1. {LEVEL 3} [Model] Vinl and Vinh reasonable
5.2.2. {LEVEL 3} [Model Spec] Vinl and Vinh reasonable

## Slide 10
Level 4 (Power) Checks for future releases
A [Pin Mapping] Complete and Correct check was proposed
Power analysis really needs new features:
  BIRD95 - Power Integrity Analysis using IBIS
  BIRD98 - Gate Modulation Effect (table format)
IBIS 5.0 adoption still in progress
  IBIS 5.1 may be submitted for EIA/ANSI standardization
  IBISCHK 5.0 parser released October 2009
  Have not yet seen IBIS 5.0 power keywords in IBIS files
Level 4 checks are planned for future IQ 2.x

## Slide 11
Notes on IQ Version 2.0
“Possible Errors” section removed
  Some items made into regular checks
“Correlation” section minimized
  Refers to IBIS Accuracy Handbook for details
IC vendor push-back on overshoot parameters
  Not many IBIS files have this
  Buffer developers simply do not measure it
  Difference between functional and destruction limits
  BIRD103 D_overshoot parameters may work better

## Slide 12
IQ Version 2.0 Status
44 draft revisions posted
In review phase for IBIS Open Forum acceptance vote
  Review phase in 3 consecutive Open Forum meetings.
  Acceptance vote scheduled for October 30, 2009.

## Slide 13
After Version 2.0
File parser bug reports
Update the IBIS Accuracy Handbook
  Emphasis on feature-selective correlation
Begin drafting IQ 2.x
  Level 4 power analysis checks

## Slide 14
Regular 2009 IQ Meeting Participants
Cisco Systems
Ericsson
Huawei Technologies
Micron Technology *
Nokia Siemens Networks
Texas Instruments *
Teraspeed Consulting Group *
Xilinx *
* IBIS model makers

## Slide 15: Future IQ expectations
IQ adoption by IC vendors
Adoption by library flow in system companies
IBIS modeling tools implementing the IQ checks