## Slide 1: Recent IBIS Activities
Bob Ross
Asian IBIS Summit
Tokyo, Japan
November 6, 2009
bob@teraspeed.com
(Revised from November 4, 2009 Shanghai, China presentation)

## Slide 2: New IBIS Logo IBIS Under TechAmerica (via mergers)

## Slide 3: New IBIS Officers 2009 - 2010
Chair: Bob Ross, Teraspeed Consulting Group, (past Chair 1996-2001)
Vice-Chair: Lance Wang, IO Methodology
Librarian: Anders Ekholm, Ericsson
Secretary: Randy Wolff, Micron Technology
Webmaster: Syed Huq, Cisco Systems
Postmaster: Mike LaBonte, Cisco Systems
Thank you Michael Mirmak, Intel Corporation for 6 successful years as Chair and host of previous Asian IBIS Summits

## Slide 4: IBIS Active Since 1993
Regular IBIS meetings
  Teleconference/Web meetings every 3 weeks
  Several standards and documents and parsers
IBIS Summits (about 5 per year)
  China, Japan, Europe, and USA (2)
Active task groups with leading experts
  Advanced Technology Modeling - AMI work
  Quality - IBIS Quality Specification
  Interconnect (ad hoc) - Touchstone Spec., ICM
  IBIS Model Review – Free review service

## Slide 5: “ibischk5” Parser Released
Ibischk5, Version 5.0.0 for IBIS Version 5.0
  Free executables: http://www.eda.org/pub/ibis/ibischk5/
  Source code licenses available for purchase
  Supports IBIS Version 5.0 (ratified 2008)
    Algorithmic model interface for Serdes analysis
    Power delivery system SSO and gate modulation
    EMI parameters
    Other – (area based thresholds)
Checks all [IBIS Ver] versions of IBIS files

## Slide 6: New Flags in ibischk5
–ami for <file_name>.ami (algorithmic model interface control file)
–numbered for numbered Error, Warning, Notes and Caution messages
Usage: ibischk5 <IBS filename>
: ibischk5 -ebd <EBD filename>
: ibischk5 -pkg <PKG filename>
: ibischk5 -ami <AMI filename>
Usage: ibischk5 -caution -numbered <IBS filename>
: ibischk5 -caution -numbered -ebd <EBD filename>
: ibischk5 -caution -numbered -pkg <PKG filename>
: ibischk5 -caution -numbered -ami <AMI filename>
The flags prior to the file name can be in any order, and the -caution and/or -numbered flags are optional.

## Slide 7: ibischk5 {–numbered} –ami file4.ami
Checking file4.ami for IBIS 5.0 Compatibility...
ERROR - Illegal Usage value A specified for Param1
ERROR - Illegal Type value B specified for Param1
ERROR - Illegal Format value C specified for Param1
ERROR - No Reserved_Parameters found
Errors : 4
File Failed
Checking file4.ami for IBIS 5.0 Compatibility...
E4627 - Illegal Usage value A specified for Param1
E4627 - Illegal Type value B specified for Param1
E4627 - Illegal Format value C specified for Param1
E4622 - No Reserved_Parameters found
Errors : 4
File Failed

## Slide 8: Released or Current Projects (Some covered in Agenda*)
Touchstone Version 2.0 ratified in April 2009*
  Public Touchstone parser “tschk2” by Agilent Technologies (2010)*
  Future Version 2.1*
IBIS Quality Specification Version 2.0 soon*
Algorithmic model interface improvements
IBIS Interconnect Spice Subcircuit Specification – (IBIS-ISS) with Synopsys approval (2010)
IBIS Version 5.1 maintenance and improvement
IBIS remains active, attracts top talent, and has international participation