## Slide 1: Sparse Matrix Mapping in Future Touchstone 2.1
Bob Ross
Asian IBIS Summit
Tokyo, Japan
November 6, 2009
bob@teraspeed.com
(Originally presented November 4, 2009 in Shanghai, China)

## Slide 2: Topics
Brief Touchstone background through Version 2.0
[Sparse Matrix Mapping] for Touchstone Version 2.1
  Physical symmetry
  Coincidentally identically data
  Extrapolate to more ports based on physical symmetry

## Slide 3: Touchstone Background and Update
Touchstone issued 1984 by EEsof
  Now part of Agilent Technologies
Touchstone “Version 1.0” is widely used
Touchstone Version 2.0 ratified by IBIS April 2009
  Format rules relaxed
  Resistance per port option for PDS
  Mixed mode features for differential setups
  http://www.eda.org/pub/ibis/touchstone_version2.0/
Agilent Technologies contracted to produce tschk2 parser – available soon, free

## Slide 4: Version “1.0” Block Arrangement
Option Line For example, # GHZ S MA R 50
N-port Data Block (rigid format rules)
Officially for Single-Ended Data
Optional Noise Data Block (n=2 only)

## Slide 5: “Version 1.0” Fixed Format Examples (f = frequency, s = data-pair)
S1P f s f s f s f …
S2P f s s s s f s s s s f s s s s f …
S3P f s s s s s s s s s f s s s s s s s s s f …
S4P f s s s s s s s s s s s s s s s s f s s s s s s s s s s s s s s s s f …
S5P f s s s s s s s s s s s s s s s s s s s s s s s s s f …
S6P f s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s s f …
Formatting, frequency ordering, and end of file implies number of ports and frequency values.
Etc …

## Slide 6: Touchstone Version 2.0 Thirteen IBIS-like Keywords -1
Comments – starting with ‘!’
  Start of line or in line until end of line
  Within file or before [Version] or after [End]
  Blank lines permitted
Required keywords (and option line) – fixed order
  [Version] 2.0
  # (option line)
  [Number of Ports] <n>

## Slide 7: Touchstone Version 2.0 Thirteen IBIS-like Keywords -2
Keywords in any order
  [Number of Frequencies] <nf>
    (required)
  [Two-Port Data Order] {21_12 | 12_21}
    (required for n=2 only)
  [Reference] <n reference resistances in port order>
  [Matrix Format] {Full | Lower | Upper}
  [Mixed-Mode Order] {Di,j, Ci,j, Si,j entries}
  [Number of Noise Frequencies] <nnf>
    (required if noise data, n=2 only)
  [Begin Information]/[End Information]
    (block reserved for future use)

## Slide 8: Touchstone Version 2.0 Thirteen IBIS-like Keywords - 3
Data block keywords
  [Network Data]
    (required to begin network data)
  [Noise Data]
    (required if noise data exists)
  [End]
    (required at end of data)

## Slide 9: Version 2.0 Block Arrangement
[Version] 2.0 # Option Line [Number of Ports] <n> plus keywords as needed
[Network Data]
More flexible formatted data
[Noise Data] (optional for n=2 only)
[End]

## Slide 10: Example: PhysicallySymmetrical 2 by 3 Connector for Expansion
1
2
3
4
5
6
7
8
9
10
11
12
Side 1
Side 2
.pkg, .icm format illustrated next

## Slide 11: [Define Package Model] 6-pin LRC(G) from 1 to 6 and Thru Path 1-7
1
2
3
4
5
6
7
8
9
10
11
12
Side 1
Side 2
L-R Thru Path
GND
C-G (& mutual k or L coupling)
Pins for one side of thru path

## Slide 12: 6 pins in [Define Package Model] Sparse_matrix: list of R, L, C …
[Capacitance Matrix] Sparse_matrix
[Row] 1
  1 6pF
  2 -1pF
  3 -1pF
  4 -1pF
  5 -1pF
  6 -1pF
[Row] 2 | etc … through [Row] 6
  2 6pF
  3 -1pF
  Etc.
Common Format for .pkg and .icm for large package (e.g., 500 to 1000 pins)
Upper triangle (forward coupling) of single-frequency LRC(G) elements

## Slide 13: [Sparse Matrix Mapping] Proposed in Version 2.1
Before [Network Data]
  [Number of Sparse Labels] <nl>
  [Sparse Matrix Mapping] {integer-labels, index-pairs}
    After [Matrix Format], if entered
    Each integer-label locates a data-pair that can be mapped into one or more index-pair (row,column) positions in the N-port
Data block keywords
  [Network Data]
    One data-pair column for each integer-label
  [End]
Fewer data-pairs under [Network Data]
  Other keywords have same meaning

## Slide 14: 12-port Coupling (1: to 7:) Physical Symmetry, Unique Coupling
1
2
3
4
5
6
7
8
9
10
11
12
GND
1: 1- GND 2: 1-2 …. 7: 1-7
Side 1
Side 2

## Slide 15: 12-port Coupling (8: to 12:) Physical Symmetry, Unique Coupling
1
2
3
4
5
6
7
8
9
10
11
12
GND
8: 1 – 8 9: 1 – 9 …. 12: 1 - 12

## Slide 16: Integer-label ‘5:’ 16 ‘index-pairs’ to map to (row,column) of N-port
1
2
3
4
5
6
7
8
9
10
11
12
5: (1,5) (5,1) (2,4) (4,2) (2,6) (6,2) (3,5) (5,3) (7,11) (11,7) (8,10) (10,8) (8,12) (12,8) (9,11) (11,9)

## Slide 17: [Matrix Format] {Full | Upper | Lower} (‘index-pairs’)
1
2
3
4
5
6
7
8
9
10
11
12
5: (1,5) (2,4) (2,6) (3,5) (7,11) (8,10) (8,12) (9,11)
(5,1) (4,2) (6,2) (5,3) (11,7) (10,8) (12,8) (11,9)
Full
Lower
Upper

## Slide 18: 2 by 3 Connector with 7 integer -labels and 7 data-pairs per Frequency
….
[Number of Ports] 12 ! Some keywords omitted
[Number of Sparse Labels] 7
[Matrix Format] Upper
[Sparse Matrix Mapping]
1: (1,1) (2,2) (3,3) (4,4) (5,5) (6,6) (7,7) (8,8) (9,9) (10,10) (11,11) (12,12)
2: (1,2) (2,3) (4,5) (5,6) (7,8) (8,9) (10,11) (11,12)
3: (1,3) (4,6) (7,9) (10,12) 4: (1,4) (2,5) (3,6) (7,10) (8,11) (9,12)
5: (1,5) (2,4) (2,6) (3,5) (7,11) (8,10) (8,12) (9,11)
6: (1,6) (3,4) (7,12) (9,10) 7: (1,7) (2,8) (3,9) (4,10) (5,11) (6,12)
[Network Data] ! Frequency and 7 data-pairs in MA format
<f1> <M1 A1> <M2 A2> <M3 A3> <M4 A4> <M5 A5> <M6 A6> <M7 A7>
[End]

## Slide 19: 6 Pin (12 Port) 2 by 3 Connector, Number of index-pairs per integer-label

## Slide 20: 40 Pin (80 Port) 2 by 20 Connector

## Slide 21: 200 Pin (400 Port) 2 by 100 Connector

## Slide 22: Connector: 5 banks of 2 by 20 pins [Matrix Format] Upper, 1: to 7:
456 index-pairs per 40 pin bank
2280 index-pairs for 5 banks
  About 5 pages of auto-generated index-pairs
  Not needed – 13,920 index-pairs for zeroed data-pairs
7 data-pairs, 7 integer-labels for 200 pins, 400 ports
Fewer data-pairs than a full 3-port !!
200 pins, banks of 40 pins each

## Slide 23: Comments
Format details still being discussed
Port numbering shown in example was for simplicity
  Any port ordering can be used
  Some port orders simplify the expansion equations
[Sparse Matrix Mapping] implies pre-processing step to move data into the full N-port
  All other keywords apply to the N-port data
  [Mixed-Mode Order] can also be used to re-order the ports

## Slide 24: Future [Sparse Matrix Mapping]
Small files for large, physically symmetrical packages and connectors
Advantages of N-port parameters
  Many frequencies
  More coupling modes and generality
  One mapping for all frequencies
Supports large packages with N-ports where the IBIS .pkg and .icm format is currently used
For future Touchstone Version 2.1