## Slide 1: PDN design and analysis methodology in SI&PI co-design
Asian IBIS Summit, November 9, 2010, Shenzhen China
Luo Zipeng (luozipeng@huawei.com)
Liu Shuyao (liushuyao@huawei.com)
Notes: <number>

## Slide 2: Agenda
Page <number>
SI&PI co-design challenge
Key parameters in PDN design
Modeling the loop inductance of high frequency capacitor
High frequency capacitor' global decouple effect
Tight coupling Power-Gnd pair in board’ PDN
SSN analysis of PDN’ SI&PI co-design via PDN’ IBIS model

## Slide 3: SI&PI co-design challenge
Page <number>
As signal IO voltage level decreasing and signal speed constantly increasing, the effect of SSN become serious,.
SSN noise directly affect noise margin of low voltage level and time margin of high speed signal.
Traditional independent SI and PI analysis bring the limitation.

## Slide 4: Key parameters in PDN design
Page <number>
Board’ PDN sketch map
Equivalent circuit of board’ PDN
PDN of Board:
VRM
Bulk capacitor
High frequency capacitor
Power-Gnd plane capacitor
Chip’ PDN
High frequency capacitor and Power-Gnd plane play an important role in PDN design;

## Slide 5: Loop inductance of high frequency capacitor
Page <number>
Fanout inductance
Via inductance of high frequency capacitor
Plane spreading inductance
Via inductance of Chip’ Power & Gnd pin

## Slide 6: Via inductance effect in Loop inductance
Page <number>
Capacitor’ ESL: 0.4~0.65nH;
Special fanout inductance: 0.25~0.3nH;
Plane spreading inductance: hundreds of pH;
Via inductance of Capacitor: 1nH~2.5nH,when in different stackup, The Value will be varied

## Slide 7: Modeling the via inductance
Page <number>
Via inductance is about 75%~80% of the total loop inductance;
As the the Power-Gnd pair space and location changed, the via inductance of capacitor may varies;
Optimizing the design of Power-Gnd pair will decrease the via inductance, increase the decouple effect of high frequency capacitor;
Evaluate the value of via inductance by simulation, comparison between simulation and measurement validate the precision of via inductance model.
measurement | Simulation | precision
2.29nH | 2.25nH | 98%

## Slide 8: Comparison of capacitor decouple effect with different via inductance
Page <number>
Power-Gnd plane space | Power-Gnd plane location | Via inductance of Caps | Corresponding line
S≤10mil | Above of the Stackup | 0.3nH＜L＜0.55nH | Red line
10mil＜S＜30mil | Above of the Stackup | 0.55nH＜L＜1.5nH | Orange line
S≤10mil | Center of the Stackup | L≈2.5nH | Green line
10mil＜S＜30mil | Center of the Stackup | 2nH＜L＜2.5nH | Yellow line
30mil＜S＜65mil | Center of the Stackup | 2.3nH＜L＜3nH | Blue line
10mil＜S＜30mil | Underside of the stackup | 3nH≤L | Black line
S≤10mil | Underside of the stackup | 3.2nH＜L | Purple line

## Slide 9: Plane spreading inductance affect high frequency cap decouple
Page <number>
Fanout inductance of cap
Via inductance of Cap
Plane spreading inductance
Designing the PDN of PCB, in order to decrease loop inductance of capacitor, high frequency decoupling capacitor will be located as close as possible to chips‘ power pin;
High frequency decaps usually locate under the chip, close to the power pin;
In actual design, Both chips and decaps need to be located on top side of PCB, for the limitation of chip's dimension, decaps only can be near to the chips, not close to power pin,
as seen as left fig B, plane spreading inductance increase while both chip and decap be located on top side of PCB;
Compared with fig A, the total loop inductance in fig B will increase, and High frequency capacitor’ decouple effect obviously decrease;
A
B

## Slide 10: Global decouple effect of high frequency cap
Page <number>
As decreasing the space between the Power Ground plane, the total loop inductance also decrease, and high frequency caps will show an global decouple effect.

## Slide 11: Power-Gnd pair space more than 30mils,high frequency capacitor show an local effect
Page <number>
Power-Gnd pair space more than 30mils, distance between chip and capacitor varying from 500mils to 1000mils, the resonance frequency and anti-resonance frequency of high frequency capacitor will change.

## Slide 12: Power-Gnd pair space less than 10mils,high frequency capacitor show an global effect
Page <number>
Power-Gnd pair space less than 10mils, distance between chip and capacitor varying from 500mils to 1000mils, the resonance frequency and anti-resonance frequency of high frequency capacitor almost keep same.

## Slide 13: Power-Gnd pair space effect analysis of PDN design
Page <number>
Distance between chip and capacitor keep constant, power-gnd pair space varying from 5.12mils to 56.2mils, the resonance frequency and anti-resonance frequency of high frequency capacitor change.

## Slide 14: Tight coupling Power-Gnd pair in PDN
Page <number>
Power-gnd space 5.12mils,power-gnd pair tightly couple
Power-gnd space 17.52mils

## Slide 15: SSN Mechanism and SI/PI Co-Design Challenges
Page <number>
Page <number>
SSN Mechanisms:
Delta-I Noise and IR Drop from the System PDN（Including Die、Pkg and PCB）
Inductive Coupling from the Whole signal link
SSN Influence :
Decrease the noise margin and timing margin
Increase Power noise and EMI problem
SSN Simulation challenges ：
Multi signal and PDN co-design
Whole PDN and Couping models
Source active models

## Slide 16: PDN Modeling and ibis active
Page <number>
Page <number>
PDN Modeling：Die+Pkg PDN Model and System PDN Model
IBIS for the active model：IBIS buffer has some advantage and limitation for SSN simulation
Coupling Modeling：Pkg Coupling Model and Via Coupling Model

## Slide 17: SSN Simulation using ibis models
Page <number>
Page <number>
Delta-I Noise and Multi Crosstalk
SI+PI Co-simulation using ibis models

## Slide 18: Conclusion
Page <number>
Page <number>
PDN directly determine the board’ power delivery system design quality, and in board’ PDN high frequency capacitor and Power-Gnd plane play an important role;
The loop inductance of high frequency capacitor decrease as smaller as possible in a well designed PDN ,and capacitor show an global decouple effect;
The tight coupling PDN adequately consider power-gnd plane capacitor, expanding the efficiency frequency band;
SSN analysis via PDN’ IBIS model enhance simulation efficiency and speed. Implementing SI&PI co-design.

## Slide 19
Notes: <number>