## Slide 1: IBIS-ISS: What It Is and What It Means to You
Michael Mirmak
Intel Corporation
Chair, IBIS Open Forum
IBIS Summit Taipei
November 12, 2010
馬夢寬
英特爾公司
IBIS 委員會主席
台北 IBIS 技術研討會
2010 年 11 月 12 日
Originally presented in Shenzhen on Nov. 9, 2010

## Slide 2: Legal Disclaimer
Notice: This document contains information on products in the design phase of development. The information here is subject to change without notice. Do not finalize a design with this information. Contact your local Intel sales office or your distributor to obtain the latest specification before placing your product order.
INFORMATION IN THIS DOCUMENT IS PROVIDED IN CONNECTION WITH INTEL® PRODUCTS. EXCEPT AS PROVIDED IN INTEL'S TERMS AND CONDITIONS OF SALE FOR SUCH PRODUCTS, INTEL ASSUMES NO LIABILITY WHATSOEVER, AND INTEL DISCLAIMS ANY EXPRESS OR IMPLIED WARRANTY RELATING TO SALE AND/OR USE OF INTEL PRODUCTS, INCLUDING LIABILITY OR WARRANTIES RELATING TO FITNESS FOR A PARTICULAR PURPOSE, MERCHANTABILITY, OR INFRINGEMENT OF ANY PATENT, COPYRIGHT, OR OTHER INTELLECTUAL PROPERTY RIGHT. Intel products are not intended for use in medical, life saving, or life sustaining applications. Intel may make changes to specifications, product descriptions, and plans at any time, without notice.
All products, dates, and figures are preliminary for planning purposes and are subject to change without notice.
Designers must not rely on the absence or characteristics of any features or instructions marked "reserved" or "undefined." Intel reserves these for future definition and shall have no responsibility whatsoever for conflicts or incompatibilities arising from future changes to them.
The Intel products discussed herein may contain design defects or errors known as errata which may cause the product to deviate from published specifications. Current characterized errata are available on request.
Copies of documents which have an order number and are referenced in this document, or other Intel literature, may be obtained by calling 1-800-548-4725, or by visiting Intel's website at http://www.intel.com.
Intel and the Intel logo are trademarks of Intel Corporation in the U. S. and other countries.
Copyright © 2010, Intel Corporation. All rights reserved.
*Other names and brands may be claimed as the property of others.

## Slide 3: Agenda
The Problem of SPICE* Model Portability
The Concept of IBIS-ISS
What Is and Isn’t Supported
IBIS-ISS and Good SPICE Usage
Status and Future Work
Summary and Call for Action!

## Slide 4: A Standard SPICE* Does Not Exist
What does the following SPICE* statement do?
  Bexample 1 2 I=sin(V(3,0))
Results depend on the SPICE tool you use
  IBIS or non-linear dependent source?
Some elements are not supported or do not share a common meaning in all SPICE variants
  Other non-universal elements include P, W, Y, Z
How do you ensure a model works in your tool or your customers’ tools?

## Slide 5: A Solution for SI/PI Interconnects
SPICE* netlists include interconnects, devices and engine commands
  e.g., .tran analysis for a driver and receiver on a PCB trace
IBIS supports portable device models directly
Engine commands are specific to EDA tools
How to ensure interconnect models are portable?
  Package, via, connector, PCB trace, on-die PDN…
IBIS-ISS: an industry baseline for interconnect modeling in SPICE

## Slide 6: IBIS-ISS in Simple Terms
IBIS-ISS: IBIS Interconnect SPICE* Subcircuits
Defines a limited set of common, basic elements useful for SI interconnect modeling
Based on documents and concepts donated by Synopsys as seen in Synopsys HSPICE*
Developed with SI community through IBIS Interconnect Task Group
  EDA vendors, IC vendors and system vendors

## Slide 7: What Is (and Is Not) Supported
Fundamental circuit elements
  Resistors, Inductors, Capacitors: R, L, K, C
  Dependent Sources: E, F, G, H
  Transmission Lines: T, W (including tabular, Foster, etc.)
  S-parameters: S
Subcircuit definitions and instantiation
  .subckt, .ends, X element
Other basic commands
  .include, .end, .param
… but no engine commands, no active device support, and no field solver

## Slide 8: Usage Model
IBIS-ISS consists entirely of subcircuits and subcircuit definitions
  IBIS-ISS does not define netlists
  Subcircuits may be nested or independent
All parameters are local, and passed explicitly
Multiple files are supported (.include)
Compliant tools simply accept IBIS-ISS files
  Meaning, properly apply IBIS-ISS assumptions within the scope of the top-level subcircuit

## Slide 9: How Does It Work?
.subckt my_trace_group 1 2 3 4 5 6 7 8 ref length=5e-3
* Units are meters
* This is a top-level subcircuit
* The user/system designer will instantiate this circuit in a netlist
Xtrace_a 1 ref 2 ref single_trace local_length=length
Xtrace_b 3 ref 4 ref single_trace local_length=length
Xtrace_c 5 ref 6 ref single_trace local_length=length
Xtrace_d 7 ref 8 ref single_trace local_length=length
* This circuit assumes no crosstalk
.subckt single_trace in local_ref out local_ref local_length=1
Wsingle in local_ref out local_ref N=1 L=‘local_length’
+ TABLEMODEL=‘single_line_table’
.include ‘single_line_table.inc’
* This file defines the tabular data using .MODEL
* This file should also be written using ISS rules
.ends
.ends

## Slide 10: Using SPICE* Correctly
Good SPICE* habits will make IBIS-ISS adoption and use easier
  Pass parameters explicitly and sparingly
  Do not rely on global parameter definitions
  Avoid using global nodes
  Use modular circuit design
  Make node, parameter and element names clear and unique
  Avoid setting engine options in subcircuits
  Avoid ambiguous units and multipliers (e.g., amps vs. atto-)
Practice using IBIS-ISS rules in your circuits today

## Slide 11: Status and Future Work
Draft v0.7 now in review
Once drafts are complete, the document will be provided to the IBIS Open Forum for approval
A parser is under consideration
Documents and background materials on-line:
  http://www.eda.org/ibis/interconnect_wip/
Mailing list available for updates and discussion:
  http://www.freelists.org/list/ibis-interconn/
Questions and comments are welcome!

## Slide 12: Summary
If you model interconnects, IBIS-ISS can help ensure usability across SPICE* tools
If you use SPICE of any kind, IBIS-ISS will be familiar to you
Following principles of good SPICE circuit construction makes IBIS-ISS easy to use
Please study, learn, discuss and comment on the IBIS-ISS draft.
Your contributions are important!