## Slide 1: Correlating C_pin Capacitance with Measurements Asian IBIS Summit Taipei, Taiwan November 12, 2010 (Presented previously at IBIS Summit on November 9, 2010)
Randy Wolff
Micron Technology
rrwolff@micron.com
Notes: <number>

## Slide 2: C_pin
Package capacitance for a specific signal [Pin]
Typically from diagonal elements of the capacitance matrix – extracted from 3D field solvers
Notes: <number>

## Slide 3: Measured Capacitance
Diagonal of matrix is total capacitance seen by each line with all other lines grounded
  Fully-loaded capacitance is useful for single line simulations
Measured capacitance is less than fully-loaded capacitance
  Signal is referenced to power and ground (pwr/gnd decoupled)
  All other signal lines are floating
Notes: <number>

## Slide 4: Why is this important?
C_comp calculation and Model correlation
  C_comp = C_signal(measured) – C_pin(measured)
  C_pin ≠ C_pin(measured)
Datasheet comparisons
  Cspecification is based on measured values, not total capacitance
  Estimating measured values from package simulation data aids in optimizing package designs to meet capacitance specifications
Notes: <number>

## Slide 5: C_pin (measured) vs. Fully-loaded Cap
Measured Pin Cap Setup
(Extracted pin cap after matrix post-processing)
Fully-loaded Cap
(Diagonals of Maxwell’s Matrix)
Other signals Floating
Pin cap
Other Signals Floating
Other signals Floating
Net of interest
Reference net
Reference net
Other signals Grounded
Fully-
loaded Cap
Other Signals Grounded
Other signals Grounded
Net of interest
Reference net
Reference net

## Slide 6: Calculating C_pin(measured)
The matrix form of the capacitance equation is [Q] = [C] * [V]
For a 2x2 system, the C matrix is :
    | Ct1 -C12 |
    | -C12 Ct2 |
Ct1 = C1 + C12 and Ct2 = C2 + C12
Notes: <number>

## Slide 7: Calculating C_pin(measured)
Deposit a charge of Q on Node 1
    | Ct1 -C12 | * | V1 | = | Q |
    | -C12 Ct2 | * | V2 | = | 0 |
Ct1 * V1 – C12 * V2 = Q
-C12 * V1 + Ct2 * V2 = 0, V2 = C12/Ct2 * V1
(Ct1 - C12^2/Ct2) * V1 = Q
Cnode1 = Q/V1 = (Ct1 - C12^2/Ct2)
In matrix form, let Q = 1 coulomb
    | V1 | = Inv (| Ct1 -C12 |) * | 1 |
    | V2 | = Inv (| -C12 Ct2 |) * | 0 |
This yields V1 and V2 and Cnode1 = 1/V1, since Q = 1
Notes: <number>

## Slide 8: Calculating C_pin(measured)
Let Node 2 be grounded - this forces V2 = 0 and allows a net negative charge on Node 2
    | Ct1 -C12 | * | V1 | = | 1 |
    | -C12 Ct2 | * | 0 | = | Q |
1: Ct1 * V1 – C12 * 0 = 1 , V1 = 1/Ct1
2: -C12 * V1 + Ct2 * 0 = Q, Q = - C12/Ct1
The only value of interest is V1, only equation 1 is needed. This is the same as eliminating the 2nd row of the [C] matrix.
V2 = 0, so all of the terms in the 2nd column will multiply to 0. This eliminates the 2nd column of [C].
The matrix equation reduces to | Ct1 | * | V1 | = | 1 |
Notes: <number>

## Slide 9: Calculating C_pin(measured)
Generalized: Let [ C ] be an n+m x n+m matrix representing n floating nodes and m nodes clamped to power or ground.
Step 1 – eliminate the rows and columns associated with clamped nodes.
  [C] -> [C’], where [C’] is an n x n matrix.
  |C’| = |Reduction Matrix2| * |C| * |Reduction Matrix1|
  If net i is clamped then row i of Reduction Matrix1 is all 0s
  If net i is floating then row i of Reduction Matrix1 is all 0s with a 1 in column x
    x = i - # of clamped nets between net 1 and net i
  If net i is clamped then column i of Reduction Matrix2 is all 0s
  If net i is floating then column i of Reduction Matrix2 is all 0s with a 1 in row x
    x = i - # of clamped nets between net 1 and net i
Notes: <number>

## Slide 10: Calculating C_pin(measured)
Step 2 – Generate Q matrix – n x n identity matrix
  Represents a 1 coulomb charge deposited on each floating node, one at a time.
Step 3 – solve for [V] matrix
  [V] = inv([C’]) * [Q], where [Q] is identity matrix
Step 4 – Calculate floating node capacitances
  Cnode(x) = 1/Vxx, where Vxx are the diagonal elements of [V]
Overall effect is mutual capacitances are reduced due to shorting of the mutual terms to power and ground nets
Notes: <number>

## Slide 11: Micron’s Capacitance Analyzer Tool
Excel spreadsheet macro
Reads in matrix data from several Field Solver tools
Solves for ‘measured’ capacitance
Nets are defined as either ‘floating’ or ‘grounded’

## Slide 12: C_pin versus C_pin(measured)
Largest Δ when signal is farthest from powers and grounds

## Slide 13: Conclusions
Capacitance matrix data must be manipulated when comparing it to measured capacitance
  Maxwell capacitance is not what is typically measured
  Important for datasheet comparisons and model to simulation correlation

## Slide 14: Acknowledgements
Thanks to Bruce Schober at Micron for development of the analyzer tool and figuring out the matrix math.

## Slide 15
Notes: <number>