## Slide 1: IBIS Status and Future Direction
Michael Mirmak
Intel Corp.
Chair, IBIS Open Forum
Asian IBIS Summit (Shanghai)
November 15, 2011
马梦宽
英特尔公司
IBIS 委员会主席
亚洲 IBIS 技术研讨会 （中国上海）
2011 年 11 月 15 日

## Slide 2: Agenda
IBIS as Organization and Standard
IBIS 5.0
Touchstone 2.0
IBIS-ISS 1.0
Timeline for Changes
Call to Action

## Slide 3: Specifications and Technologies
IBIS: both an organization and a standard
IBIS – I/O Buffer Information Specification
  Version 5.0 today (includes IBIS-AMI support)
Touchstone 2.0
  Ratified April 2009
  TSCHK2 parser also offered
IBIS-ISS: Interconnect SPICE Subcircuit
  Version 1.0 ratified October 2011

## Slide 4: IBIS Specification Direction
5.1: Clarifications and Style Improvements
  New, more readable format
  Significant changes to IBIS-AMI
    Version control, plus clarifications to clocking, tables, crosstalk
  Support for weak tie-up/tie-down definitions
  Clarifications to [Composite Current]
  Fixes to EBD format
  Fixes to [Test Data] and [Test Load]
5.2: Major features, still under discussion
  Support for repeaters
  Links to IBIS-ISS, Touchstone
  C_comp clarifications

## Slide 5: Touchstone 2.x
Description/format for network parameters
  Primary use in industry is for S-parameters
  2.0 introduces mixed-mode support and per-port impedance
Touchstone 2.1/3.0 Approved Changes
  Sparse Matrix format
  Binary file representation (compression)
Change under discussion
  Support for explicit port-node mapping

## Slide 6: IBIS-ISS 1.0
Interconnect SPICE Subcircuit Specification
Universal SPICE format for interconnects
  Packages, cables, connectors, traces, etc.
Basic SPICE elements supported
  R, L, G, C, some sources
Supports Touchstone, W-element data
  Both frequency and time domains supported
Long-term successor to PKG, EBD, ICM

## Slide 7: Timeline for Changes
IBIS 5.1
  Expecting changes to close by end of 2011
  Draft complete and in approval cycle in Q1’12
Touchstone 2.1
  Q1’12 for approved changes
Touchstone 3.0 & IBIS-ISS 1.0
  Does IBIS-ISS resolve port-node mapping issue?
Key challenge:
smoothly linking all three specifications

## Slide 8: Call to Action
For tool vendors…
  Are you planning to support these improvements?
For system designers
  Can you use these to improve your design margins?
For IC vendors
  Can these help you better specify your devices?
Please become familiar with the
specifications and provide feedback!

## Slide 9: For More Information…
IBIS 5.0
  http://www.eda.org/ibis/ver5.0/
IBIS-ISS 1.0
  http://www.eda.org/ibis/ibis-iss_ver1.0/
Touchstone 2.0
  http://www.eda.org/ibis/touchstone_ver2.0

## Slide 10: Q/A