## Slide 1: IBIS Update and Parsers
 2011 Teraspeed Consulting Group LLC
Bob Ross
Asian IBIS Summit
Yokohama, Japan
November 18, 2011
bob@teraspeed.com

## Slide 2: Presentation Topics
 2011 Teraspeed Consulting Group LLC
Updates
ibischk5
  Operation
  Spread sheet for messages
  Some new checks
tschk2
  Operation
  Messages
Conclusions

## Slide 3: IBIS Home Page (under revision) http://www.eda.org/ibis/
 2011 Teraspeed Consulting Group LLC

## Slide 4: IBIS Organization
 2011 Teraspeed Consulting Group LLC
TechAmerica (www.techamerica.org)
  Top level organization (offices around the world)
  Merger of several standards and trade organizations
  IBIS under SSTC (Standards and Technology Council)
IBIS Officers 2011 - 2012
  Chair: Michael Mirmak, Intel Corporation
  Vice-Chair: Lance Wang, IO Methodology
  Librarian: Anders Ekholm, Ericsson
  Secretary: Randy Wolff, Micron Technology
  Webmaster: Mike LaBonte, SiSoft
  Postmaster: Mike LaBonte, SiSoft
  (Past Chair): Bob Ross, Teraspeed Consulting Group

## Slide 5: Accomplishments and Projects
 2010 Teraspeed Consulting Group LLC
IBIS-ISS (IBIS-Interconnect Spice Subcircuit) Specification
  Version 1.0 released October, 2011
  HSpice subset with Synopsys permission
IBIS Version 5.1 (ongoing current project for 2012)
  IBIS BIRDs (Buffer Issue Resolution Documents)
    Standard IBIS, about 5 BIRDs
    IBIS-AMI (IBIS-Algorithmic Model Interface) cleanup, about 15 BIRDs
  Reformatting into Word document with true graphics
Quality Committee focusing on IBIS-AMI checks to be added to the Quality Specification (ongoing for 2012)

## Slide 6: Current and Future Projects
 2010 Teraspeed Consulting Group LLC
IBIS Version 5.2 (or 6.0) – (future under discussion)
  Analog models
  Jitter parameters
  Multi-lingual links
  Back-channel modeling
  IBIS linkage to IBIS-ISS through [External Model] and [External Circuit]
    Allows using parameterized IBIS-ISS subcircuits
  And more …
Touchstone Version 2.1 (future for 2012)
  Sparse matrix mapping
  Binary format
Ongoing ibischk5 and tschk2 parser maintenance

## Slide 7: “ibischk5” Parser
 2011Teraspeed Consulting Group LLC
Ibischk5, Version 5.0.7
  Free executables: http://www.eda.org/ibis/ibischk5/
  Supports IBIS Version 5.0 (ratified 2008)
    Algorithmic model interface for Serdes analysis
    Power delivery system SSO and gate modulation
    EMI parameters
    Other – (area based thresholds)
Checks all [IBIS Ver]s of IBIS files
  (1.1, 2.1, 3.2, 4.2, 5.0)
Over $114,000 of contracted work since 1993
Supports .ibs, .pkg, .ebd, and .ami formats
  directly or through linkages from top level file

## Slide 8: New Flags in ibischk5
 2011 Teraspeed Consulting Group LLC
–ami for <file_name>.ami (algorithmic model interface control file)
–numbered for numbered Error, Warning, Notes and Caution messages
Usage: ibischk5 <IBS filename>
: ibischk5 -ebd <EBD filename>
: ibischk5 -pkg <PKG filename>
: ibischk5 -ami <AMI filename>
Usage: ibischk5 -caution -numbered <IBS filename>
: ibischk5 -caution -numbered -ebd <EBD filename>
: ibischk5 -caution -numbered -pkg <PKG filename>
: ibischk5 -caution -numbered -ami <AMI filename>
The flags prior to the file name can be in any order, and the -caution and/or -numbered flags are optional.

## Slide 9: ibischk5 {–numbered} –ami file4.ami
 2011Teraspeed Consulting Group LLC
Checking file4.ami for IBIS 5.0 Compatibility...
ERROR - Illegal Usage value A specified for Param1
ERROR - Illegal Type value B specified for Param1
ERROR - Illegal Format value C specified for Param1
ERROR - No Reserved_Parameters found
Errors : 4
File Failed
Checking file4.ami for IBIS 5.0 Compatibility...
E4627 - Illegal Usage value A specified for Param1
E4627 - Illegal Type value B specified for Param1
E4627 - Illegal Format value C specified for Param1
E4622 - No Reserved_Parameters found
Errors : 4
File Failed

## Slide 10: New: Message Number File (1155 unique message strings)
 2011 Teraspeed Consulting Group LLC

## Slide 11: Message Columns (for documentation and sorting)
Number (printed message number)
Symbol in Code (by module grouping)
  Example: ALGMODERR_25 (message 25 of 36 AMI module messages)
Message String (all unique message strings)
Parameters (if applicable for printed % arguments)
  For line numbers, keywords, subparameters, etc.
Comment (brief description)
Category (Error, Warning Notes, Caution, etc.)
Classification (E, W, N, C added for easier sorting)
 2011 Teraspeed Consulting Group LLC

## Slide 12: Recent ibischk5 Fixes
dV of [Ramp] dV/dt_r, dV/dt_f Caution checks
  BUG104, BUG123, BUG130 (case-sensitivity crash)
  Can be used to find the exact dV values based on I-V tables and specified ramp load conditions
  Calculated value reported if wrong value entered
[Model Spec] timing test load entries
  BUG122 for waveform crossing Vmeas test
[ISSO PU] and [ISSO PD] table time entry mismatches
  BUG115, BUG116
  BUG129 time alignment test from Error to Caution
 2011 Teraspeed Consulting Group LLC

## Slide 13: Bug List for Filed BUG Reports http://www.eda.org/ibis/bugs/ibischk/
 2011 Teraspeed Consulting Group LLC

## Slide 14: “tschk2” Parser
 2011 Teraspeed Consulting Group LLC
Checks Touchstone Version 1.0 (TS1) and Version 2.0 (TS2)
  Error and Warning numbers
  Free executables: http://www.eda.org/ibis/tschk2/
Converts TS1 to TS2, TS2 to TS1 where practical with -canonical* flags
Provides comment headers and real, imaginary format (RI) with -describe flag
Source code package includes 440+ test cases
C++, well documented
Thanks to contractor Agilent Technologies

## Slide 15: tschk2 {-canonical*} FILE
 2011 Teraspeed Consulting Group LLC
{-canonical | -canonical-v2}
  TS1, TS2  TS2
  Provides number of ports, frequencies and other information
  Un-normalizes TS1 Y-, Z-, G- and H-parameters and effective noise resistance
{-canonical-v1}
  TS1, TS2  TS1 where practical
  Applies column formatting rules and 2-port 21_12 ordering
  Normalizes TS2 Y-, Z-, G- and H-parameters and effective noise resistance
  No mixed mode or selectable reference resistance processing

## Slide 16: tschk2 {-describe} FILE (header comments, RI format)
 2011 Teraspeed Consulting Group LLC
[Network Data]
! freq S11re S11im S12re S12im S13re S13im S14re S14im
S15re S15im S16re S16im
! S21re S21im S22re S22im S23re S23im S24re S24im
S25re S25im S26re S26im
! S31re S31im S32re S32im S33re S33im S34re S34im
S35re S35im S36re S36im
! S41re S41im S42re S42im S43re S43im S44re S44im
S45re S45im S46re S46im
! S51re S51im S52re S52im S53re S53im S54re S54im
S55re S55im S56re S56im
! S61re S61im S62re S62im S63re S63im S64re S64im
S65re S65im S66re S66im
-0.665574600466 -0.0006609751214130001 0.333068101839 0.000663504688568 0.333100908672 -0.0006633295929
Etc.

## Slide 17: 71 tschk2 Messages
 2011 Teraspeed Consulting Group LLC

## Slide 18: Message Groupings
Message chart in source code package
Message categories (starting number)
  Full Error (1000)
  Format Error (2000)
  Options Error (2100)
  Keyword Order (2200)
  Data Format (2300)
 2011 Teraspeed Consulting Group LLC

## Slide 19: Conclusions
 2011 Teraspeed Consulting Group LLC
ibischk5 and tschk2 parsers - free to officially check files for specification compliance
Parser development also checks specification for accuracy and clarity
BUG process helps maintain integrity of parsers with latest fixes
Parsers are critical to IBIS success

## Slide 20: Useful Links Under IBIS Home Page: www.eda.org/ibis/
 2011 Teraspeed Consulting Group LLC
ver5.0/ IBIS Version 5.0 (August 29, 2008)
ibischk5/ ibischk5 Version 5.0.7 (Pending 2011)
touchstone_ver2.0/ Touchstone Version 2.0 (April 24. 2009)
tschk2/ tschk2 Version 2.0.0 (December 2009)
quality_ver2.0/ IBIS Quality Specification (Oct. 30, 2009)
ibis-iss_ver1.0/ Interconnect SPICE Subcircuit Specification
Version 1.0 (New - October 7, 2011)
editorial_wip/ Editorial Task Group (wip)
interconnect_wip/ Interconnect Task Group (wip) - suspended
macromodel_wip/ Advanced Technology Task Group (wip)
quality_wip/ Quality Task Group (wip)
(wip: work in progress)