## Slide 1: Quality of S-parameter models Asian IBIS Summit, Yokohama, November 18, 2011
Copyright © 2011 by Simberian Inc. Reuse by written permission only. All rights reserved.
Yuriy Shlepnev
shlepnev@simberian.com
Notes: <number>

## Slide 2: Outline
Introduction
S-parameters in frequency and time domains
Constrains on S-parameters in frequency domain
Quality metrics for reciprocity, passivity, causality
Rational approximation and final quality metric
Conclusion
Contacts and resources
<number>
© 2011 Simberian Inc.

## Slide 3: S-parameter models
<number>
S-parameter models are becoming ubiquitous in design of multi-gigabit interconnects
  Connectors, cables, PCBs, packages, backplanes, … ,any LTI-system in general can be characterized with S-parameters from DC to daylight
Electromagnetic analysis or measurements are used to build S-parameter Touchstone models
Very often such models have quality issues:
  Reciprocity violations
  Passivity and causality violations
  Common sense violations
And produce different time-domain and even frequency-domain responses in different solvers!
© 2011 Simberian Inc.
07/29/26
Notes: <number>

## Slide 4: System response computation requires frequency-continuous S-parameters from DC to infinity
<number>
Fourier Transforms
impulse response matrix
stimulus
system response – time domain (TD)
FD
TD
© 2011 Simberian Inc.
scattering matrix
stimulus
system response – frequency domain (FD)
07/29/26
Notes: Integrals in these equations and infinite limits of the integration are the major problem when we are doing time domain computations with tabulated S-parameters defined at a discrete set of frequencies. Even computations in frequency domain are not trivial, because of a channel component models may be discretized differently and S-matrix interpolation is not trivial task.
<number>

## Slide 5: Possible approximations for discrete models
Discrete Fourier Transform (DFT) and convolution
  Slow and may require interpolation and extrapolation of tabulated S-parameters (uncontrollable error)
Approximate discrete S-parameters with rational functions (RMS error)
  Accuracy is under control over the defined frequency band
  Frequency-continuous causal functions defined from DC to infinity with analytical impulse response
  Fast recursive convolution algorithm to compute TD response
  Results consistent in time and frequency domains
Not all Touchstone models are suitable for either approach
07/29/26
© 2011 Simberian Inc.
<number>

## Slide 6: Common S-parameter model defects
<number>
Model bandwidth deficiency
  S-parameter models are band-limited due to limited capabilities of solvers and measurement equipment
  Model should include DC point or allow extrapolation, and high frequencies defined by the signal spectrum
Model discreteness
  Touchstone models are matrix elements at a set of frequencies
  Interpolation or approximation of tabulated matrix elements may be necessary both for time and frequency domain analyses
Model distortions due to
  Measurement or simulation artifacts
  Passivity violations and local “enforcements”
  Causality violations and “enforcements”
Human mistakes of model developers and users
How to estimate and rate quality of the models?
© 2011 Simberian Inc.
07/29/26
Notes: <number>
In general, use of different algorithms in EDA or in-house tools to increase the bandwidth, interpolate data, enforce quality and to do time-domain analysis lead to differences in the responses.

## Slide 7: Causality of LTI system (TD & FD)
The system is causal if and only if all elements of the time-domain impulse response matrix are delayed causality (for interconnects):
This lead to Kramers-Kronig relations in frequency-domain
07/29/26
© 2011 Simberian Inc.
<number>
Kramers, H.A., Nature, v 117, 1926 p. 775..
Kronig, R. de L., J. Opt. Soc. Am. N12, 1926, p 547.
derivation

## Slide 8: Causality estimation - difficult way
Kramers-Kronig relations cannot be directly used to verify causality for the frequency-domain response known over the limited bandwidth at some points
Causality boundaries can be introduced to estimate causality of the tabulated and band-limited data sets
  Milton, G.W., Eyre, D.J. and Mantese, J.V, Finite Frequency Range Kramers Kronig Relations: Bounds on the Dispersion, Phys. Rev. Lett. 79, 1997, p. 3062-3064
  Triverio, P. Grivet-Talocia S., Robust Causality Characterization via Generalized Dispersion Relations, IEEE Trans. on Adv. Packaging, N 3, 2008, p. 579-593.
07/29/26
© 2011 Simberian Inc.
<number>
Even if test passes – a lot of uncertainties due to band limitedness

## Slide 9: Causality estimation - easy way
“Heuristic” causality measure based on the observation that polar plot of a causal system rotates mostly clockwise (suggested by V. Dmitriev-Zdorov)
07/29/26
© 2011 Simberian Inc.
<number>
Plot of Re(S[i,j]) as function of Im(S[i,j]), or polar plot
Start frequency
End frequency
Rotation in complex plane is mostly clockwise around local centers
Re
Im
Causality measure (CM) can be computed as the ratio of clockwise rotation measure to total rotation measure in %.
If this value is below 80%, the parameters are reported as suspect for possible violation of causality.
Algorithm is good for numerical models (to find under-sampling), but no so good for measured data due to noise!
Notes: Exact estimation of causality of a system described with a frequency-domain response within a limited frequency band is not possible in general
Alternative causality measure is Root Mean Square (RMS) Error of a Rational approximation of tabulated data (always causal)
<number>

## Slide 10: Stability and passivity in time-domain
The system is stable if output is bounded for all bounded inputs
A multiport network is passive if energy absorbed by multiport for all possible incident and reflected waves
If the system is passive according to the above definition, it is also causal
Thus, we need to check only the passivity of interconnect system!
07/29/26
© 2011 Simberian Inc.
<number>
P. Triverio S. Grivet-Talocia, M.S. Nakhla, F.G. Canavero, R. Achar, Stability, Causality, and Passivity in Electrical Interconnect Models, IEEE Trans. on Advanced Packaging, vol. 30. 2007, N4, p. 795-808.
(BIBO)
(does not generate energy)

## Slide 11: Passivity in frequency domain
Power transmitted to multiport is a difference of power transmitted by incident and reflected waves: or
Quadratic form is non-negative if eigenvalues of the matrix are non-negative:
07/29/26
© 2011 Simberian Inc.
<number>
(U is unit matrix)
Sufficient condition only if verified from DC to infinity (impossible for discrete Touchstone models)

## Slide 12: Good Touchstone models of interconnects
Must have sufficient bandwidth matching signal spectrum
Must be appropriately sampled to resolve all resonances
Must be reciprocal (linear reciprocal materials used in PCBs)
Must be passive (do not generate energy)
Have causal step or impulse response (response only after the excitation)
07/29/26
© 2011 Simberian Inc.
<number>
from DC to infinity!

## Slide 13: Quality metrics (0-100%) to define goodness
Passivity Quality Measure:
Reciprocity Quality Measure:
Causality Quality Measure: Minimal ratio of clockwise rotation measure to total rotation measure in % (should be >80% for numerical models)
07/29/26
© 2011 Simberian Inc.
<number>
should be >99%
should be >99%
First introduced at IBIS forum at DesignCon 2010

## Slide 14: Preliminary quality estimation metrics
Preliminary Touchstone model quality can be estimated with Passivity, Reciprocity and Causality quality metrics (PQM, RQM, CQM)
07/29/26
© 2011 Simberian Inc.
<number>

## Slide 15: Example of preliminary quality estimation
07/29/26
© 2011 Simberian Inc.
<number>
Small passivity & reciprocity violations in most of the models
Low causality in some measured data due to noise at high frequencies

## Slide 16: Rational approximation of S-parameters as the frequency-continuous model
Pulse response is analytical, real and delay-causal:
Stable
Passive if
Reciprocal if
<number>
May require enforcement
Continuous functions of frequency defined from DC to infinity
© 2011 Simberian Inc.
07/29/26
Notes: Rational approximation is particularly suitable for S-parameters. S-parameters of any LTI system can be approximated with the rational functions over a limited frequency band. There is a form of rational approximation with multiple delays.
<number>

## Slide 17: Rational approximation can be used to
Compute time-domain response of a channel with a fast recursive convolution algorithm (exact solution for PWL signals)
Improve quality of tabulated Touchstone models
  Fix minor passivity and causality violations
  Interpolate and extrapolate with guarantied passivity
Produce broad-band SPICE macro-models
  Smaller model size, stable analysis
  Consistent frequency and time domain analyses in any solver
Measure the original model quality
07/29/26
© 2011 Simberian Inc.
<number>

## Slide 18: Final quality estimation
Accuracy of discrete S-parameters approximation with frequency-continuous macro-model, passive from DC to infinity
Can be used to estimate quality of the original data
07/29/26
© 2011 Simberian Inc.
<number>

## Slide 19: Example of final quality estimation
07/29/26
© 2011 Simberian Inc.
<number>
All rational macro-models are passive, reciprocal, causal and have acceptable accuracy (acceptable quality of original models)
Improved tabulated models (re-sampled)

## Slide 20: Conclusion: How to avoid problems with S-parameter models?
Use reciprocity, passivity and causality metrics for preliminary analysis
  RQM and PQM metrics should be > 99% (acceptable level)
  CQM should be > 80% for all causal numerical models
Use the rational model accuracy as the final quality measure
  QM should be > 90% (acceptable level)
Discard the model with low RQM, PQM and QM metrics!
  The main reason is we do not know what it should be
Models that pass the quality metrics may still be not usable or mishandled by a system simulator
  Due to band-limitedness, discreteness and brut force model fixing
Use rational or BB SPICE macro-models instead of Touchstone models for consistent time and frequency domain analyses
<number>
© 2011 Simberian Inc.
07/29/26

## Slide 21: Contact and resources
Yuriy Shlepnev, Simberian Inc.
  shlepnev@simberian.com
  Tel: 206-409-2368
To learn more on S-parameters quality see the following presentations (also available on request):
  Y. Shlepnev, Quality Metrics for S-parameter Models, DesignCon 2010 IBIS Summit, Santa Clara, February 4, 2010
  H. Barnes, Y. Shlepnev, J. Nadolny, T. Dagostino, S. McMorrow, Quality of High Frequency Measurements: Practical Examples, Theoretical Foundations, and Successful Techniques that Work Past the 40GHz Realm, DesignCon 2010, Santa Clara, February 1, 2010.
  E. Bogatin, B. Kirk, M. Jenkins, Y. Shlepnev, M. Steinberger, How to Avoid Butchering S-Parameters, DesignCon 2011
  Y. Shlepnev, Reflections on S-parameter quality, DesignCon 2011 IBIS Summit, Santa Clara, February 3, 2011
07/29/26
© 2011 Simberian Inc.
<number>