## Slide 1: Power Aware Features of IBISv5.0 – Accuracy and Challenges
Vipul Pursottam Patel
Prabhat Ranjan
Richa Ahuja
- ST Microelectronics
Asian IBIS Summit
Taipei, Taiwan
November 21, 2011

## Slide 2: Agenda
Introduction
BIRD98 [ISSO PU] / [ISSO PD]
BIRD95 [Composite Current]
Accuracy Enhancements
Challenges

## Slide 3: Introduction
For Improved SSO simulations in non-ideal power supply environment IBIS ver.5.0 introduced the following features :
  Added [ISSO PU] & [ISSO PD] tables proposed in BIRD98.
    - To model Gate Modulation effect.
  Added [Composite Current] tables proposed in BIRD95.
    - For more accurate analysis for ground and power bounce associated with
    simultaneous switching noise.

## Slide 4: BIRD98 [ISSO PU] / [ISSO PD]
Due to SSO noise, the actual drive strength may vary during transients depending on the instantaneous value of the supply voltage.
  - This phenomena is usually called the “Gate Modulation Effect“
  [ISSO PU] / [ISSO PD] define the effective current of the pullup/pulldown structures as a function of the voltage on the pullup/pulldown reference nodes.
In IBIS (prior to IBISv5) Working point can move only
along the same Vgs =VDD characteristic.
- During supply bounce, actual working point shifts to
Vgs = VDD ± ΔVbounce characteristics.
Higher is the bouncing noise, the higher is the mismatching
between IBIS and Spice results.

## Slide 5: BIRD95 [Composite Current]
Describes Rising and Falling edge total current from the Power Reference terminal of the buffer.
The current causing the Supply bounce will include :
  I_byp - Bypass current
  I_pre - Pre-Driver current
  I_cb - Crow-bar current
  I_term - Termination current (if Present)
  I_byp & I_pre play a significant role in determining the supply bounce.
  Not modeled by IBIS ver. Prior to 5.0
I_total = “I_byp” + “I_pre” + “I_cb” + “I_term”
([Composite Current])
*Image taken from IBIS 5.0 Specification document.

## Slide 6: [Composite Current] Sample data
50 Ohm Resistive load at PAD to Pull Down Reference
Voltage
Current
Voltage
Current
Time (ns)
Time (ns)
50 Ohm Resistive load at PAD to Pull Up Reference
Rising event only

## Slide 7: [Composite Current] Observation 1
  “The currents documented in the I-T table correspond to the voltages in the V-T table at the identical time points and for the given *_fixture load." *
    - The best data points for a specific V-T table will not be
    the same best points for corresponding I-T table .
    - Generation tools can miss Important information in I-T
    data.
      Pre-driver current peaks occur in the
      region of initial constant voltage.
*Text taken from IBIS 5.0 Specification document.

## Slide 8: [Composite Current] Observation 2
- If Initial dead time removed from V-T tables , I-T waveforms
also need to be adjusted similarly.
- Pre-driver current information will be lost.
- [Composite Current] information cannot be effectively used.
- Model developers need to support 2 Separate Models, one
with dead time removed and other without removal.
  This constraint (I-T data time-correlated with V-T data) need to be removed to accurately model the V-T Waveforms and I-T waveform. (“BIRD 141”)
  For High Speed buffers, Some simulators require removal of Initial dead time (if greater than half bit period of the driving signal), to avoid overclocking.

## Slide 9: [Composite Current] Observation 3
  No info regarding Pull Down reference terminal current in IBIS models !!
  - Simulators can only assume Pull Down terminal current equal to Pull Up
  reference current ?
  - Accuracy of Power Down terminal current simulations reduced.
  - May impact SSN number estimation.

## Slide 10
Accuracy Enhancements

## Slide 11: Simulation Setup
  Comparison of power/ground supply node current and voltage for IBIS 4.2 and IBIS 5.0 model with Reference Spice model in SSO simulation.
PKG
R=0.2 Ω
L= 8.0nH
C=1.0pF
1
0
1
0
I(VDD)
I(GND)
V(VDD)
V(GND)
Probe Point
Decoupling Capacitance
  Corner : Max.
  Frequency : 50MHz
  Far End Capacitive Load: 25pF
  Decoupling Capacitance between Supply and ground of each Buffer: 4pF
Zo = 50 Ω
PKG
PKG
PKG
PKG
PKG
Zo = 50 Ω
Zo = 50 Ω
GND
VDD
1
0

## Slide 12: Result 1 : I(VDD)/V(GND) SPICE-IBISv4.2-IBISv5.0
Improved matching
In Power supply current
Simulation.
Improved matching
In Supply bounce
Simulation
Accuracy Enhanced of IBIS Models
With :
[Composite Current],
[ISSO PU],
[ISSO PD].
* From SPICE simulation

## Slide 13: Result 2 : I(VDD)/V(GND) SPICE-IBISv5.0 (with & without decoupling capacitance)
Improved matching with de-cap added to spice model in Power supply current Simulation.
Improved matching with de-cap added to spice model in Ground bounce Simulation.
No method to specify
‘individual buffers internal De-coupling capacitance’ between its supply nodes in IBIS syntax.
* From SPICE simulation

## Slide 14: Challenges
  [Composite Current] time-correlation with V-T waveforms can lead to loss of important pre-driver current info in overclocking and non-overclocking models. This constraint need to be removed.
  No method to specify ‘individual buffers internal De-coupling capacitance’ between its supply nodes in IBIS syntax
  - Can specify On-die decoupling capacitance between pins using Series Model at component
  level.
  - As a model supplier, Internal de-coupling capacitance is required during validations as well as
  to pass on this info to customers for simulations at their end.

## Slide 15
THANK YOU