## Slide 1: Combined I-V Table Checking Problem
Asian IBIS Summit
Shanghai, China, November 15, 2013
Bob Ross Yingxin Sun and Joy Li
Teraspeed Consulting Group Cadence Design Systems
bob@teraspeed.com sunyx@cadence .com
joyli@cadence.com
Presented by Anders Ekholm, Ericsson

## Slide 2: Real Data from BUG140 and Cadence Presentations
BUG140: http://www.eda.org/ibis/bugs/ibischk/bug140.txt
(In all test cases, the [Gnd Clamp] data is 0.0 in the region of interest)
Presentations
  “Golden Parser Non-monotonic Warning’s Investigation” by Yingxin Sun and Joy Li, November 9, 2012: http://tinyurl.com/byqu7yn (Presented at the IBIS Quality Committee November 27, 2012)
  “Combined I-V Table Checks (BUG140)”, January 31, 2013 IBIS Summit, Bob Ross, Yingxin Sun, and Joy Li
  “Ibischk5 Specification and Parser”, May 15, 2013 IBIS Summit, Bob Ross and Mike LaBonte (Signal Integrity Software)

## Slide 3: BUG140 Issue
Unexpected Non-Monotonic Warnings for Combined I-V Tables (derived from monotonic data)
Combined I-V table checks:
  [Pulldown] + [Gnd Clamp] + [Power Clamp]
  [Pullup] + [Gnd Clamp] + [Power Clamp]
Ibischk5 parser is de facto standard for IBIS model correctness (and ibischk5 is embedded in tools)
Some companies require 0 Errors, 0 Warnings
IBIS Quality Spec, recommends 0 Errors and 0 Warnings
Warning messages create support issue for model authors or automatic modeling utilities

## Slide 4: Facts
No specification REQUIREMENT that individual or combined I-V tables be monotonic
No stated method to sum mismatched voltage points (piecewise linear interpolation is allowed and used)
Non-monotonicity often occurs outside of normal simulation region – in clamping region and not a problem
Ibischk5 parser is working correctly

## Slide 5: Observations
Non-monotonic behavior can occur
  Combined I-V table slope is small
  I-V table points are misaligned due to
    Offset V intervals due to Gnd, Vdd and delta V
    Different reference voltages (min/max)
    Extraction done with piecewise linear interpolation calculations (if not done right)
  Combination of above cases
Example (y = x^2) next shows monotonic tables yielding non-monotonic summations

## Slide 6: Example: x Step 2, Offset by 1 (Red: Interpolated Value)
x y1 y2 y1-y2 = 0?
= x^2 = x^2
0 0
1 2 1 1
2 4 5 -1
3 10 9 1
4 16 17 -1
5 26 25 1
6 36
Non-monotonic due to piecewise linear interpolation on both columns

## Slide 7: x Step 0.02, Offset by 0.01 (Red: Interpolated Value)
x y1 y2 y1-y2
= x^2 = x^2
0.00 0.0000
0.01 0.0002 0.0001 0.0001
0.02 0.0004 0.0005 -0.0001
0.03 0.0010 0.0009 0.0001
0.04 0.0016 0.0017 -0.0001
0.05 0.0026 0.0025 0.0001
0.06 0.0036
Still non-monotonic with higher resolution data

## Slide 8: x Steps 0.02 and 0.01, 0.00 Offset (Red: Interpolated Value)
x y1 y2 y1-y2
= x^2 = x^2
0.00 0.0000 0.0000 0.0000
0.01 0.0002 0.0001 0.0001
0.02 0.0004 0.0004 0.0000
0.03 0.0010 0.0009 0.0001
0.04 0.0016 0.0016 0.0000
0.05 0.0026 0.0025 0.0001
0.06 0.0036 0.0036 0.0000
Different resolution data causes non-monotonic combination

## Slide 9: bug140a.ibs Maximum Data (Vdd = 1.3 V)
1.8 V
1.8 V
Power Clamp
Pulldown

## Slide 12: BUG140 Resolution
Change WARNING to NOTE
  Valid solution for user
  Avoids tool and model developer support issues
Add “based on piecewise linear interpolation” to message
No practical fix
  Still issues with higher resolution or choosing percentage threshold for non-monotonic warning
  Piecewise linear interpolation is legal, and spline fitting would just hide information

## Slide 13: Checking bug140a.ibs
IBISCHK5 V5.1.2
Checking bug140a.ibs for IBIS 3.2 Compatibility...
NOTE (line 39) - Pulldown Typical data is non-monotonic
NOTE (line 42) - Pulldown Minimum data is non-monotonic
NOTE (line 42) - Pulldown Maximum data is non-monotonic
NOTE (line 135) - Pullup Typical data is non-monotonic
NOTE (line 137) - Pullup Maximum data is non-monotonic
NOTE (line 138) - Pullup Minimum data is non-monotonic
WARNING - Combined Pulldown for Model: iobuf Maximum data is non-monotonic
Errors : 0
Warnings: 1
File Passed

## Slide 14: Fixed bug140a.ibs in Version 5.1.3
IBISCHK5 V5.1.3
Checking bug140a.ibs for IBIS 3.2 Compatibility...
NOTE (line 39) - Pulldown Typical data is non-monotonic
NOTE (line 42) - Pulldown Minimum data is non-monotonic
NOTE (line 42) - Pulldown Maximum data is non-monotonic
NOTE (line 135) - Pullup Typical data is non-monotonic
NOTE (line 137) - Pullup Maximum data is non-monotonic
NOTE (line 138) - Pullup Minimum data is non-monotonic
NOTE - Combined Pulldown for Model: iobuf Maximum data is non-monotonic based on piece-wise linear interpolation
Errors : 0
File Passed

## Slide 15: Closure
For best checking results, use the latest version of ibischk5
Parser being updated as new BUG reports are submitted and processed.