## Slide 1: Introducing IBIS 6.0
Michael Mirmak
Intel Corp.
Chair, IBIS Open Forum
Asian IBIS Summit
Yokohama, Japan
November 22, 2013
http://www.eda.org/ibis/

## Slide 2: Agenda
IBIS 6.0 in Summary
  Key Features
  Changes from IBIS 5.1
What problems does 6.0 address?
Issues to Resolve
What’s Next?
Questions

## Slide 3: Key Features of IBIS 6.0
IBIS 6.0 was approved September 20, 2013
  http://www.eda.org/ibis/ver6.0/
Major additions focus on IBIS-AMI
  Adds redriver and retimer support
  Expands jitter/noise parameters
  Clarifies analog buffer impedance descriptions
  Supports IBIS-ISS (Interconnect SPICE Subcircuits) and Touchstone 1.x/2.0

## Slide 4: Other Changes from IBIS 5.1
Clarifications of A/D and D/A converters in [External Model] and [External Circuit]
  Parameter passing now supported!
Additional files supported for IBIS-AMI
  Including explicit paths
  Identifiers for individual IBIS-AMI model instances
List Tips for IBIS-AMI Lists
  Associates labels with parameter lists
Improved organization of the document
  Easier to read and use

## Slide 5: IBIS 6.0 Support Examples
How do I model a mid-bus repeater?
  Recall the repeater types: retimers and redrivers
  Think of redriver as filtering and/or amplifying analog signals
  Think of retimer as using clock-data recovery to re-transmit data
RX
(filter)
TX
(amp)
Device
Device
Redriver
RX
(CDR)
10101…
TX
Device
Device
Retimer

## Slide 6: IBIS 6.0 Support Examples
How do I model a mid-bus repeater?
  Use [Repeater Pin] to identify RX and TX pins
  Define “Redriver” or “Retimer” in the .ami parameters file under “Repeater_Type”
  For Retimers, ensure AMI_GetWave is defined and included
from the IBIS 6.0 specification

## Slide 7: IBIS 6.0 Support Examples
Where to “put” the analog impedance of the buffer?
What if I can’t easily represent the analog behavior of my buffer using traditional IBIS?
  In 6.0, use IBIS-ISS to represent complex analog buffer behavior
  Traditional IBIS becomes ideal (TX or RX)
TX Equalizer
IBIS-AMI
TX Equalizer
and Jitter
IBIS-ISS
Analog Model
(SPICE, Touchstone)
Ideal
Traditional
IBIS Model
Concept
Implementation

## Slide 8: IBIS 6.0 Support Examples
What if your algorithmic model isn’t a single file?
  Multiple files, in different locations, now supported
  From the .ami parameters file…
(Supporting_Files (Usage Info) (Type String)
(Description "Additional files and directories required by this model")
(Table
(“this_directory")
(“custom_functions.dll")
(“that_directory/core_functions.dll")
)
)
IBIS-AMI
Algorithmic
Model
DLL
“this_directory”
(all files)
custom_functions.dll
“that_directory”
core_functions.dll
EDA Tool
.ami Parameters
File

## Slide 9: Issues to Resolve
Ensuring true IBIS-AMI model compatibility
  Some models under IBIS 5.x place buffer analog information in the executable (DLL or SO file)
  This may be a problem for some tools
  Use of IBIS 6.0 improved analog modeling can help ensure portability
Algorithmic Model
IBIS .ibs Analog Model
Channel (package + PCB, etc.)
Analog portion, according to IBIS 5.x
DLL portion, according to some models and tools
Analog buffer information

## Slide 10: Issues to Resolve
Ensuring true IBIS-AMI model compatibility
  Some models under IBIS 5.x place buffer analog information in the executable (DLL or SO file)
  This may be a problem for some tools
  Use of IBIS 6.0 improved analog modeling can help ensure portability
Algorithmic Model
Ideal
IBIS .ibs Analog Model
Channel (package + PCB, etc.)
Analog portion, according to IBIS 6.0
DLL portion
IBIS-ISS/SnP
for Buffer Impedance

## Slide 11: Issues to Resolve
Improving IBIS packages
  Two separate approaches being discussed
  Objective is to finalize a package model format that…
    Can interact with IBIS and related files
    Supports time- and frequency-domain modeling data in IBIS-ISS format
    Supports arbitrary numbers of crosstalking signal lines in individual segments
  Target is to include this in the next major IBIS release

## Slide 12: What’s Next?
A parser: IBISCHK6
  Check new keyword syntax
  Check new IBIS-AMI parameter syntax
  Simple checks for IBIS-AMI DLL/SO executables?
    Are the required IBIS-AMI functions present?
    Do the functions execute (instead of crashing)?
Is a parser for IBIS-ISS required?
  SPICE features used in IBIS-ISS are very common across EDA tools
IBIS version updates
  IBIS continues to target updates twice per year

## Slide 13: Questions?