## Slide 1: Introducing IBIS Version 6.1
Michael Mirmak
Intel Corporation
http://www.ibis.org/
ASIAN IBIS Summit
Shanghai, China
November 9, 2015

## Slide 2: Agenda
IBIS 6.1 Overview and Development
Key Features
  AMI Improvements
  Traditional IBIS Improvements
Methods for Providing Feedback
References

## Slide 3: Specifications and Activities
IBIS Version 6.1 approved Sept. 11, 2015
  Nearly two years to the day after Ver. 6.0 approval
  Freely available at http://www.ibis.org/ver6.1/
Waiting for IBIS 6.2 for possible SAE standardization
A free syntax checker/parser under development
  Release tentatively expected in November
  Source code license is available for purchase
  Current ibischk6 licensees will receive a free update

## Slide 4: Key Features of IBIS 6.1
AMI improvements
  Extending IBIS-AMI for PAM4 Analysis
  Model dependencies are supported through a new API
  Buffer directionality for AMI models
“Traditional” IBIS improvements
  V-t table delay and overclocking
  Package RLC Matrix Diagonals
  Power Pin Package Modeling
  New keyword [Initial Delay] for Submodels and Driver Schedules
Plus corrections, clarifications, and a recommendation

## Slide 5: AMI Improvements
PAM4 Signaling
  Expands IBIS’s AMI support beyond 2 levels (NRZ) to 4 (PAM4)
  Adds “Modulation”, “PAM4_Mapping”, offset and threshold Reserved Parameters
  Re-defines bit-time and clock-times concepts
Model Dependencies
  Allows the final values of some .ami parameters to depend on the values of others, or of IBIS [Model]s
  New flow resolves dependencies before simulation
  Adds “AMI_Resolve” and “AMI_Resolve_Close” functions
  Adds “Resolve_Exists” and “Model_Name” Reserved Parameters
  Adds “Dep” Usage Type

## Slide 6: AMI Improvements (2)
Buffer Directionality
  Paving the way for DDR4 and beyond under AMI
  Associates all Reserved Parameters and Model_Types with directions (Tx, Rx)
    Most Serdes buffers are Tx-only or Rx-only
    DDR4 DQ buffers are I/O (bi-directional)
  Enables explicit information to be used by EDA tools about the direction for a given I/O buffer in a particular simulation
  Adds “Direction” descriptor to all Reserved Parameters
  Adds “Executable_Tx” and “Executable_Rx” subparameters to the [Algorithmic Model] keyword

## Slide 7: Traditional IBIS Improvements
Overclocking and delay
  [Initial Delay] defines the explicit amount of time, before transitions, embedded in the V-t and any I-t tables
  Supported for both single-Model and [Driver Schedule] structures
Package and Power Pin Modeling
  Diagonal package matrix values are enforced positive-only, and more mathematical assumptions are documented
  More rigorous rules are defined for EDA tool interpretation of partial Package Models which do not cover the entire [Pin] list
  Added support for [Merged Pins] where a single pin covers the parasitics of multiple physical pins

## Slide 8: Feedback is Welcome
Anyone may submit IBIS specification change proposals (BIRDs – Buffer Issue Resolution Documents)
  This is the primary mechanism for making IBIS changes
  http://ibis.org/birds/
Bugs and enhancement requests may also be proposed
  The BUG report covers both
  http://ibis.org/bugs/ibischk
The IBIS Open Forum and Task Group teleconferences welcome public participation
Your feedback is vital for keeping IBIS relevant
and useful to the industry!

## Slide 9: References
IBIS Web site: www.ibis.org
  Links to Task Groups available there
Specifications
  IBIS 6.1: www.ibis.org/ver6.1/
  IBISCHK6 parser (6.1 in progress): www.ibis.org/ibischk6/
  Touchstone: www.ibis.org/touchstone_ver2.0/
Summit Presentations
  www.ibis.org/summits/
IBIS 4.0 Cookbook
  www.ibis.org/cookbook/
Training
  www.ibis.org/training/