## Slide 1: Some Results for General K-table Extraction Proposal Using SPICE Bob Ross, Teraspeed Labs bob@teraspeedlabs.com Xuefeng Chen, Synopsys xfchen@synospsys.com Asian IBIS Summit Taipei, Taiwan November 13, 2015 (From material originally presented January 30, 2015, this presentation given Oct. 28, 2015 & Nov. 9 2015)

## Slide 2: Updated Material
More derivation detail: January 30, 2015, “General K-Table Extraction Proposal Using SPICE”
  http://www.ibis.org/summits/jan15/ross2.pdf
  Contains Summit references
Some results and other observations here
Purpose – Use SPICE for PROTOTYPING IBIS extraction algorithms (with general C_comp, on-die, package structures and fixture loads)

## Slide 3: Overview
Fixed C_comp to local GND for extraction
Detailed C_comp model from S-parameters or IBIS-ISS allowed
IBIS Interconnect BIRD proposal adds on-die and package models
SPICE-based extraction proposal supports total path measurement with more detailed C_comp/on-die/package structures
Limitations exist

## Slide 4
Standard IBIS Model
Package
Fixed Clamps and C_comp
Drivers

## Slide 5: Generalized V-T Extraction Load (with L/R/C_dut)
Calculate V(t) and I(t) from load information

## Slide 6: Direct V(t), I(t) Solution
Xuefeng Chen, Asian IBIS Summit (China), September 11, 2007: V(t), I(t) extracted directly for L/R/C/V_fixture by applying i=C*dv(t)/dt and v=L*di(t)/dt
Extension can include L/R/C_dut (where L/R/C_dut replaces the L/R/C_pin values for the measured pin)
Ku(t) and Kd(t) tables extracted using the 2-equations/2-unknowns (2EQ/2UK) method (later)

## Slide 7: Indirect Feedback Solution Next
Avoids encoding equations for complex structures
Calculates K-tables with high-gain (e.g., 1E7) feedback loop multiplier
  Kur(t), Kdr(t) from two rising V-T waveforms and fixtures
  Kuf(t), Kdf(t) from two falling V-T waveforms and fixtures
Calculated and specified responses converge
Requires vendor-specific SPICEs (versus IBIS-ISS)
  Tables
  Feedback loop issues with tables

## Slide 8: Partial SPICE Circuit Showing 2EQ/2UK K-Table Extraction
I1(t) = Ku(t)*Iu(V1(t)) + Kd(t)*Id(V1(t))
I2(t) = Ku(t)*Iu(V2(t)) + Kd(t)*Id(V2(t))
Kdr
Kur

## Slide 9: SPICE Encoding
I-V tables: G elements (VCCS)
V-T tables: PWL voltage sources
Voltage rails: Entered
SPICE interpolation
  Allows higher resolution time steps in V-T tables
  Interpolates G table currents
I-V and V-T tables extended from final values
Convergence criteria adjustable
K-tables printed for Kur(t), Kdr(t); Kuf(t), Kdf(t)
Simulation done with K-table drivers:
  G elements for K-tables
  Scaled controlled ramp (1V/nS)
  Step stimuli (0 to 1, 1 to 0)

## Slide 10: Part of SPICE Encoded IBIS Prototype for Simulation
Kur, Kdr
Kuf, Kdf
Enter simulation load
Ideal Step Stimulus
Table switching control

## Slide 11: General Proposed Single-ended C_comp Subckt Model
(Notation and details under development)
C_comp_I: If needed for series path
  Resistance needs to be de-embedded from I-V tables
A_signal: Output
Extend model for differential connections
C_comp Subckt with series component
A_signal
C_comp_I
A_puref
A_pcref
A_pdref
A_gcref

## Slide 12: SPICE Extraction of V(t), I(t) Setup and C_comp A_signal Node
PC
C_comp Subckt
GC
On-die Subckt
Package Subckt
L/R/C/V Fixture
V-T
K
-
+
Vsense = 0V
V(t), I(t)
PU, PD V(t) node and I(t) are calculated using an ideal high gain (e.g., K=1e7) amplifier
V-T table (originally extracted at the Fixture) is now a PWL driver

## Slide 13: 2EQ/2UK SPICE Setup to Generate Ku(t), Kd(t) Tables
2EQ/2UK Module
Ku(t) Kd(t)
Load 1
Load 2

## Slide 14: Ideal Ramp Test Cases
Reference Waveforms
  1 ns ramp (0% to 100%) into 50 W-to-gnd and 50 W-to-vcc loads
  5 V supply
  2 ns duration
C_comp cases
  0 pF (0p)
  4 pF (4p)
  4 pF || (4 pF – 50 W) (4p_4p-50)
Pullup/Pulldown I-V tables
  50 W straight lines
1001 point extractions (not critical)

## Slide 15: K-tables Shapes Versus Time (s) No L_fix, C_fix
Chart: 
C_comp :
0 pF
4 pF
4 pF || (4 pF - 50 W)

## Slide 16: K-tables Versus Time (s) – With L_fix=10 nH, C_fix=4 pF Fixtures
Chart: 
C_comp :
0 pF (without C/L_fix)
0 pF
4 pF
4 pF || (4 pF - 50 W)
New shapes with ideal ramp and reactive fixtures

## Slide 17: 4 ns Cycle Simulations for 4p_4p-50 C_comp Model
Chart: 
K-tables for C_comp model reproduces ideal ramps (50 W to gnd, 50 W to vcc)

## Slide 18: Test Case Notation Change for Vout(t) & Isense(t); Given V(t)
Package Subckt
Rfix = 50 W, Vfix = 0 V
V-T
K
-
+
Vsense = 0V
Vout(t), Isense(t)
PU, PD Vout(t) node and Isense(t) are calculated using an ideal high gain (e.g., K=1e7) amplifier
V-T table (originally extracted at the Fixture) is now a PWL driver
V(t)
No C_comp, no clamps, just a Package model which could be a C_comp model or an on-die model
Lpkg
Cpkg

## Slide 19: Lpkg = 0 nH, Cpkg = 0.004 nF
Continuous V(t) and dV(t)/dt
Closed-form references (50 W to GND)

## Slide 20: Extractions using Laplace Element
Same as closed-form references K-tables

## Slide 21: Lpkg = 2 nH, Cpkg = 0.004 nF
VOUT discontinuities: Feedback loop fails
Closed-form references (50 W to GND)

## Slide 22: Observations and Conclusions
Result accuracy
  K-table extraction insensitive to K=1e5 to K=1e9 feedback multipliers
  Requires SPICE maximum accuracy settings
  Not sensitive to number of extraction points
Severe test cases
  Sharp waveform derivative discontinuity in ideal ramp
  Large C_comp model load can be used
  Large L_fixture, C_fixture reactive loads are ok
  BOTH L_pkg, and C_pkg do not converge (even with smooth waveforms) – therefore topology limited and must use tool-dependent methods
  Fails for T-line models (delay in feedback loop)
  Works for S-parameter, Laplace transform, lumped models