## Slide 1: IBISCHK6 V6.1.3 and Executable Model File Checking Bob Ross, Teraspeed Labs bob@teraspeedlabs.com
Asian IBIS Summit
Tokyo, Japan
November 18, 2016

## Slide 2: Goals and Contents
New ibischk6 V6.1.3 executables available at the same location:
www.ibis.org/ibischk6/
Fixes 7 bugs
Differences (new ibischk6 file names)
New – executable model file checking per BUG179 enhancement for [Algorithmic Model] Executable lines
Source code quality assurance tests
Some limitations

## Slide 3: New BUGs 174-180 Fixed www.ibis.com/bugs/ibischk/

## Slide 4: New Names for ibischk6
Command line operation:
Windows:
  ibischk6_32.exe (versus ibischk6.exe)
  ibischk6_64.exe (versus ibischk6.exe)
Linux (Ubuntu):
  ibischk6_32 (versus ibischk6)
  ibischk6_64 (versus ibischk6)
Used for source code quality assurance tests per BUG179
Macintosh osx_32, osx_64 (also uploaded), but not part of source code release

## Slide 5: New Command Line Based on ibischk6 Name
Example: ibischk6_32.exe ”ibischk6_32” command
IBISCHK6 V6.1.3
IBISfile validation:
This program has been provided free to the electrical
engineering community by the IBIS Open Forum. The
purpose of this program is to validate that the contents
of ASCII device data in a file specified conform to the
IBIS specification.
Usage: ibischk6_32 <IBS filename>
: ibischk6_32 -ebd <EBD filename>
: ibischk6_32 -pkg <PKG filename>
: ibischk6_32 -ami <AMI filename>
Usage: ibischk6_32 -caution -numbered <IBS filename>
: ibischk6_32 -caution -numbered -ebd <EBD filename>
: ibischk6_32 -caution -numbered -pkg <PKG filename>
: ibischk6_32 -caution -numbered -ami <AMI filename>
The flags prior to the file name can be in any order, and the -caution and/or -numbered flags are optional.

## Slide 6: Can Rename ibischk6 File (Examples Below)
ibischk6.exe as in earlier versions for “ibischk6” command
ibischk613_32.exe showing version and bits detail for “ibischk613_32” command
Etc. - the new ibischk6 file name shows up in the Usage: lines, as shown on previous slide

## Slide 7: Syntax and Notation Related to BUG179
Under [Algorithmic Model] Executable, Executable_Rx and Executable_Tx lines have this information:
Platform is operating system such as Linux, Windows
Bits is 32 or 64 for common platforms
File_Name is “executable model file” name such as abc.dll or abc.so
Parameter_File is the .ami file
Platform_Compiler_Bits File_Name Parameter_File

## Slide 8: Testing and Executable Combinations
32-bit and 64-bit operating system, ibischk6_* and executable model files are done consistent with the platform operating system
  Ibischk6_32 will work on 64-bit platforms, but will load and test 32 bit executable model files
Specification does not impose a requirement, but internal Windows requires executable names with at least a dot “.”
Message will give the recommended (but not required) extension

## Slide 9: bug179-1.ami Full Function Existence Checking
(bug179
(Reserved_Parameters
(AMI_Version (Usage Info)(Type String)(Value "6.1"))
(Init_Returns_Impulse (Usage Info)(Type Boolean)(Value True))
(GetWave_Exists (Usage Info)(Type Boolean)(Value True))
(Resolve_Exists (Usage Info)(Type Boolean)(Value True))
)
)

## Slide 10: Function Existence Testing
Test file names:
: noicgr No “C” combinations above and below
A: icg AMI_Init, AMI_Close, AMI_GetWave
B: ic AMI_Init, AMI_Close
C: icgr AMI_Init, AMI_Close, AMI_GetWave, AMI_Resolve, AMI_Resolve_Close
D: icr AMI_Init, AMI_Close, AMI_Resolve, AMI_Resolve_Close

## Slide 11: Some Tests for ibischk6_32.exe when Checked with bug179-1.ami
| Normal case: GetWave and ResolveExists return true
|
Executable Windows_1_32 noicgr_32.dll bug179-1.ami
Executable Windows_2_32 ic_32.dll bug179-1.ami
Executable Windows_3_32 icg_32.dll bug179-1.ami
Executable Windows_4_32 icgr_32.dll bug179-1.ami
Executable Windows_5_32 icr_32.dll bug179-1.ami
Executable Windows_6_64 noicgr_64.dll bug179-1.ami
Executable Windows_7_64 ic_64.dll bug179-1.ami
Executable Windows_8_64 icg_64.dll bug179-1.ami
Executable Windows_9_64 icgr_64.dll bug179-1.ami
Executable Windows_10_64 icr_64.dll bug179-1.ami
|
 Executable lines for 64-bit Windows lines not checked
5 Errors
3 Errors
2 Errors
Good
1 Error
Lines 112 to 121

## Slide 12: Partial Report for ibischk6_32.exe with New Error Codes
E4702 (line 112) - Code file noicgr_32.dll does not contain required AMI_Init() function
E4703 (line 112) - Code file noicgr_32.dll does not contain required AMI_Close() function
E4704 (line 112) - Code file noicgr_32.dll does not contain AMI_GetWave() function, required because GetWave_Exists=True in AMI file bug179-1.ami
E4705 (line 112) - Code file noicgr_32.dll does not contain AMI_Resolve() function, required because Resolve_Exists=True in AMI file bug179-1.ami
E4706 (line 112) - Code file noicgr_32.dll does not contain AMI_Resolve_Close() function, required because Resolve_Exists=True in AMI file bug179-1.ami
E4704 (line 113) - Code file ic_32.dll does not contain AMI_GetWave() function, required because GetWave_Exists=True in AMI file bug179-1.ami
E4705 (line 113) - Code file ic_32.dll does not contain AMI_Resolve() function, required because Resolve_Exists=True in AMI file bug179-1.ami
E4706 (line 113) - Code file ic_32.dll does not contain AMI_Resolve_Close() function, required because Resolve_Exists=True in AMI file bug179-1.ami
E4705 (line 114) - Code file icg_32.dll does not contain AMI_Resolve() function, required because Resolve_Exists=True in AMI file bug179-1.ami
E4706 (line 114) - Code file icg_32.dll does not contain AMI_Resolve_Close() function, required because Resolve_Exists=True in AMI file bug179-1.ami
E4704 (line 116) - Code file icr_32.dll does not contain AMI_GetWave() function, required because GetWave_Exists=True in AMI file bug179-1.ami
Line 115 is Good (0 Errors):
Executable Windows_4_32 icgr_32.dll bug179-1.ami

## Slide 13: Summary for Platforms/Bits Test for Full Test Case
... Status of [Algorithmic Model] Executables for Windows 32:
icr_64.dll: Windows 64: Not Checked
icgr_64.dll: Windows 64: Not Checked
icg_64.dll: Windows 64: Not Checked
ic_64.dll: Windows 64: Not Checked
icr_32.dll: Windows 32: Checked
icgr_32.dll: Windows 32: Checked
icg_32.dll: Windows 32: Checked
ic_32.dll: Windows 32: Checked
noicgr_64.dll: Windows 64: Not Checked
icr_32.dll: Windows 64: Not Checked
icgr_32.dll: Windows 64: Not Checked
icg_32.dll: Windows 64: Not Checked
ic_32.dll: Windows 64: Not Checked
noicgr_32.dll: Windows 64: Not Checked
icr_64.dll: Windows 32: Checked, has platform issue
icgr_64.dll: Windows 32: Checked, has platform issue
icg_64.dll: Windows 32: Checked, has platform issue
ic_64.dll: Windows 32: Checked, has platform issue
noicgr_64.dll: Windows 32: Checked, has platform issue
noicgr_32.dll: Windows 32: Checked

## Slide 14: Summary for Platforms/Bits Test for Full Test Case (Continued)
icr_64.so: Linux 64: Not Checked
icgr_64.so: Linux 64: Not Checked
icg_64.so: Linux 64: Not Checked
ic_64.so: Linux 64: Not Checked
icr_32.so: Linux 32: Not Checked
icgr_32.so: Linux 32: Not Checked
icg_32.so: Linux 32: Not Checked
ic_32.so: Linux 32: Not Checked
noicgr_64.so: Linux 64: Not Checked
icr_32.so: Linux 64: Not Checked
icgr_32.so: Linux 64: Not Checked
icg_32.so: Linux 64: Not Checked
ic_32.so: Linux 64: Not Checked
noicgr_32.so: Linux 64: Not Checked
icr_64.so: Linux 32: Not Checked
icgr_64.so: Linux 32: Not Checked
icg_64.so: Linux 32: Not Checked
ic_64.so: Linux 32: Not Checked
noicgr_64.so: Linux 32: Not Checked
noicgr_32.so: Linux 32: Not Checked
... This IBISCHK6 executable supports Windows 32 bit only
Errors : 28
File Failed

## Slide 15: Status Report Lines
Checked
Not checked
Checked, has platform issue
  Platform bits different than operating system platform Bits
  Executable model file does not have dll or so extension
  Ibischk6_32 cannot load 64-bit executable model files and visa versa
“… This IBISCHK6 executable supports Windows 32 bit only”
  Refers to ibischk6_32.exe used in test

## Slide 16: Recommended Extensions
Windows: dll
Linux: so
No requirement but some Windows versions require executable names with at least a dot “.”
Other messages may suggest .dll for Windows or .so for Linux)

## Slide 17: Limits and Issues
ibischk6_32 works on 64-bit platforms if 32-bit executable model files load and work on the platform
Platform name examples shown in the IBIS Specification – some may be specified in the future
  Case insensitive Windows
  Case insensitive Linux
For unknown platform names, ibischk6 will try to load executable model file and run the functional existence test

## Slide 18: Future and Conclusion
No reference IBIS-AMI waveform checking
Some commercial vendors offer reference IBIS-AMI waveform checking
ibischk6 V6.1.3 valuable for function existence testing for Reserved_Parameters documented in the .ami file