## Slide 1
Robert J. Haller
Signal Integrity Software, Inc.
6 Clock Tower Place – Suite 250
Maynard MA. 01754
978-461-0449 X 15
Notes: Hi, How is everyone ?
Brief Introduction.

## Slide 2: SPICE versus IBIS
Notes: Contrary to popular belief, IBIS models can be extremely accurate over 1GHz.
This is a waveform overlay of Hspice and IBIS simulations of an LVDS interface running at 1.25GHz.
Correlation is excellent, time-shifts are intentional, but getting this level of correlation was not easy and not always possible.
In many cases though this is the exception and not the rule.
I would have not confidence in this model had I not run both IBIS and SPICE.
IBIS work well at some varying frequencies, but a methodology is needed that supports both SPICE and IBIS.

## Slide 3: SPICE versus IBIS
Why SPICE ?
Why IBIS ?
Why BOTH?
Notes: Now that I have your attention. In today’s presentation I plan on reviewing the primary advantages and disadvantages of SPICE and IBIS.
Some of you are probably already aware of these issues, but today’s high speed designs exacerbate the problems.
I advocate both IBIS and SPICE are required to meet the high speed design challenges of today and tomorrow.

## Slide 4: Why SPICE?
Advantages
  Industry Standard
    Berkley SPICE is Free
    HSPICE has widespread acceptance
  Accurate
    Transistor level models
    Connectors, WLINE’s – Lossy transmission lines
    Rail collapse, ground bounce
    Return path
    If you can build it, you can model it
Disadvantages
  Performance can be slow
  Inconsistent net list formats and cryptic spice syntax
Notes: Everyone knows and loves SPICE. There are a lot of free versions available and it is presently the industry Standard
SPICE allows you model at the transistor level and has robust package, connector and Lossy transmission line models.
If you can build it, You can Model it.
Complicated spice circuit simulation is generally very slow. You can often waste a lot of time trying to isolate a simple design problem.
Convergence can be an issue and SPICE syntax is cryptic (not to mention error messages). TIME STEP TO SMALL
You are also probably all aware that Some Vendors Will not or Do not provide SPICE models….

## Slide 5: Why IBIS?
Advantages
  Fast
  Easy
  Doesn’t reveal proprietary information
  Complete chip definition
    Pin out
    Cell Usage
    AC and DC specifications
Disadvantages
  IBIS model quality is generally poor
  Accuracy can be an issue
    Practical Issues and Limitations
    Connectors/package models
    Intrinsic cell delay characteristics
    Different results from different simulators (portability)
  IBIS committee slow to respond
Notes: Most people are aware that IBIS models run an order of magnitude FASTER than SPICE.
IBIS simulators also make it EASY to drop down models, T-lines and perform what-if simulations to your hearts content.
Another primary reason semiconductor vendors release only IBIS models is to protect proprietary circuit and process information.
IBIS model quality and accuracy is the primary disadvantage.
Different results from different simulators – There are about 20 subtle components to an IBIS model that can significantly affect the portability of this model. IV crossing through zero, VT curves, How many curves.

## Slide 6: Need both SPICE and IBIS
I’m not the only one who thinks so
  Best of Both Worlds
    Mixed-signal HDLs put IBIS on steroids (Glenn Perry ee_design 9/12/02
  Will Hobbs (Intel - Oct 98) said:
    We Need to find a happy coexistence between structural and behavioral.
    We need to keep pushing IBIS to meet emerging needs
  Many others…
If only we had it now (some of us do :-)
Notes: I am not the only person that thinks we need to use Both SPICE and IBIS.
Many people are convinced that we need to use both each for there respective strengths.
Here are a few examples.

## Slide 7: Conclusions
High quality accurate IBIS models can be created
  Hard work in most cases
  Sometimes unachievable
  Often, model has limitations
We need SPICE and IBIS
  Best of both worlds
IBIS open forum must meet emerging needs
Notes: Wrap Up ….