## Slide 1
IBIS Summit at PCB Conference East
Westford, MA
October 15, 2002
Arpad Muranyi
Signal Integrity Engineering
Intel Corporation
arpad.muranyi@intel.com
I
S
e
More Details on True Differential Buffer Characterization

## Slide 2
Background
The author of this presentation introduced a page on true differential buffers in his “Introduction to IBIS Models and IBIS Model Making” class materials in September 2000
  a proprietary LVDS buffer was used to make recommendations for generating IV and Vt curves to convert it to an IBIS model
  the buffer used in this example did not have on-die termination
Hazem Hegazy gave two presentations in January and March 2001 at IBIS summits on this subject
  quoting the above class material, some shortcomings of the suggested technique were pointed out and explained by Hazem
    models of buffers with on-die termination made this way are inaccurate
    miscorrelation with original SPICE model under different loading conditions
  new techniques were demonstrated giving better correlation with the original SPICE model, Proposal-III being the best and most accurate

## Slide 3
True differential buffers (LVDS)
IBIS doesn’t support them directly but they can be approximated with two different methods
R=R_fixture
V=Avg(Vswing)
R=R_fixture
Rise
Fall
V-t curves
Ia
R=R_fixture
V=Avg(Vswing)
Hi
Lo
I-V curves
R=R_fixture
Ib= -Ia
V=Avg(Vswing)
Rise
Fall
V-t curves
Ia
Ib= -Ia
Hi
Lo
I-V curves
* A. Muranyi “Introduction to IBIS Models and IBIS Modeling”, September 2000, p. 87.

## Slide 4
LVDS SPICE and IBIS model overlay
* A. Muranyi “Introduction to IBIS Models and IBIS Modeling”, September 2000, p. 88.

## Slide 5
Miscorrelation of original technique
* H. Hegazy and Mohammed Korany “LVDS Modeling”, IBIS Summit, March 2001, p. 14.

## Slide 6
Motivation for this study
Hazem’s Proposal-III essentially introduces the idea of measuring the common and differential currents of the buffer separately
  great idea, similar to RLGC matrices of T-lines having self and mutual entries leading to common and differential impedance (not the same as common mode and differential mode impedance, see references)
  the concept of common and differential impedance is well known and understood
Intentional or not, differential buffers also have common and differential currents (or impedance)
  if intentional, this can be from on-die terminations, etc…
  if not intentional, this can be caused by the non ideal characteristics of current sources, leakages, etc…
Proposal-III, however, is lacking generality for measuring the differential portion of the output currents

## Slide 7
True differential buffers with IBIS v3.2
[Series Pin Mapping]
  allows the mapping of series elements, such as R, L, C and current tables to pins which already have a [Model] assignment
  a series current (and/or) R, C elements could be used to account for the differential currents
  the regular [Model] associated with the same two pins could be used to account for the common currents
[Series Current]
[Series MOSFET]
[R Series]
[C Series]
[Rc Series]

## Slide 8
New IV curve measurement setup
Ip
Sweep Vp while
holding Vn
Hi
Lo
I-V curves
In
Step through
same range as Vp
When Vp = Vn we are measuring the common current
When Vp  Vn we are measuring the common plus differential currents
To get the differential current alone we need to subtract the common current from the total current (i.e. normalize along the diagonal)

## Slide 9
IV surface of measured (total) currents
Ip vs. Vp and Vn
(low state)
In vs. Vp and Vn
(high state)
Differential buffer in drive mode without a 100  parallel resistor

## Slide 10
Differential IV curve and impedance
Differential impedance (when Vp is low)
Differential current (when Vp is low)
Idiff = 0
Differential buffer in drive mode without a 100  parallel resistor

## Slide 11
IV surface of measured (total) currents
Differential buffer in drive mode with a 100  parallel resistor
Ip vs. Vp and Vn
(low state)
In vs. Vp and Vn
(high state)

## Slide 12
Differential IV curve and impedance
Differential buffer in drive mode with a 100  parallel resistor
Differential current (when Vp is low)
Idiff = 0
Differential impedance (when Vp is low)

## Slide 13
IV surface of measured (total) currents
Differential buffer in receive mode without a 100  parallel resistor
Ip vs. Vp and Vn
(low state)
In vs. Vp and Vn
(high state)

## Slide 14
Differential IV curve and impedance
Differential buffer in receive mode without a 100  parallel resistor
Differential current (when Vp is low)
Idiff = 0
Differential impedance (when Vp is low)

## Slide 15
IV surface of measured (total) currents
Differential buffer in receive mode with a 100  parallel resistor
Ip vs. Vp and Vn
(low state)
In vs. Vp and Vn
(high state)

## Slide 16
Differential IV curve and impedance
Differential buffer in receive mode with a 100  parallel resistor
Differential current (when Vp is low)
Idiff = 0
Differential impedance (when Vp is low)

## Slide 17
Conclusion
As seen on the previous plots, the differential current is a function of the voltages on the two I/O pins
  a complete description would require a multi dimensional current table
However, the normal operating region (where the signaling occurs) could be approximated with one of the available keywords with reasonable accuracy
  if the operating region includes strongly non linear shapes, this technique will need to rely on BIRD75 features

## Slide 18
Further study and work needed
This concept needs to be proven with examples
  this could be done in the near future
Need to develop a differential C_meter to measure capacitive coupling between pins
  [C Series] can be used to hold this value in the IBIS model
More experiments need to be done to find out how the differential current varies with respect to time during transitions from one state to another
  do we need Vt curves for these differential elements also?
Simulation tool vendors should implement the series element features in IBIS v3.2 ASAP!
  unfortunately not all tools support these v3.2 keywords yet

## Slide 19
Questions on Vt curve measurements
If the differential currents are constant during transitions, we can cancel them by placing an equal and opposite sign current source between the pins, so that the Vt curves represent the time dependency of the common currents alone
However, if the differential currents are time varying, we may need a more elaborate method to extract Vt curves for the common and differential currents independently (TBD)
R=R_fixture
V=Avg(Vswing)
R=R_fixture
Rise
Fall
V-t curves
I=-Idiff

## Slide 20
References
Steve Kaufer and Kellee Crisafulli, “Terminating Differential Signals on PCBs”, Printed Circuit Design, March 1999
Douglas Brooks, “Differential Impedance”, Printed Circuit Design, August 1998
Eric Bogatin, “Differential Impedance Finally Made Simple” Bogatin Enterprises, updated May 31, 2002, (www.BogatinEnterprises.com)