## Slide 1: IBIS Interconnect Specification
Stephen Peters, Intel Corp.

## Slide 2: Current Status
Draft interconnect spec ICM 1.0 released for review (Yeah!)
  Available on IBIS website under the “Connector Info” link
  Comments have been received
No feature changes from last report
  Some technical items were clarified
Critical ICM 1.0 features
  Specification encompasses both connectors and package style interconnect
  Frequency dependant effects are captured via S-parameter matrices
  Both regular and non-regular connectors are supported
Moving forward...
  parser development -- funding, contractor, testing
  integration into multi-lingual modeling proposal??

## Slide 3: Overview
A .icm file supports one (1) interconnect family
  Each interconnect family includes one or more individual interconnect descriptions
Individual interconnect descriptions include the following:
  Basic info like manufacture, description, mating conditions, model limit (max slew rate), etc.
  The model type (MLM, SLM or S-parameter).
  A path description, either ‘tree’ or ‘nodal’, that describes how the matrices are interconnected.
  Where applicable, info that allows pin swathing.
  Mapping between external pins/node of interconnect and the rows of the matrix.
Matrixes contain either RLGC or S-parameter data (via external Touchstone file).

## Slide 4: Overview (cont.)
Specification supports three different types of interconnect:
  Regular (no pins missing) rectangular connectors
    Swathable, can use either path description
  Regular, non-rectangular connectors
    Not swathable, can use either path description
  Irregular connector/interconnect
    Not swathable, must use nodal path description
Nodal vs. Tree type path descriptions
  [Tree Path Description] cascades matrices back to back, each row of matrix corresponds to a single pin, same # of pins front and back
  [Nodal Path Description] connects matrices via explicit node names, can build arbitrary structures with missing pins, different size matrices, etc.

## Slide 5: MLM and SLM Models
MLM = Multi-line (coupled) models
  Use for including pin-to-pin coupling
  Spec specifies partial inductance values and Maxwell capacitance values in matrix
  Intent is to support xtalk and return path simulations.
SLM = Single lines (un-coupled) models
  SLM_EvenMode/OddMode/Quiescent models have documented ground return paths(!)
  SLM_General only documents GSR ratio
  Spec specifies loop inductance in matrix
  The intent is to ‘bracket’ interconnect performance under specific conditions
S-parameter models
  By definition are coupled models, unused terminals terminated by reference impedance

## Slide 6: Length vs. Multiplier Matrix Specification
Path description specifies how to interpret the data in an RLGC matrix
  Len = per-unit-length, intended for distributed transmission line elements. Expansion by multiplication.
  Mult = lumped elements, intended to be rendered into circuit netlists. Expansion by cascading sections.
  S-parameter is always lumped, non-cascade
[Derivation Method] keyword in matrix section provides a cross reference
Two styles for two different purposes…
  Per unit length results from a 2-D extraction of parallel structures (I.e. package traces)
  Unit multiplier results from a 3-D extraction of non-regular structure (I.e. connectors)