## Slide 1
Tim Coyle
IBIS Summit Meeing
October 21, 2003
IBIS User Experiences

## Slide 2: Model Maker to Model User
Spent last 2 years making IBIS files
Now using other people's IBIS files

## Slide 3: Where is IBIS at today?
Well recognized modeling standard
Over 25+ companies members of the IBIS Open Forum Group
Solid 3.2 spec
Future AMS enhancements

## Slide 4: What do you get today for a 3.2 model?
Almost all IBIS files will pass parser
  Either it's a good model or a really bad model
Timing load inlaced (vref,cref,rref)
V/T data

## Slide 5: So what's the problem?
Accuracy is the problem
So the IBIS file passes the parser, and the I/V and V/T curves look valid, but what is the accuracy of the model?

## Slide 6: Why it's Important
IBIS files used for timing margins
If the model is off, then the timing is off
People are basing designs off of simulation of IBIS files

## Slide 7: How do you define accuracy?
Have to overcome issues such as
  What tests to use
  What tool to use for verification
Previous work done with Accuracy Handbook
Current work being done with Quality group

## Slide 8: How do you get accuracy?
Don't count on manufacturers
  How many manufacturer's have devoted resource to IBIS? Most are either designer or applications engineer playing an IBIS modeler
Do manufacturer's understand how IBIS files are being used by the customer?
  Is a curve check enough of a validation?

## Slide 9: An example of my procedure
Create min/typ/max HSPICE netlists from design database (no package, include esd)
Simulate HSPICE models to ensure they meet datasheet spec
Run simulations to extract I/V and V/T curve
Check with parser, compare IBIS in t-line load to SPICE in t-line load
But what did I miss? What is the accuracy spec missing?

## Slide 10: What to do about accuracy?
The proof is in the numbers
Need to start having an open-dialog with your vendors
  Understand their process for creating models
  Ask for data such as tester data, char data, etc.
  Ask them if they would make/break a system based upon model

## Slide 11: It's not just accuracy...
Other aspects of IBIS modeling that are still open-ended, some basic, some not...
  Package models (ICM solution?)
  ESD clamps (Kamps of current?)
  Tool issues (it goes beyond tech support)

## Slide 12: The IBIS Community
For a non-proprietary specification, the IBIS community is rather quiet
What are some possible factors
  Slow economy
  Maybe not as proprietary as you think
    Modeling advantages
    Software sales

## Slide 13: IBIS – The Paradox
IBIS will always battle 2 questions:
  Is it as accurate as SPICE?
  How fast can it go?
Where's the proof?

## Slide 14: The Answer
The only answer is involvement
What if we gave a list of IBIS issues to the best modelers, put them in a room with no affiliation to company/self interest/etc., just pure engineering?

## Slide 15: My Part
Wanted to keep track of current going-ons of IBIS (new app notes, articles, etc.)
Wanted a venue not associated with any company or organization to freely discuss IBIS issues
Why not a website?

## Slide 16: The Website
www.ibisdeveloper.com
Hosting out of my own pocket (no affiliation with Sun or anyone else)
Will announce in a couple of weeks
Worst Case scenario
  A good links page for IBIS information
Best Case scenario
  A cohesive community of IBIS developers

## Slide 17: The Website
If you want to contribute
  Timothy.Coyle@sun.com

## Slide 18: Questions?